Meataxe-64
HPMI for AS primes.
Richard Parker 18.3.2019

Section 1 – Introduction.

This document is a specification of the AS-code based HPMI, used for characteristics 5-193 in meataxe64..

Definition. Let A be an abelian group. An AS Set Z for A is a set such that every element of A is of the form z1 − z2 for z1,z2 in Z.

For example Z = { 0, 1, 2, 4, 8, 9, 18 } is an AS Set for the additive group mod 29.

In broad-brush terms, the AS-code based HPMI is based on taking each vector V of B and making z.V for all z in an AS-set. Any multiple Aij of V can then be added by adding one and subtracting one of these precomputed vectors. There are, however, several details to sort out.

Reduction mod p. The elements in Bfmt and Cfmt take up considerably more bits than is strictly necessary, and a "bias" added so that seven adds and seven subtracts can be done without overflow or underflow. Reduction is done by using AND to get the top few bits, XOR to clear these bits, SHIFT RIGHT to get these bits into the units position, MULTIPLY then ADD to get the result the same as the original (mod p) and then ADD to add in the "bias". For the larger primes (certainly from 67 upwards) the entries are held in a 16-bit field. For 17-61 a 10-bit field can be used - storing three entries in each 32-bit integer - but this requires the pmulld instruction so is only used if sse4.1 is implemented in the chip. For 5-13, an 8-bit field is used.
Hence the BwaMad routine chooses between the following assembler routines . . .
pcjas for 8- or 16-bit primes if AVX2 is available
pcaas for 8- or 16-bit primes using SSE2
pcjat for 10-bit primes using AVX-2
pcdas for 10-bit primes using SSE4.1
The first two are slighly faster, as they use pmullw (16-bit) rather than the slower 32-bit pmulld, but the ability to pack three entries in a 32-bit word rather than two more than compensates for this.

Making the AS-code multiples. All the AS-codes include zero and one, and an addition-chain method is used, where each entry is made by adding two previous ones and reducing mod p. In most cases a couple of multiples are made that are not needed for the AS code itself. For example for p=59 the code is described as

0 1 2 [3] 6 [7] 14 15 22 25 32

Each entry is readily seen to be the sum of two previous, but 3 and 7 are not part of the addition chain and are discarded. This is coded up in tabmake.c for interpretation by pcdasc, which uses SSE - no AVX-2 version of BSeed for AS-primes has yet been implemented.

Conversion to Afmt. It is a happy coincidence that a good AS-code exists for 53 and for 72, 112 and 132 so that the conversion to Afmt is a simple byte-wide table look-up in all cases. Hence the alcove for p=5 is 21, and for p in {7,11,13} it is 14, even though seven adds and seven subtracts are always done.

Suggestions for improvement.
An AVX-512 version of BwaMad and possibly BSeed are overdue.
An AVX-2 version of pcdasc (BSeed) may be worthwhile
The AS codes used minimize the memory occupied. In some cases it may be slightly faster to use a slightly bigger code (but still less than 16) that can be made (BSeed) more rapidly.

Section 2 – The AS-codes.

Here is the list of AS codes used. In every case each entry is the sum of two previous, though in a few cases some guidance on this is given in small print for the human reader. The numbers in [] are not part of the AS code, but are needed to make the AS code using an addition chain. It seems unlikely that an AS-code of size 16 or less exists for p>193.

5	000 100 010 001 [011] 021 [101] 202 [022]
        044 224 [110] 312 334 113 430 443 310
224=022+202, 312=202+110, 334=312+022, 113=334+334, 430=334+101 443=224+224, 310=202+113
7	00 01 10 02 03 20 30 22 33
11	00 01 10 [02] 12 04 [24] 25 48 61 [71] 96 32 42 56 88
61=48+24 96=71+25 32=71+71 56=32+24 88=56+32
13	00 01 10 02 20 [04] 14 18 [21] 42 [43] 64 [10,7] 71 48 75 92 11,8 95
64=43+21 71=10,7+10,7 48=10,7+71 75=71+04 92=21+71 11,8=75+43 95=11,8+11,8
17	0 1 2 [3] 5 8
19	0 1 2 [3] 6 9
23	0 1 2 3 [4] 7 11
29	0 1 2 4 8 9 18
31	0 1 [2] 4 [5] 10 12 17
37	0 1 [2] 4 5 [6] 12 14 20
41	0 1 2 3 4 [5] 10 15 20
43	0 1 2 4 [5] 8 13 18 23
47	0 1 [2] 4 [5] 9 14 19 21 25
53	0 1 2 4 [5] 8 13 18 23 28
59	0 1 2 [3] 6 [7] 14 15 22 25 32
61	0 1 [2] 3 5 [7] 9 [16] 21 37 44 51
67	0 1 2 3 6 12 [14] 18 32 46 60
71	0 1 2 3 [4] 8 12 [14] 24 25 39 53
73	0 1 [2] 3 [4] 7 [9] [13] 15 [18] 31 36 54 63
79	0 1 [2] [3] 5 8 [11] [12] 16 27 29 35 47 70
83	0 1 2 4 8 [9] 18 36 72 61 63 41 61=72+72 41=61+63
89	0 1 [2] 4 5 [6] 12 14 [16] 32 48 49 64 70
97	0 1 2 3 6 12 18 20 26 46 [66] 68 39 39=68+68
101	0 1 2 3 4 [6] 12 [13] 17 24 30 43 56 68
103	0 1 2 3 4 [5] [6] 12 19 24 38 44 57 76
107	0 1 2 [3] 6 7 10 [11] [16] 22 24 35 51 70 77
109	0 1 [2] 4 [5] [10] 15 17 21 42 47 49 91 73 101 73=91+91
113	0 1 [2] 4 [8] 9 16 [17] [21] 23 29 40 50 66 82 84
127	0 1 [2] 4 [5] 10 14 [15] 17 22 [31] 33 64 66 86 101 103
131	0 1 [2] [4] 8 12 [13] 21 29 58 31 [70] 83 96 117 7 99
137	0 1 2 3 4 [8] 12 20 [21] 25 40 46 60 67 88 108
139	0 1 2 4 [5] [6] 11 13 22 28 33 41 47 66 82 89
149	0 1 [2] [3] 5 [6] [10] 13 [14] 23 33 36 42 48 59 72 86 88 93
151	0 1 2 3 6 9 12 [14] 18 [20] 24 44 64 84 104 124 138
157	0 1 2 3 4 [8] 12 20 28 48 56 84 [29] 33 62 91 120
163	0 1 2 3 4 [5] [9] 13 [16] 21 [29] 38 45 61 67 76 114 137 81
167	0 1 [2] [3] 5 [7] 9 [14] 17 31 36 [48] 96 98 115 118 121 128 130 139
173	0 1 2 3 4 5 6 7 [14] 18 28 46 [92] 94 [32] 38 66 124 75
179	0 1 2 3 4 5 6 [9] [11] 17 34 43 [52] 53 61 96 114 107 159
181	0 1 [2] 3 5 7 9 11 13 [22] 35 [44] 55 88 110 [119] 124 141 163 125
191	0 1 2 3 6 [12] 18 [19] 31 38 [40] [80] 120 122 98 141 139 143 183 [117] 65
193	0 1 2 4 [3] [7] 11 [15] [26] 27 52 [59] 118 [56] 174 121 82 180 89 185
[125] 136 152

Section 3 – Reduction mod p.

The following table expresses in detail how the reduction proceeds. For each prime, the "bits" column specifies how many bits each entry occupies. [On very old chips - those without sse4.1 - primes 17-61 are done in 16 bits, due to the lack of pmulld to do the 32-bit multiply needed for reduction]. The "red" column specifies the principle used for reduction. For example for the prime 23 "32=9" means that all but the top five bits are removed, shifted 5 places right, multiplied by 9 and added in. "res red" gives the maximum value that can be obtained from a number of "bits" bits using this reduction technique - in practice the full range is not usually used and the result is therefore less than this. "Red range" gives the range that may exist after this process - from 0 up to "res red". AS gives the range that 7 adds and 7 subtracts may result - assuming (worst case) that all the values are 0 or p-1. The bias is the value added to stop subtraction underflowing. It is 7*characteristic except for p in {5,7} where it is 6*characteristic (though I think 7*characteristic actually works for all!). "end range" is "Red range" + "AS" + "bias" and is visibly in the range on "bits" bits in all cases.

P	bits	red	res red	Red range	AS	bias	end range
5	8	16=1	15+1.15	[0 30]	[-28 28]	30	[2 88]
7	8	8=1	7+1.31	[0 38]	[-42 42]	42	[0 122]
11	8	16=5	15+5.15	[0 90]	[-70 70]	77	[7 217]
13	8	16=3	15+3.15	[0 60]	[-84 84]	91	[7 235]
17	10	32=15	31+15.31	[0 496]	[-112 112]	119	[7 727]
19	10	32=13	31+13.31	[0 434]	[-126 126]	133	[7 693]
23	10	32=9	31+9.31	[0 310]	[-154 154]	161	[7 625]
29	10	32=3	31+3.31	[0 124]	[-196 196]	203	[7 523]
31	10	32=1	31+1.31	[0 62]	[-210 210]	217	[7 489]
37	10	128=17	127+17.7	[0 246]	[-252 252]	259	[7 757]
41	10	128=5	127+5.7	[0 162]	[-280 280]	287	[7 729]
43	10	64=21	63+21.15	[0 378]	[-294 294]	301	[7 973]
47	10	64=17	63+17.15	[0 318]	[-322 322]	329	[7 969]
53	10	64=11	63+11.15	[0 228]	[-364 364]	371	[7 963]
59	10	64=5	63+5.15	[0 138]	[-406 406]	413	[7 957]
61	10	64=3	63+3.15	[0 108]	[-420 420]	427	[7 955]
67	16	512=43	511+43.127	[0 5972]	[-462 462]	469	[7 6903]
71	16	512=15	511+15.127	[0 2416]	[-490 490]	497	[7 3403]
73	16	512=1	511+1.127	[0 638]	[-504 504]	511	[7 1653]
79	16	256=19	255+19.255	[0 5100]	[-546 546]	553	[7 6199]
83	16	256=7	255+7.255	[0 2040]	[-574 574]	581	[7 3195]
89	16	512=67	511+67.127	[0 9020]	[-616 616]	623	[7 10259]
97	16	512=27	511+27.127	[0 3940]	[-672 672]	679	[7 5291]
101	16	512=7	511+7.127	[0 1400]	[-700 700]	707	[7 2807]
103	16	128=25	127+25.511	[0 12902]	[-714 714]	721	[7 14337]
107	16	128=21	127+21.511	[0 10858]	[-742 742]	749	[7 12349]
109	16	128=19	127+19.511	[0 9836]	[-756 756]	763	[7 11355]
113	16	128=15	127+15.511	[0 7792]	[-784 784]	791	[7 9367]
127	16	128=1	127+1.511	[0 638]	[-882 882]	889	[7 2409]
131	16	1024=107	1023+107.64	[0 7811]	[-910 910]	917	[7 9638]
137	16	512=101	511+101.127	[0 13211]	[-952 952]	959	[7 15122]
139	16	512=95	511+95.127	[0 12576]	[-966 966]	973	[7 14515]
149	16	512=65	511+65.127	[0 8766]	[-1036 1036]	1043	[7 10845]
151	16	512=59	511+59.127	[0 8004]	[-1050 1050]	1057	[7 10111]
157	16	512=41	511+41.127	[0 5718]	[-1092 1092]	1099	[7 7609]
163	16	512=23	511+23.127	[0 3432]	[-1134 1134]	1141	[7 5707]
167	16	512=11	511+11.127	[0 1908]	[-1162 1162]	1169	[7 4239]
173	16	256=83	255+83.255	[0 21420]	[-1204 1204]	1211	[7 23835]
179	16	256=77	255+77.255	[0 19890]	[-1246 1246]	1253	[7 22389]
181	16	256=75	255+75.255	[0 19380]	[-1260 1260]	1267	[7 21907]
191	16	256=65	255+65.255	[0 16830]	[-1330 1330]	1337	[7 19497]
193	16	256=63	255+63.255	[0 16320]	[-1344 1344]	1351	[7 19015]

Section 4 – Formats.

Afmt consist of one skip/terminate byte (for sparsity) and seven bytes, where the top nybble of each byte specifies which of the 16 slots to add and the second nybble which to subtract. Each byte of Afmt is looked up in a table Thpa, which is populated in hpmitabas (in tabmake.c) by first interpreting the program using Dfmt bytes, and then trying all pairs (i,j) to see what slot[i]-slot[j] comes to (as Dfmt using DSSub) and setting Thpa[that] to be (i<<4)+j.

The cauldron is always 128 bytes, so is 126 columns (p=5 so as to be an integral number of Dfmt bytes), 128 columns (7,11,13), 96 columns (17-61 if sse4.1 available) and 64 columns otherwise.

Bfmt is simply Dfmt, with the sparsity tested and the extra zero rows/columns added to make the brick complete. Expansion is done in BSeed . .
f->SeedMagic==1	expands from 8 to 16 bits.
f->SeedMagic==4	expands from 8 to 10 bits.
f->SeedMagic==5	expands from two in a byte to one in a byte (for 7,11,13).
f->SeedMagic==6	expands from three in a byte to one in a byte (5 only).
In the Bwa, the values are always in the range 0 . . . (p-1).

Cfmt consists of 8, 10 or 16-bit quantites with a bias added, so that the next round of subtractions will not underflow. Nevertheless the entries are correct mod p and CtoD has only to reduce the numbers mod p to get them ready for packing, which in the case of p={5,7,11,13} requires putting more than one in a byte. This is done in 'c' using f->bar48, set (in FieldASet) to be 248/prime rounded up. Division by the prime (a rather slow instruction) is avoided by multiplying by f->bar48 then shifting 48 positions right, which is always correct with 16-bit numbers.

Section 5 – Parameters in f->parms structure.

The FIELD structure has an array of nine uint64_t values passed to the performance critical BwaMad routines pcjas, pcaas, pcjat and pcdas, and also the BSeed routine pcdasc. This is populated by hpmitabas (in tabmake.c) with the following meanings.

f->parms[0] characteristic. Repeated every 8,10,16 bits
f->parms[1] shift for "red" in table. Scalar 64-bit value
f->parms[2] mask to get top bits for reduction. Repeated every 8,10,16 bits.
f->parms[3] 2^S (f->parms[1]) - p. repeated every 8,10,16 bits.
f->parms[4] size of one slot - always 128. Scalar. \ multiplied to give
f->parms[5] size of AS code (slots used). Scalar. / slice stride.
f->parms[6] always 7. Scalar. Used in pcdasc but not BwaMad - implicitly 7.
f->parms[7] 2^S % p, repeated (16 / 32) bits depending on which multiply in use.
f->parms[8] = czer - bias as uint64_t. Repeated every 8,10,16 bits.

Section 6 – Greasing the brick.

The greasing of the brick is done seven times - once for each slice. The intial value(s) are put in by BSeed, putting row 1 (17-193), rows 1 and 2 (7-11) or trows 1, 2 and 3 (5) into each slice. Row zero is always zero (set by BwaInit). The computation runs with the "accumulator" initially holding row 1, and the "destination" pointer set to row 2.
The f->prog (copied from achain in tabmake.c) is then interpreted. There are four kinds of bytes.
Values 0-79 are the "star" chain values. The specified row is added into the accumulator, the result stored in the "destination" which is then incremented.
Values 80-159 load the accumulator from row (value - 80).
Values 160-239 set the destination pointer as (value-160)
Value 255 is the terminator.

As an example, the table (in achain) for 19 is
  19,6,5, 1,1,3,163,3,255, whose meaning is . . .
For the prime 19, there are 6 bytes of code. (the shift for reduction is 5 places)
acc = 1 dest = 2	0 1
1	acc = 2 dest = 3	0 1 2
1	acc = 3 dest = 4	0 1 2 3
3	acc = 6 dest = 5	0 1 2 3 6
163	acc = 6 dest = 3	0 1 2 3 6
3	acc = 9 dest = 4	0 1 2 9 6

The achain tables were all computed by hand, but have been tested. Hence the AS-codes in section 2 are only given implicitly by following the achain program, as is done to populate Thpa for Afmt conversion.

The following of the program is the job of pcdasc, which works in SSE only (no AVX version so far). In pcdasc reduction is done relying on the fact that the numbers in both the accumulator and in the slots are at most p-1. It is done by adding 2N-p from f->parms[3], AND with the mask from f->parms[2], then shifting right f->parms[1] places then subtracting the shifted value from the unshifted value to get a mask which is all 1 if the number was bigger than p, and all 0 if not. This mask is ANDed with p and subtracted to complete the reduction.