Meataxe-64
HPMI specification.
Richard Parker 18.3.2019
** This document is incomplete **

Section 1 – Introduction

This document specifies and describes the High Performance Meataxe Interface (HPMI). At present, the HPMI does matrix multiplication over fields of prime order between 2 and 193 inclusive, though the design is usable for larger primes also. Extension fields are done using the "linf" module to reduce the problem to matrix multiplication over the prime field, so also rely on the performance of the HPMI, and though in principle the HPMI could be used directly for extension fields, so far I know of no case where this would be the fastest method.

This document is aimed at assisting both the use and the maintenance of the HPMI modules, and also provides the low-level description for anyone wishing to understand the technology being used.

The primary objective of the HPMI is to achieve the fastest possible matrix multiply-and-add, for which the BrickMad function is used to perform C += A x B for a particular size and shape - namely alcove x cauldron - chosen by the HPMI - of a brick of matrix B, and though the number of rows (a box) of A/C may vary, there is a number recbox that is recommended by the HPMI so that matrix C can be expected to reside in a suitable cache level - usually L2.

The overall objective is to multiply matrices held in the general-purpose format called Dfmt, but to do so at top speed, it is usually best to do some reformating (an operation of quadratic complexity) to minimize the work done at cubic complexity. The HPMI assumes that this is always done, and in no case so far has this proved inappropriate. In particular, handling padding (at the left-hand and bottom of the matrix) and sparsity seems worthwhile even when avoiding the "move" might otherwise seem worthwhile.

Therefore, the HPMI converts matrix A into a suitable format (Afmt), matrix B into another suitable format (Bfmt), computes the result of C+=AxB in a third format (Cfmt) and provides routines for performing the necessary format conversions - the idea being that the format conversions are done to relatively massive matrices, so that the conversion time becomes relatively negligible compared to the (cubic) multiplication time. As an aside, usually it seems to be better to do large-scale additions in Dfmt rather than doing a conversion from Dfmt to Cfmt to avoid it. For this reason, there is no "reverse" conversion from Dfmt to Cfmt.

The principle is that to compute C = A x B we . . .

DtoA	Convert A from Dfmt to Afmt
DtoB	Convert B from Dfmt to Bfmt
CZer	Zeroize C
BrickMad	Do all the multiply-and-adds
CtoD	Convert C from Cfmt to Dfmt.

A programmer wishing to implement a new characteristic typically first writes BrickMad to work as fast as possible on that machine, thereby defining Afmt, Bfmt and Cfmt, and then writes the conversion programs.

BrickMad itself consists of three phases, though with the possible exception of a user wishing to keep a small number of seeded/greased bricks, the programmer using the HPMI will not need to know this.

BSeed	to put the vectors of B into the Brick Work Area (BWA).
BGrease	to compute all the linear combinations necessary
BwaMad	to actually perform the work.

The latter is almost always written in assembler, and is the performance-critical heart of meataxe64. For small characteristics, anyway, the BGrease operation can also be of some importance in the performance sense.

All these routines are specified, with performance as the only objective, leaving extension fields, memory allocation, Strassen etc. to the calling functions. In meataxe64 these are handled by linf and slab.

Section 2 – The abstract form of HPMI data.

A programmer wishing to use the HPMI routines directly, as well as a programmer wishing to maintain the HPMI code itself, needs to be aware of the abstractions used for the various formats. The aim is that the HPMI can be used in a uniform way irrespective of the prime it is working over, and as the methods used internally vary considerably, the structure of HPMI data (Afmt, Bfmt and Cfmt) is not entirely straightforward. This section therefore aims to make this abstract structure clear. Some of the variables are contained in the FIELD structure, and are populated by hpmiset. Others are chosen - often necessarily with some care - by the calling routines.

Section 2.1 - Afmt

void DtoA(DSPACE * ds, uint64_t * ix, Dfmt *d, Afmt *a,
uint64_t nor, uint64_t stride)

Afmt conversion is designed to take an integral number of Dfmt bytes at a time. The number of rows (the box) may be any value, but it is recommended that recbox be used except for the last box (which will be smaller) so that the cache be appropriately used for the Cfmt. The ix array must be of a size sufficient to hold all the alcoves, and the correct size is noc/alcove (rounded up) uint64_t variables, or 8*(noc+f->alcove-1)/f->alcove) bytes. The stride parameter is the number of bytes in a full row and is there to allow partial conversions - see appendix 1.

Many alcoves are, in general, converted by this call, so that the output needs a rigidly defined memory layout. The Afmt area must be allocated by the caller as a collection of alcoves numbering noc/alcove (rounded up), where each alcove consists of abase + (nor * alcovebytes). In fact, the total allocation must be at least eight bytes longer than this to allow for 8-bytes loads. The "abase" quantity is usually 1 (allowing for the terminator) but sometimes (e.g. for the "NEW2" method), there may be additional Afmt needed to prepare the brick for use specific to the alcove.

The output of the j-th alcove therefore starts at a + (j * [abase + nor*alcovebytes]). If there is considerable sparsity, it may well be that the output for some alcoves is considerably less than abase+nor*alcovebytes in length, but no mechanism is provided to salvage this space, though this would in principle be possible - perhaps by providing a function "how long is this chunk of Afmt".

There is a parameter "recbox" which is provided by the HPMI in the FIELD structure as being a suitable value for the number of rows to use for this call, and it is recommended that this be used for all but the last chunk of rows. The HPMI chooses this with regard to the size of L2 cache (so that maxbox cauldrons of Cfmt live comfortably in L2) and also with regard to the L1 cache structure for the DtoA call.

As a rule, DtoA is implemented by processing each row in turn, appending the Afmt to each alcove as it goes. This would thrash the cache if maxbox*alcovebytes were, for example, 4096 or very close, but hpmiset has enough information to make a good choice and avoid this problem.

There is no need to align the Afmt in any way, though it is best aligned at least 8 bytes (which malloc does anyway). There may also be a small performance improvement for some future characteristics if it is allocated to a cache-line boundary, but even pmul does not do this at the moment.

The structure of Afmt is specifed by AfmtMagic value. 2 is the standard GF(2), 2 uses each byte translated via Thpa - somewhat coincidentally the grease value for the AS codes is always the number of entries in a byte - for 5-193 - the AS codes, and 3 is for GF(3) getting out of Logic-6 format.

Section 2.2 - Bfmt

Bfmt encodes one "brick" - an alcove x cauldron submatrix - in a form suitable for use in BrickMad. The caller may scatter bricks of Bfmt around memory at will (provided their location is recorded!). A call to DtoB may populate the Bfmt area with f->bbrickbytes of data, or it may use less. The exact amount used is returned by the call. At present this will either be f->bbrickbytes or 1 - a one-byte flag specifying (==0) that the entire brick is zero or (==1) that it is not. Later intermediate length values are thinkable if partial sparsity is ever implemented. Apart from cache considerations, there is no requirement for Bfmt to be aligned in any way. In all cases so far, an array of blocks each f->bbrickbytes long holds the data, though a reduced memory usage (and hence cache occupation) is possible if the matrix is very sparse.

uint64_t DtoB (DSPACE * ds, Dfmt * d, Bfmt * b, uint64_t nor, uint64_t stride)

This function produces one brick of Bfmt from the input Dfmt. The input starts at the pointer d, which is typically in the middle of a row but must be on a byte boundary. The cauldron is defined to be an integral number of bytes, available in f->dfmtcauld, so this is viable. The DSPACE is set to the size of the Bfmt, and hence usually has cauldron columns but may be smaller if the end of the matrix is being processed. The "stride" parameter gives the actual length of the Dfmt rows - the number of bytes between corresponding columns of the input. Similarly "nor" will usually be <alcove>, but may be smaller at the bottom of the matrix. The output is at most f->bbrickbytes long, but may be smaller. It is not unreasonable to simply treat the Bfmt as a collection of bricks each of exactly that size, but the actual size of the conversion is returned (the uint64_t return value) so that any wasted space (due to sparsity in matrix B) can be salvaged if required.

There is no function to convert Bfmt back into Dfmt. This is, in principle, possible, but no use for such a function has yet arisen.

For all characteristics except 3, Bfmt is simply Dfmt (indicated by BfmtMagic==1), except that sparsity (whole brick = 0) is tested, and incomplete rows and columns (the left and bottom of the matrix) have been zeroized so that the (presumably repeated) BSeed calls can be faster.
For characteristic 3 (BfmtMagic==3), the reformat for Logic6 is done, which is a moderately slow and complicated operation.
Other values of BfmtMagic (including 2 - can't remember why) are available for future use.

Section 2.3 - Cfmt

A block of Cfmt consists of "nz2" blocks, each being "nor" rows of "cfmtcauld" bytes. A cauldron is guaranteed to be an integral number of bytes in Dfmt. The Cfmt represents a matrix with nor rows and noc columns, where nz2 is the minimum number of cauldrons needed to hold noc columns (i.e. noc/cauldron rounded up). Notice that each block is all the rows for a single cauldron of columns. Hence the first nor x cfmtcauld bytes are the first few columns all the way down the matrix, and only after this come the next few columns - again all the way down the matrix. There is no padding at the end of each block - a block has precisely nor rows with no appended zero rows - but the last cauldron will usually have appended zero columns to make the cauldron complete.

Section 2.3.1 - CZer

void CZer(DSPACE * ds, Cfmt *c, uint64_t nor) is used to set a complete matrix to (Cfmt) zero. It should not be assumed that binary zero will do this, as - more often than not - this is not the case. Mod 3, for example, zero is all 1 in binary and for AS primes there is a bias.

Section 2.3.2 - CtoD

void CtoD(DSPACE * ds, Cfmt *c, Dfmt *d, uint64_t nor, uint64_t stride) is used to convert a complete matrix in Cfmt into Dfmt. Notice that ds.noc may not be an integral number of cauldrons, so this routine must cater for partial extraction from the last cauldron.

A pointer to a Cfmt matrix should be aligned to 64 bytes, but there is no guarantee that cauldbytes will be divisible by 64 bytes, in which case a lesser alignment will be tolerated. In other words if X is 64-byte aligned, then X + N.cauldbytes is acceptably aligned for all values of N.

One use for the routine is to convert a complete matrix, and for this, the "stride" variable is simply the number of bytes used in for the vector.

It is also possible to use this routine when the Cfmt is not the complete matrix. In this case it must be either an integral number of cauldrons (and the DSPACE set to that length) or it must be the end of the Dfmt row (in which case the DSPACE must be set to the number of columns in the part represented. In either case the Cfmt pointer must point to the beginning of a cauldron. This allows for a long Dfmt row to be made by plonking several complete cauldrons in.

In all cases, the "stride" parameter is the length in bytes of the actual destination Dfmt row, which may therefore be considerably larger than the DSPACE and Cfmt rows.

Notice that even if matrix C is dealt with in multiple "boxes", Cfmt goes all the way down the first cauldron to the bottom before starting on the second one - there is no relation between the way the rows of A are divided and those of C. The current usage converts the entire matrix C to Dfmt, of unbounded size, with one call. It would be possible to do it piecewise, in an attempt perhaps to keep C in cache, though with the penalty of loading the translation tables more often into cache. I have little insight as to which might be better, but the HPMI itself does not dictate it.

The structure of Cfmt is specifed by CfmtMagic, where 1 is simply Dfmt, 2 is uint16_t, 3 is Logic-6 for GF(3), 4 is three 10-bit itemsin a uint32_t, 5 and 6 are uint8_t where 6 is GF(5) so packs three to a byte in Dfmt. In cases 2,4,5,6 a reduction modulo p is needed as there is a bias (always divisible by p) added.

Section 3 – Using the HPMI

It is not really expected that the HPMI be used very much on its own. Matrix multiplication is handled over the ground field by the "pmul" module, over extension fields by the "linf" module, and usually the yet-higher "slab" module is used to handle matrix multiplication over arbitrary fields, including those that where the HPMI and/or the linf implementations are not yet available.

Nevertheless some upgrades of all these modules are anticipated in future, particularly in the area of Gaussian and the better use of cache, so it seems appropriate to get the use of the HPMI documented, partly to facilitate these upgrades and partly to highlight any remaining difficuties with its use.

The routine hpmiset must be called first. This is often done as a result of calling FieldSet (in the "slab" module). It sets a collection of public variables, and also some "private" variables and tables for use only by the hpmi module. If lower level control is wanted, FieldASet1 is called first (which does not call either of hpmiset nor linftab) and then calling hpmiset.

void hpmiset(FIELD * f) to set (into the given field) the public and private variables for the HPMI to work in the characteristic of the given field. If there is not an HPMI implementation available, the "cauldron" variable is set to zero.

The HPMI works by dividing matrix B (the right-hand multiplier) into bricks which consist of an alcove x cauldron rectangle of the matrix, where both alcove and cauldron are chosen by hpmiset. A right-hand multiplier always consists of complete bricks, so that frequently extra zero columns are added to the last brick of a row and extra zero rows added to the bottom to ensure this. This is all handled in the HPMI routines, however - the Dfmt matrices do not need to be padded.

The DtoA and DtoB routines take a DSPACE and a stride. The DSPACE specifies how long the row is whose conversion is requested, whereas the stride specifies how many bytes are in the row altogether. This allows the extraction of a subset of the columns without the need to chop the Dfmt up first. Both require the caller to be aware of the structure of the destination format as described above. The DSPACE, as always, contains a pointer to the FIELD structure.

A block of Afmt is therefore box x alcove, a block of Bfmt is alcove x cauldron and a block of Cfmt is box x alcove. box is usually "recbox" and is a thousand or two rows. Only DtoB is really designed to handle a single block, however.

The main driving routine for the HPMI in meataxe64 is PLMul (in pmul.c). This handles a matrix of any size, though it is often a few thousand in all three dimensions, particularly if Strassen kicks in. The first step here is to convert matrix B in its entirety to Bfmt, one brick at a time and the last step is to convert matrix C into Dfmt with one single monstrous call.

Between these there are three nested loops.

The outer one is over "boxes" down A/C. For each box . . .
The Afmt is made
The next loop is over the cauldrons of B/C. For each cauldron k
The next loop is over the alcoves of A/B. For each alcove j
BrickMad of box x alcove x cauldron

It is far from clear that this is the best order of events. In particular it may be wise to try to keep parts of both A and B in cache as well as C, on which the above order concentrates.

The conversion to Bfmt does and from Cfmt can work one block at a time. DtoA must start on a byte boundary, so that N alcoves must be processed by any call except the last, where N alcoves is an integral number of bytes of Dfmt. In other words N*alcove must be divisible by f->pentbyte for each call except possibly the last in the row.

Section 4 – Implementing in the HPMI

Section 4.1. Strategy for writing an HPMI implementation.

At the very heart of the drive for performance in meataxe64 is the BwaMad routine, and the initial design effort naturally starts here. A value for <alcove> and <cauldron> are to be chosen so that the Brick Work Area (BWA) is of a size appropriate to the expected placement in cache (usually L1). The second consideration is to design BSeed and BGrease to populate the BWA with the intended structure, taking into account the intended grease code. It can easily happen that computing the greased vectors, which is done frequently, threatens to swamp the time taken for BwaMad, making an otherwise good scheme less attractive. Also, there is often a compromise to strike between leaving too much work to the BSeed routine versus increasing the size of the brick in Bfmt. After this, the job of converting writing DtoA, DtoB and CtoD are often fairly routine - indeed some may already be available.

In addition to the public variables, there are eight compulsory private ones that must be supplied by hpmiset. These are AfmtMagic, BfmtMagic, CfmtMagic, SeedMagic, GreaseMagic and BwaMagic, which are used to decide which functions to exectute, and czer to hold the value to initialize a Cfmt matrix to zero (in Czer) and bzer to hold the value to initialize the BWA. There may also be tables (computed by tabmake.c) of which the current ones are

Thpv	To deal with Dfmt -> bit values for characteristics 3-13
Thpa	To assist with Afmt conversion - typically a grease code table
Thpb	To assist with Bfmt conversion
Thpc	To assist with Cfmt -> Dfmt conversion.

Section 4.2. Variables and tables set (in FIELD) by hpmiset

Firstly there are the six "Magic" numbers, used to switch the stated routine between various algorithms. These are described below

AfmtMagic	DtoA
BfmtMagic	DtoB
CfmtMagic	CtoD
SeedMagic	BSeed
GreaseMagic	BGrease
BwaMagic	BwaMad

czer	The value put in all words of Cfmt to set it to zero
bzer	The value put in all words of the bwa to initialize it
bfmtcauldbytes	The number of bytes in a cauldron in Bfmt

Firstly the CZer function currently sets every word to be the czer value, and the BwaInit sets every word to the bzer value. There are currently no "Magic" values for either of these two routines, but in principle they may be needed later.

Section 4.3. DtoA

The overall control of this routine is provided by the AfmtMagic parameter in the FIELD structure

If AfmtMagic==1, further detail provided by the alcovebytes parameter, so that each block of Afmt is alcovebytes long, consisting of a 1-byte skip/terminator value and (alcovebytes-1) bytes of Dfmt data, except if all those bytes are zero it is treated as sparsity as described below ("Skip/Terminate).

If AfmtMagic==2, each block of Afmt is 8 bytes long, consisting of the skip/terminate byte and seven bytes produced by looking up a byte of Dfmt in the Thpa table. If all seven input bytes are (Dfmt) zero, it is treated as sparsity as described below ("Skip/Terminate).

If AfmtMagic==3, at present it converts batches of 12 entries into one skip/terminate and three Afmt bytes converted for use in characteristic 3 only. This may need to be revisited and generalized later. It is currently fixed at 3 slices of grease level 4 with a particular layout of the BWA assumed. The Thpv and Thpa tables are used for this conversion.

The Skip/Terminate byte is used in all the above methods. Before each alcove of Afmt data (3 or 4 bytes) comes a byte that specifies how many zero alcoves have been skipped. This may take any value up to (and including) 250. If more than 250 zero alcoves are encounterend, 250 are skipped but then one is actually output as zero, thereby allowing another up-to-250 zero rows to be skipped. This byte takes the value 255 to indicate that there are no more (non-zero) rows, and the detection of this value terminates the BwaMad.

In principle there are no restrictions on the designer, apart from being able to give a reasonable maximum size in "alcovebytes". Sparsity detection is not compulsory.

Section 4.4. DtoB

The operation of this routine is controlled by the BftmMagic variable which currently, because BfmtMagic=1 is just Dfmt, only takes two values.

If BfmtMagic==1 the Bfmt consists of Dfmt, with <alcove> rows of <bfmtcauld> bytes taken (with edge and bottom protection) from the input Dfmt matrix and put (starting at the second byte, leaving room for the sparsity indicator) into the Bfmt. If the Dfmt is entirely zero, the first byte is set to 0 and the length returned as 1. Otherwise the first byte is set to 1 and the length returned as 1 + alcove*bfmtcauld.

If BfmtMagic==3, A conversion specific for characteristic 3 is performed. This includes converting the matrix into the logic-6 bit-slice format using the Thpb look-up table to convert Dfmt bytes into logic-six-like format.

There is no function to convert Bfmt back into Dfmt.

The programmer should note the following when considering Bfmt.

1. There should usually be a fast-path for the case of a full-sized brick. Typically at least 95% of the calls to DtoB will be full-sized, so that tests for the exceptional smaller cases should ideally be excluded from the inner loops in the fast-path.

2. Nevertheless the routine must cater for the case of fewer rows, fewer columns or (typically 0.04% of the calls) both, padding out the resulting Bfmt with zero columns and/or rows to make the output brick of standard size.

3. Notice that the BSeed routine has an opportunity for further processing, so that Bfmt is truly a format private to the HPMI. Bfmt itself is chosen to do as much of the conversion work as possible, subject to not expanding the data size too much (for memory bandwidth reasons). Typically the BGrease does the computation of the extra rows needed for grease - it being faster to recompute them each time than to fetch them from memory.

4. In principle Bfmt can be chosen freely. In practice it is common to use the first byte as a flag (0 means the whole brick is zero, 1 means it is non-zero) to save time when matrix B is very sparse.

5. If the number of columns (noc) does not specify an integral number of bytes, the DtoB routine may assume that the remainder of the last byte of Dfmt is zero. Hence, DtoB may only be called with noc not divisible by pentbyte at the right-hand end of the row.

Section 4.5. CtoD

The overall control of this routine is provided by the CfmtMagic parameter in the FIELD structure

If CfmtMagic==1, the data (typically dfmtcauld bytes long) is simply copied out of the bwa into the correct position in the Dfmt matrix.

If CfmtMagic==2, the data is extracted as uint16_t from the Cfmt, bar48 used to reduce it, and the data is then put as a uint8 into the receiving Dfmt.

If CfmtMagic==3, the Thpc table is used to convert from a logic-6 format back into Dfmt. This is specialized for characteristic 3 use.

If CfmtMagic==4 (10 bits) the data is extracted as uint32_t from the Cfmt, split into three values, then reduced using bar48 then the three items put separately into three bytes of Dfmt. This is suitable for characteristics 17-61, and only if SSE4.1 is available so that reduction can use the 32-bit multiply (otherwise CfmtMagic=2 is used and these primes are done in 16 bits).

If CfmtMagic==5, the data is extracted as uint8_t from the Cfmt, bar48 used to reduce it, and two items are then put together for Dfmt byte ouptut, as needed for characteristics 7,11,13.

If CfmtMagic==6, the data is extracted as uint8_t from the Cfmt, bar48 used to reduce it, and three items a put together for each byte of Dfmt outpt, catering for characteristic 5.

Section 4.6 - BrickMad

For normal use, the simplest way to do the key brick-multiply-and-add is to use the BrickMad function.

void BrickMad(FIELD *f, uint8_t * bwa, Afmt *a, Bfmt *b, Cfmt *c) to get the Bfmt brick b into the bwa and grease it, and then to multiply it by the Afmt string a (of arbitrary length), adding the result into the Cfmt block c (of the "same" length).

The number of rows of A/C is specified implicitly by the Afmt, and the other two dimensions are fixed - alcove and cauldron.

As mentioned in the introduction, BrickMad internally consists of three component subroutines - BSeed, BGrease and BwaMad. There is usually no need to understand these three components. They are there partly to clarify implementation, and partly to allow for the possibility that repeated BSeed and BGrease calls can be avoided, though this is normally counter-productive since usually more time will be lost moving the data around (the BWA is often considerably larger than the Bfmt brick) than will be saved.

The documentation of BSeed, BGrease and BwaMad are therefore included below.

Section 4.7. BSeed

The overall control of this routine is provided by the SeedMagic parameter in the FIELD structure

If SeedMagic==1, (8->16) the vectors (depending on slots and slices) are put into the correct positions by loading as uint8_t and storing as uint16_t.

If SeedMagic==2, the vectors are memcpy'd into the correct positions in the BWA for characteristic 2 use, going to positions 1,2,4,8,17,18,20,24,33,34, . . .

If SeedMagic==3, the vectors are similarly memcpy'd into the correct positions for characteristic 3 use, namely 1,2,5,14,42,43,46,55,83,84,87,96

If SeedMagic==4, (8->10) the vectors are converted from 8 bits to 10 bits, putting three in each 32-bit word. The cauldron must be divisible by 3.

If SeedMagic==5, ("4"->8) Each byte of the Dfmt produces two bytes of 8-bit output. The cauldron must be divisible by 2.

If SeedMagic==6, (Characteristic 5 ->8) Each byte of Dfmt provides three bytes of output as needed for characteristic 5. The cauldron must be divisible by 3.

If SeedMagic==7, (New characteristic 2) the whole block of 32x128 bytes is copied into the brick work area missing the first position (which is left as zero).

Section 4.8. BGrease

The overall control of this routine is provided by the GreaseMagic parameter in the FIELD structure.

If GreaseMagic==1, the pcchain routine is used to make all the greased multiples.

If GreaseMagic==2, the pcxor routine is used to make all (8x11) further rows needed in the grease table for characteristic 2.

If GreaseMagic==3, the pcad3 routine is used to make all (3x36) further rows needed in the grease table for characteristic 3.

Section 4.9. BwaMad

At the very heart of the drive for performance in meataxe64 is the BwaMad routine.

void BwaMad(const FIELD *f, uint8_t * bwa, int sparsity, Afmt *af, Cfmt *c) to do C += A x B, where A is the <box> x <alcove> matrix encoded by the Afmt in af, B is the <alcove> x <cauldron> matrix held (and usually greased according to the sparsity value) in the brick work area bwa, and C is the <box> x <cauldron> Cfmt matrix at c. The values of <alcove> and <cauldron> are constants determined by the HPMI (and set by hpmiset into the FIELD structure) but the value of <box> can vary, though it often takes the recommended value <recbox> suitable for the processor.

In principle, the DtoB routine (convert to Bfmt) may inspect the brick and select a <sparsity> value suitable for that particular brick, allowing the BSeed and BGrease complete freedom as to how the bwa is populated. Notice that the Afmt and Cfmt cannot depend on the brick, so the scope here is limited. In practice, so far sparsity is either zero (brick is zero) or 1 (brick is non-zero).

The overall control of this routine is provided by the BwaMagic parameter in the FIELD structure.

If BwaMagic==1, the pcjas (AVX) or pcaas (SSE) routines (in pcrit) are used to perform the BrickMad depending on the machine type 'mact'. This uses 16-bit multiply operation. Note that this needs the "parms" are to be correctly set up. This is suitable for 8 or 16 bit operation (but not 10, for which BwaMagic is 4).

If BwaMagic==2, the pcbm2 routine (in pcrit) is called to perform the operation

If BwaMagic==3, the pcbm3 routine (in pcrit) is called to perform the operation.

If BwaMagic==4, the pcjat (AVX) or pcdas (SSE) routines (in pcrit) are used to perform the BrickMad depending on the machine type 'mact'. This uses 32-bit multiply operation and hence needs SSE4.1. This is only used for 10-bit primes.

If BwaMagic==5, the pch2 routine (in pcrit) is called to perform the operation for characteristic 2 using the new methods.

Section 4.10. BwaInit.

extern void BwaInit(const FIELD *f, uint8_t *bwa) to initialize the given bwa (Brick Work Area) to be suitable for working over the given field. This typically sets the vectors to zero that will need to be zero for every possible brick.

Appendix 1 – Exact rules for noc.

DtoA. If the noc parameter is divisible by the number of entries in a byte (pentbyte) there is no difficulty. If it is not divisible, however, the remainder of columns in the last byte must be zero. This will be the case at the end of a row, but will not, in general, be true otherwise. Hence if it is required to convert partial rows into Afmt all partial rows except the last must consist of a number of columns divisible by pentbyte. This will anyway be needed so that the next part starts on a byte boundary. It would also be efficient if each part were an integral number of alcoves, so that no time is wasted adding in needless zero vectors.

DtoB. Again the noc parameter must either be divisible by the number if entries in a byte (pentbyte) or the remaining columns in the last byte must be zero. As a rule, all but the last brick will anyway be <cauldron> columns wide, and it is guaranteed that cauldron is divisible by pentbyte (in contrast to the situation in DtoA).

CtoD. Here there is no choice. The matrix given to CtoD must be a complete matrix, and DCut/DPaste used to make smaller matrices if this is required.

Appendix 2 – Characteristic 3.

In may ways, characteristic 3 is exceptional. In particular a block of Afmt is not an integral number of bytes of Dfmt, and the bit-slice nature of operations necessitates several features that are not needed in any other characteristic. In particular there are four look-up tables needed.

Thpv is a table to convert mod-3 Dfmt, with five entries per byte, into a 10-bit field with two bits per entry. The conversion is little-endian to little-endian, so that the "first" entry of the Dfmt ends up in the bottom two bits after lookup. Thpv consists of 243 16-bit integers.

Thpa is used to convert into Afmt. It is a byte->byte table converting quadruples of numbers mod 3 in a format where each entry occupies 2 bits (as emergest from Thpv) into their position in the grease table . . . either 0 or and even number 2-80 being a vector whose first entry is 1, and the next being its negative. Hence the semantics is

0000 0000 0001 0002 0010 0020 0011 0022 0012 0021 0100 0200 0101 0202 . . .

but the table is the inverse - given the four-entry vector, where does it appear in this list. This table is very specific (at the moment anyway) to a grease level of four.

Thpb is used to convert from Dfmt into Bfmt. It is a table converting a five-entry Dfmt byte into a 64-bit field, where bottom five bits of the top 32-bits are 1 unless the corresponding entry is 1, and the bottom five bits are 1 unless the corresponding entry is 2. Bfmt can then be made by processing chunks of data five bits at a time.

Thpc is used to convert from Cfmt into Dfmt, and does the reverse computation, except that the input is only 10 bits long instead of 64.