Meataxe-64 - Pcrit.
Richard Parker 2.5.2019

Section 1 – Introduction

The performance critical routines of meataxe64 are held in four source files as follows . . .

- pc1.s General functions, mainly called from field.c
- pc2.s HPMI in characteristic 2
- pc3.s HPMI in characteristic 3
- pc5.s HPMI using Add/Subtract technology for 5-193.

They are written in x86 assembler (meataxe64 only works on 64-bit x86 chips), and have names beginning "pc" - Performance Critical.

Meataxe64 classifies x86 computers into broad classes labelled with the letters a-m, where a is the oldest and m represents a computer with AVX-512. Several routines have been implemented several times so that they run ever faster on more modern machines.

The main purpose of these routines is to enable the HPMI to multiply matrices at the maximum possible speed. These are all described in section 2.

The pc1 routines are described in section 3, and are, in principle, for general-purpose use. They are mainly called from the "field.c" module to speed up some of the critical Dfmt functions.

Section 2 – HPMI routines.

There are basically ony two kinds or routines for HPMI use - the "bm" routines to do the main BrickMad functionality, and the "ac" (addition-chain) routines to grease the brick prior to BrickMad. These are implemented in a broadly similar way for p=2, p=3 and p=5-193, and also for SSE, AVX-2 and (for some) AVX-512.

The BrickMad routines.

These functions are all broadly similar. They take a pointer to the Afmt (a), a pointer to the Brick (bv) and a pointer to the Cfmt (c), and performs the function of multiplying the matrix represented by a by the matrix represented by bv, and adds the result into the matrix represented by c, where pc2... is characteristic 2, pc3... is characteristic 3 and pc5... is for 5-193. The pc5 routines take a further parameter "parms" containing nine words used by the routines to drive the computation. The pc*bma routines use SSE and should run on all 64-bit x86 machines (though this has not been tested on any machine earlier than "Nehalem" as I have not been able to lay my hands on one). Similarly pc*bmj uses AVX-2 and pc*bmm uses AVX-512. For pc5, there are the bmw and bmd versions for SSE and AVX-2, where bmw does the multiplications used in reduction at the word (16-bit) length, whereas the bmd routines use the doubleword (32-bit) multiplies, which are a little slower and need SSE4.1 (hence the name pc5bmdd, where the last 'd' indicates class d - where SSE4.1 is present). On AVX-512, the 32-bit version is always used - it is the same speed, and it saves having another machine class for the BW option.

Here are the prototypes for the BrickMad functions.

void pc2bma(const uint8_t *a, uint8_t * bv, uint8_t *c);
void pc2bmj(const uint8_t *a, uint8_t * bv, uint8_t *c);
void pc3bma(const uint8_t *a, uint8_t * bv, uint8_t *c);
void pc3bmj(const uint8_t *a, uint8_t * bv, uint8_t *c);
void pc5bmwa(const uint8_t *a, uint8_t * bv, uint8_t *c, const uint64_t * parms);
void pc5bmdd(const uint8_t *a, uint8_t * bv, uint8_t *c, const uint64_t * parms);
void pc5bmwj(const uint8_t *a, uint8_t * bv, uint8_t *c, const uint64_t * parms);
void pc5bmdj(const uint8_t *a, uint8_t * bv, uint8_t *c, const uint64_t * parms);
void pc5bmdm(const uint8_t *a, uint8_t * bv, uint8_t *c, const uint64_t * parms);

The Addition Chain routines.

Again, these functions are all broadly similar. They take a pointer to a "prog" - a string of bytes interpreted to drive the population of the brick work area, a pointer to the brick work area and a "stride" used to move from one slice to the next. The number of slices is, however, implicit (eight for mod 2, three for mod 3 and seven for the AS primes).

Here are the prototypes of the functions written so far.

void pc2aca(const uint8_t *prog, uint8_t * bv, uint64_t stride);
void pc2acj(const uint8_t *prog, uint8_t * bv, uint64_t stride);
void pc2acm(const uint8_t *prog, uint8_t * bv, uint64_t stride);
void pc3aca(const uint8_t *prog, uint8_t * bv, uint64_t stride);
void pc3acj(const uint8_t *prog, uint8_t * bv, uint64_t stride);
void pc3acm(const uint8_t *prog, uint8_t * bv, uint64_t stride);
void pc5aca(const uint8_t *prog, uint8_t * bv, const uint64_t * parms);

The "parms" array is held in the FIELD structure and has the following structure.

parms[0]	The characteristic of the field - equal to f->charc.
parms[1]	A shift value S. This is used in both routines, and in different ways.
The more stringent requrement comes from pcbmas, where it must be the
shift needed to convert the masked value into the units position. In the
case of pcchain, it needs to be a shift within the bit-length of the values,
and such that 2S > characteristic.
parms[2]	The mask used in pcbmas. This must have all the bits set within the bit-
length of the values from 2S upwards. For pcchain, all that is needed is
that the 2S bit is set, and all lower bits unset.
parms[3]	2S − p. This is used only in pcchain, and is added to a value so that the
2S bit is set if and only if the value was p or greater.
parms[4]	cfmtcauld - the number of bytes in a cauldron in Cfmt. At present this
value must be 128 for both routines.
parms[5]	Slots - the number of code words for each slice. This value may be
larger than the actual number of code words - it is used to determine
where the next slice starts.
parms[6]	Slices. At present this is not used by pcbmas as it is assumed to be 7.
It should be set to 7 for future compatibility. It is used in pcchain and
must be correctly set for that routine.
parms[7]	2S % p. This is the multiplier, used only in pcbmas, to convert the
shifted masked bits into the number to add on to the lower bits.
parms[8]	Bias. This is the bias added into the values at the end of reduction to
ensure that subtraction cannot cause underflow.

The central idea is to interpret the string of bytes (in prog) as a set of instructions to compute the chain by adding two already computed multiples and then reducing modulo the prime.

The byte-code.
At the start of interpreting a byte, the following state is held.
The accumulator - a cauldron, held in vector registers.
The destination slot.

At the start, the accumulator is loaded with slot number 1 (which is always seeded by BSeed) and the destination slot set to 2.

The interpretation of the prog bytes is given below. The structure is the same for all characteristics (including 2 and 3)

0-79 add the slot of that number into the accumulator, store the result in the destination slot, and increment the destination slot. For star chains, or for parts of the computation that can be done by a star chain, these (and stop!) are the only codes needed, and they are expected to form the commonest instructions by some margin.
80-159 load the accumulator from the slot number 80 less than the byte-code.
160-239 set the destination slot to be 160 less than the byte code
240-254 Unused and reserved for future use.
255 stop - the program has completed.

As an example, take P=71
Slot	0 1 2 3 4 5 6 7 8 9 4 7
AS-code	0 1 2 3 [4] 8 12 [14] 24 25 39 53
byte-code	1 1 1 4 4 2 86 6 1 164 7 167 7 255

For the AS-primes, reduction in the Addition Chain routines (of a number known to be less than 2p) is done by the following method. Bear in mind that all these operations are done to 64-bit chunks contain more than one entry each.

Firstly a number 2S−p (provided in the parameters) is added, where S is chosen so that 2S > p. The result has the 2S bit set if and only if the result was p or larger.
Secondly a logical 'and' is done with 2S to keep this bit only. higher bits may be set in the mask, as they will not be set in the value after 2S−p has been added.
This bit (1 if reduction required, 0 if not) is then shifted into the units position (the original is retained as well.
The the shifted bit is subtracted from the unshifted bit to make a number that is either all 1 (if subtraction of p is wanted) or all zero otherwise.
A logical AND is then done between p and this result. This is then p if subtraction is required and 0 otherwise.
All that remains is to subtract this value from the original one.

Section 3 – pc1.s - general purpose - functions.

mactype.

The mactype function is used to determine the class of the machine, along with an indication of the size of the "intermediate" cache. Further bytes are not used, and set to the character '0' for future use.

void mactype(char mact[8]) to populate the 8 characters of the provided mact array with details of the machine that the software is currently running on. The idea of this routine is to answer, as simply as possible, the questions that the meataxe64 application needs answers to - basically which routines to call, and how big to make things so they are suitable for cache. By far the most important is the first byte - the class.

mact[0] - the class. The first byte is the "class", as described below, aimed at the choice of routines to call. In principle it could be advantageous to write a separate routine for each class, but in practice, for a particular job, many classes are equivalent as new instructions available are not useful. Hence, for example, the mod-2 HPMI routine exists for "legacy" SSE (class 'a'), AVX-2 (class 'j') and AVX-512 (class 'm'). These are the most important classes, but class 'd' (SSE4.1) is needed for 32-bit multiply in vectors allowing 10 bit entries for 17-61 in pc5.s.

Class 'a'. This must work on every x86-64 computer there ever was, though whether the "c" compiler and the libraries will is another matter. None of Intel's earlier notebook CPUs (Core Duo, Pentium M, Celeron M, Mobile Pentium 4) implement Intel 64, so they do not have a class at all, but very early chips did not implement the LAHF/SAHF and CMPXCHG16 instructions, and SSE3 also came later. Most processors from 2003 - 2004 and many in 2005 will need this class.

Class 'b'. The use of CMPXCHG16 and LAHF/SAHF is allowed, as are all the SSE3 extensions. Needs the following three flags (else class is 'a')
lahf_lm (LAHF in long mode) 8000001 ecx bit 0 value 1
cx16 (CMPXCHG16) %ecx bit 13 value 0x2000
pni (SSE3 - Prescott new instructions) %ecx bit 0 value 1.
Hence the programmer of a class 'b' machine may additionally use the following instructions.
LAHF, SAHF, CMPXCHG16, FISTTP LDDQU ADDSUB HADDPS MOVDDUP
MOVDDUP is a double-precision broadcast, so will be needed for the HPMI if it uses double-precision.

Class 'c'. The additional use of the SSSE3 instructions are allowed.
ssse3 (SSSE3 extensions) %ecx bit 9 value 0x200
Again, all fairly specialized instructions. The extra instructions available are . . .
PSHUFB PALIGNR PHADD/SUB PMULHRSW PMADDUBSW PABS PSIGN
I believe the VIA Nano 2000 is in this class.
AMD chips 2007-2009 seem to be in this class.
AMD low-power Bobcat is in this class.

Class 'd'. The additional use of the SSE4.1 instructions are allowed.
sse41 (SSE4.1 extensions) %ecx bit 19 value 0x80000.
This is a large set of important instructions, including the PMULDQ used in the reduction of 10-bit fields (primes 17-61) in the AS HPMI. It is the class
MOVNTDQA PACKUSDW PMOV(S/Z)X PBLENDVB PBLENDW PCMPEQQ
PINSRB/D/Q PMULLD PMULDQ PMIN/PMAX(S/U)(B/W/D)
PHMINPOSUW MPSADBW PTEST
I believe the VIA Nano 3000 and Intel Nehalem is in this class.

Class 'e'. The additional use of the SSE4.2 instructions are allowed.
sse42(SSE4.2 extensions) %ecx bit 20 value 0x100000
popcnt (POPCNT) %ecx bit 23 value 0x800000
The extra instructions available are . . .
POPCNT CRC32 PCMPGTQ PCMPESTRI etc. (Intel Manual Section 4.1)
I believe the Intel Westemere is in this class.

Class 'f'. This class allows the use fo the CLMUL instruction.
clmul (PCLMULQDQ) %ecx bit 1 value 2
The extra instruction available is just PCLMULQDQ.
This class is needed for the routines for large fields of characteristic 2.
It appears that the new low-end Intel pentium/celeron chips are in this class.

Class 'g'. This class allows the additional use of AVX instruction set, and ideally all routines using the SSE vector registers should be rewritten for this class, as it allows the VEX-encoded 128-bit instructions (rather than the "legacy" ones), as well as the three-operand versions (avoiding the occasional copying). Also allows the use of the 256-bit registers for floating point use (only).
avx (AVX-1) %ecx bit 28 value 0x10000000
The AMD Bulldozer is in this class.
The Intel Sandy/Ivy Bridge are in this class.

Class 'h'. The BMI1 instructions are new in this class.
ANDN BEXTR BLS(I/MSK/R) TZCNT
bmi1 (BMI1) 07 %ebx bit 3 value 8
The AMD Piledriver and Steamroller are in this class
The AMD low-power Jaguar is in this class.

Class 'i'. The BMI2 instructions are new in this class.
BZHI MULX PEXT/DEP RORX SARX SHRX SHLX
bmi2 (BMI2) 07 %ebx bit 8 value 0x100
I believe the AMD Excavator is in this class.

Class 'j'. Previously called HASwell. This class includes the AVX-2 instruction set, allowing the use of 256-bit registers for integer use.
avx2 (AVX-2) 07 %ebx bit 5 value 0x20
movbe (MOVBE) %ecx bit 22 value 0x400000
This class does not have fma.
There may be some Intel Haswell, Broadwell and Skylake in this class as may be AMD Ryzen. Don't know which are 'j' and which 'k'.

Class 'k'. Includes the use of Fused Multiply-Add, doubling the speed of floating point matrix multiplication but otherwise class 'h' - does not have all of BMI2, AVX2, MOVBE.
fma (Fused multiply/add) %ecx bit 12 value 0x1000.
AMD piledriver and steamroller (but not bulldozer) are in this class. bulldozer has an idioynchratic fused multiply-and-add that meataxe64 does not utilize and has no class to indicate its presence.

Class 'l'. Includes all of bmi2, avx2, movbe and fma - equivalent to j+k.

Class 'm'. Includes 'l' and AVX-512F and AVX-512DQ..

mact[1] - the seccache - secondary cache indicator.

This field is used only to decide the "recbox" parameter - the number of rows of matrix C that should be deal with at once.

It takes one of three values, and is used to guide the use of second-level cache.

seccache '0'. This indicates that the use of 128K (per thread) of second level cache is OK.
seccache '1'. This indicates that the use of 256K (per thread) of second level cache is OK.
seccache '2'. This indicates that the use of 512K (per thread) of second level cache is OK.

The remaining routines are of general purpose applicability, but designed primarily for use from the "field" module. They exist to speed up those areas of the field module that warrant it, as assembler implementation is usually faster than in "c".

void pc1xor(a/j)(Dfmt * d, const Dfmt * s1, const Dfmt * s2, int nob).
This routine performs an 'exclusive or' of a string of bytes (described as Dfmt which is a unint8_t) d = s1 ^ s2 of length 'nob' bytes. The implementations use vectorization where possible (SSE for a, AVX-2 for j) and are tuned for cases where nob is fairly large but not divisible by a large power of two, and the areas are not assumed to be aligned in any way. These routines are used in the FIELD routines DAdd and DSub in characteristic 2, and indirectly from DSMad if the scalar is 1. They are not used in the HPMI in characteristic 2, for which the pc2ac(a/j/m) and pc2bm(a/j/m) routines are used.

The ideas for the following four routines (pcunf, pcxunf, pcbif and pcbunf) originate in the year 1999 in meataxe32. They do table look-up at byte length of various sorts for use in the DAdd, DSub, DSMul and DSMad routines in field.

void pcunf(Dfmt * d, uint64_t nob, uint8_t * t1) Class 'a'.
This routine takes each byte of the string d, looks it up in the table t1, and replaces the input byte by the result. The implementation works 1 byte at a time at the moment . . . some inprovement would be possible by fetching and storing the results in larger chunks. It is only used for DSMul at the moment, though the routine may have more general applicability.

void pcxunf(Dfmt * d, Dfmt * s, uint64_t nob, uint8_t * t1) Class 'a'.
This routine takes each byte of the string s, looks it up in the table t1, XORs the result into the corresponding byte of the string d, and replaces that byte into the string d. The length of the strings is given by the 'nob' parameter. The implementation works at 8 byte length for as much of the string can be processed that way, and then does the bytes singly. The routine is only used in the DSMad routine of the field module in fields {4,8,16,32,64,128,256} when the scalar is neither 0 nor 1.

void pcbif(Dfmt * d, Dfmt * s1, Dfmt * s2, uint64_t nob, uint8_t * t2) Class 'a'.
This routine takes the two bytes, one from s1 and one from s2, looks up 256*s1+s2 in the table t2 and puts the result in the string d. All three strings are nob bytes long. The implementation works four bytes at a time except for the last 0-3, which are done singly. The routine is used in DSAdd and DSSub for fields of odd characteristic 3-251.

void pcbunf(Dfmt * d, Dfmt * s, uint64_t nob, uint8_t * t1, uint8_t * t2) Class 'a'.
This takes pairs of bytes, one from s and one from d, with 'nob' pairs of bytes processed. Firstly the s byte is looked up in the table t1, and then the result and the byte from d looked up in the table t2. It is the result of the first table look-up that is shifted 8 places, though in all the applications so far the table t2 is anyway commutative. The implementation unrolls the loop 8 times. It is used in the DSMad routine for fields of odd characteristic when the multiplier is neither 1 nor -1.

The following two routines are used for DSMad in characteristic 2 fields of order 217 - 263.

void pccl32 (const uint64_t * clpm, uint64_t scalar, uint64_t noc,
        uint32_t * d1, uint32_t * d2) Class 'g'
void pccl64 (const uint64_t * clpm, uint64_t scalar, uint64_t noc,
        uint64_t * d1, uint64_t * d2) Class 'g'
These routines use the "carryless multiplication" instruction as available if the class of the machine is at least 'g'. It takes words (either 32 or 64 bits, depending on which routine is being discussed).

The following two "Barrett" routines are used to take unsigned integers x and, given a "base" b, express x as a0+a1b+a2b2+a3b3... where the same conversions are done repeatedly to different integers x. The conversion is first "prepared" by calling the pcbarprp routine, which is given the sizes (64,32,16 bits for input, 32,16,8 bits for output, the base b, the number of digits to be produced and the maximum value that must be handled, all of which is packed up into the private array "barpar" (Barrett parameters) ready for (usually) repeated use by the pcbarrett routine. The base must not be a power of two!

This should be viewed as a preliminary version. It will be incorporated into meataxe64 as described here, but experience may dictate some changes, so the specification here should not be considered stable yet. In particular the specification of the input and output lengths may be improved, and if vector implementation are used, the mactype will need to be given to pcbarprp.

The intended use is for large-ish extension fields, where the Dfmt needs to be chopped into smaller pieces so that look-up tables can be used. This is particularly needed for PExtract and the vector add/subtract routines (probably using spac/sqid).

void pcbarprp(int inp, int oup, long base, int digits, uint64_t maxval, uint64_t * barpar) to produce the "barpar" array suitable for taking input of size inp, which must be {0,1,2} meaning 64, 32 or 16 (and is usually f->paktyp) and expressing all the inputs as "digits" to base "base" of size oup which is 1,2 or at least 3 and is often f->ppaktyp) meaning 32, 16 or 8. The maximum possible input is given in maxval and is usually f->fdef-1.

void pcbarrett(uint64_t * barpar, Dfmt * input, Dfmt * output, uint64_t entries, uint64_t stride) to perform the conversion of the input stream ("entries" long) to the output stream according to the scheme as selected by the pcbarprp call that produced the barpar array. The implementation is based on Barrett, whereby division by the base b is replaced by multiplication by 2s/b followed by a right shift of s places, and the pcbarprp routine is responsible for choosing s such that this always works. The stride is the distance between two consecutive output entries.