Meataxe-64
Albrecht Utilities.
Richard Parker 7.4.2019

Section 1 – Introduction.

This document is the "ideas" document for the project of including many more extension fields into meataxe64. As of today, a good implementation exists for all quadratic and cubic extensions and {16,32,81,243,625}, and rather less good ones for {64,128,256}. As a suggested scope, the aim is to get good ones for all non-prime fields up to 100,000.

The principle for doing this, as Martin Albrecht taught me, is to . . .

extract the matrix in the extension field pd into d matrices over the ground field p, one for each coefficient of expression of the extension field elements as polynomials over the ground field modulo the defining polynomial, which - in meataxe64 - is always taken as the Conway polynomial.

extraction linear forms are then used to make certain linear combinations of these extracted matrices over the ground field to make e matrices (e > d).

multiply these e matrices in pairs to produce e product matrices

assembly linear forms to make d linear combinations of these product matrices, which are the coefficients of the extension field, as if the answer had been extracted.

assemble these matrices to form the answer.

For large extension field degrees, performing the linear forms threatens to dominate the work, so to minimize the impact of this, there is a program zem (elementary matrices) to factorize the matrices involved in both extraction and assembly linear forms into as few operations as possible. This is considered to be of more general applicability and is documented as a "proper" program, albeit still in src2. It is based on a beam search, and it is hoped that it can find the "best" way to compute these linear forms. In principle it works over any field, though only prime fields are needed for this project.

The albf program takes as input the extraction linear forms matrix and computes from it the assembly linear forms matrix. The rows of the extraction matrix are tensored with themselves (or indeed a different extraction matrix) and the assembly linear forms needed to make the answer computed.

The albe program reads the output of albf on the extraction forms to write the 'c' code suitable for cut-n-paste into the linf.c source, and the alba program does a similar job for the assembly forms. These two program interpret the output of albf in different ways, since they must operate in opposite directions.

As of today, all the above programs are written and partly debugged - they produce an output that can drive linf, but sadly do not produce the correct answer. Hopefully a day's debugging will sort that out.

The remaining piece of the puzzle - in many ways the interesting one - is to produce the extraction linear forms matrix, and I believe that two further programs are needed, which I propose to call albi (Interpolation) and albx (eXstension).

The albx program considers the target extension field as a two-step extension. It is assumed that the first step extraction linear forms are known, and interpolation is performed to extend the field further.

The albi program uses simple interpolation, but allows for some of the point values to lie in various extension fields.

As of now, I have little idea how to do either of these.