Meataxe-64
The "functions" layer.
Richard Parker 17.12.2017

Section 1 – Introduction.

This document is the second version of the description of the "functions" layer of meataxe64. It is still expected to evolve considerably as the development continues, but the aim is that the early sections of this document specify parts that are stable, later sections less stable, yet later sections designs that are yet to be implemented and yet later ones just ideas.

Section 2 – General comments.

The functions all work with matrices held on filestore. It may be appropriate, when working with smallish matrices, to use a RAM-disk to avoid too much disk IO.

Each filename is associated with a silent flag, which is 0 if logging of this file is required and 1 if not.

If any (output!) filename is given as "NULL", the output is discarded. If the silent flag is 0, the checksum is still logged, however.

Some functions may need to chop on disk if the matrices are too big to fit in memory. As of today (1.10.17) no functions actually do this, but for future stability, the initial substring of the filenames for temporary files is given as <const char * tmp> to any functions that may need to do this.

Section 3 – Gaussian Elimination.

Matrix multiplication is relatively easy to do by repeated chopping. At least three levels are needed for fairly obvious reasons . . .

- On disk to produce sub-matrices that fit into the available memory
- In memory to produce smaller sub-matrices for individual cores to work on
- And again into yet smaller sub-matrices to make better use of cache

For Gaussian elimination, it is not too hard to chop "horizontally" so that the parts have fewer rows, albeit still of full length. To achieve maximum efficiency when chopping "vertically" as well, we must use methods that introduce a couple of concepts that may well be new to the reader who may imagine they already know all there is to know about Gaussian elimination.

NREF - Negative Reduced Echelon Form. This is the main tool used in meataxe64 for handling Gaussian elimination. For any given row space, to say that the basis is in NREF has two implications - one on the basis, and one on the way it is held in the computer.

A matrix is in NREF if
- Each row has a specified entry (its "pivotal entry" or just "pivot") that is -1, and this entry is the only non-zero entry in its column.
- The pivotal entry of any row is to the right of the pivotal entries in all previous rows,

It is not required, though usually true in practice, that the pivotal entry is the first non-zero entry in each row.

In meataxe64, an NREF matrix is held as
- A bit-string specifying which columns contain the pivots. This implies also which row that pivot in in, since the first set bit is the pivot for the first row, the second set bit is for the second row and so on.
- The remnant, containing the entries for all the rows on the columns that are not pivotal - where the bit in the bit-string is unset.

Here is an example of a matrix in NREF. Notice that it is necessary to specify the pivotal columns as exemplified here - the fifth column could alternatively be the pivot for the second row.

        0 -1 0 2 0 0 1 2
Matrix 0 0 -1 5 -1 0 7 5
        0 0 0 3 0 -1 4 2

Bit String 0 1 1 0 0 1 0 0

Remnant 0 2 0 1 2
        0 5 -1 7 5
        0 3 0 4 2

The fProduceNREF function takes a matrix and puts it into NREF using row operations. Only the column-select bit-string and the remnant R (as a matrix) are output, and (see below) the columns chosen may not be "standard".

The fProduceNREFRS function does a similar job, but produces a row select, and guarantees that both the column-select and row-select are standard.

A column is said to be standard if there is a row in the span of the rows where the first non-zero entry is in that column. Another definition is that a column is standard if it is linearly independent of all previous columns. Similarly a row is standard if it is linearly independent of all previous rows.

There are applications where any NREF for an input matrix is just fine, and in that case fProduceNREF is the correct routine to call. This gives the routine permission to use various performance-enhancing tricks. In other applications, a row-select may be rneeded and either row-select, column select or both required to be standard. This limits the routine to more conventional methods which are, hopefully, still well implemented and frequently are no slower than fProduceNREF.

As of today, even fProduceNREF produces standard columns, but this is expected to change in future and if standard columns are required, fProduceNREFRS should be used.

A common requirement is that we are given another matrix X whose rows are of the same length as our original matrix A and we wish to clear the pivotal columns in that matrix too. In meataxe64 this is done by two steps, having used either of the previous routines to put the matrix A into NREF.

The first step is to run the fColumnExtract program, that separates the columns of X, producing two matrices D and E - the selected columns and the non-selected columns.

The second step is to run fMultiplyAdd to multiply D by the remnant R and add the result into the matrix E. This way we get our result without the zero columns.

The process may be visualized by imagining the matrix A and X to be

A = -1 R

X = D E

The column-extract produces the matrices D and E, and then D.R is added to E.

Section 3 – Functions believed to be stable.

void fTranspose(char * tmp, char *in, int sin, char *out, int sout)
to transpose matrix "in" to form matrix "out".

void fMultiply(char * tmp, char *m1, int s1, char *m2, int s2, char *m3, int s3)
to multiply m1 by m2 and put the result in m3. m1 must be a matrix, m2 can be a matrix or a map.

void fMulMatrixMap(char *m1, int s1, char *x2, int s2, char *m3, int s3) to multiply a matrix m1 by the permutation or map x2 to produce the matrix m3.

void fMultiplyAdd(char * tmp, char *m1, int s1, char *m2, int s2, char *m3, int s3, char * m4, int s4) to multiply m1 by m2, add in m3 and put the result in m4. Initially this will be a composite function (just calling fmul and fadd) as a proper implementation requires memory footprint control on the matrix being added, which I haven't yet got a clear idea of.

uint64_t fProduceNREF(char * tmp, char *m1, int s1, char *b2, int s2, char *m3, int s3)
to put the matrix m1 into NREF with the bit-string of pivotal columns in b2, and the remnant in m3. The rank (number of rows) is returned. The selected columns may not be standard.

uint64_t fProduceNREFRS(char * tmp, char *m1, int s1, char *br, int sr, char *bc, int sc, char *mr, int sr)
to put the matrix m1 into NREF with the bit-string of standard pivotal rows in br, the bit-string of standard pivotal columns in bc, and the remnant in mr. The rank (number of rows) is returned.

void fAdd(char *fn1, int s1, char *fn2, int s2, char *fn3, int s3)
to add matrices fn1 and fn2, and put the result int fn3.

void fColumnExtract(char *bs, int sbs, char *in, int sin, char *sel, int ssel, char * nsel, int snsel)
to separate the columns of matrix "in" into two matrices according to the bit-string "bs". The selected columns go to "sel" and the non-selected columns go to nsel.

void fRowRiffle(char *bs, int sbs, char * ins, int sins, char * inn, int sinn, char * out, int sout) to combine the rows from ins (selected) and inn (non-selected) according to the bit-string bs, producing the output with both sets of rows (riffled) in out.

void fPivotCombine(char * b1, int s1, char * b2, int s2, char * bc, int sbc, char * br, int sbr) to do the "pivot combine" operation to bit-strings b1 (original pivots) and b2 (new pivots) to produce bc (the combined pivots) and br (the riffle to be used).

uint64_t fColumnRifffleIdentity(char *bs, int sbs, char *rm, int srm, char *out, int sout) to do a column-riffle with the input matrix and the identity matrix. The set bits correspond to columns to be taken from the input matrix, and the unset bits to columns from the identity matrix. The number of rows of rm must be equal to the number of unset bits in the bit-string. This is used to make a null-space at the end of the Lübeck nullspace method.

void fFrobenius(char * m1, int s1, char * m2, int s2) to apply the Frobenius automorphism to the matrix m1 to produce m2.

int fFieldContract(char * m1, int s1, uint64_t fdef2, char * m2, int s2) to write the matrix m1 over the subfield fdef2 if possible. If the given field is not a subfield (the same field is allowed), or the function is not yet able to handle the case the function aborts. If the field is a subfield but the entries do not all lie in that subfield, 1 is returned and matrix m2 is not produced. If all goes well, zero is returned. The "standard basis" procedure can be used to choose a basis where this should succeed.

int fFieldExtend(char * m1, int s1, uint64_t fdef2, char * m2, int s2) to write the matrix m1 over the extension field fdef2. The function aborts if the given field is not an extension field (the same field is allowed), or the function is not yet able to handle the case - extending very large non-prime fields yet further may cause difficulty, as the current implementation first builds a look-up table of size equal to the order of the starting field in these cases.

void fExteriorSquare(char * m1, int s1, char * m2, int s2) to produce the exterior square of matrix m1 and write the result to matrix m2.

void fExteriorCube(char * m1, int s1, char * m2, int s2) to produce the exterior cube of matrix m1 and write the result to matrix m2.

void fSymmetricSquare(char * m1, int s1, char * m2, int s2) to produce the symmetric square of matrix m1 and write the result to matrix m2.

void fTensor(char * m1, int s1, char * m2, int s2, char * m3, int s3) to tensor the matrices m1 and m2 to produce the result in m3.

FELT fTrace(char * m1, int s1) to compute the trace of the matrix m1, and return the resulting field element.

void fProjectiveVector(char *m1, int s1, uint64_t pvec, char *m2, int s2) to select a single vector from the space spanned by m1, as selected by the integer in pvec, and write the single vector to the matrix m2. The single vectors chosen all span different 1-spaces. If pvec=0, the first row of m1 is chosen. The next q values of pvec select the second row plus x.first row for x=0,1,...(q-1) in that order. Then next q2 values select the third row plus x.second + y.first for (x,y) in lexicographic order and so on. If pvec >= (qdim-1)/(q-1) then the function aborts.

Section 4 – Functions awaiting re-packaging.

The functions on this list exist as programs, and all that is needed to produce them is to convert the programs into subroutines, write a tiny program to call the new function and to test the result.

uint64_t fech(char * tmp, char *m1, int s1, char *br, int sr, char *bc, int sc,
        char *m4, int s4, char *m5, int s5, char *m6, int s6) to do a full echelon form operation on matrix m1. br is the row-select bit-string, bc is the column-select bit-string, etc. The rank is returned. This function is currently not needed by anything - it is probably only a low-level function, and although it may be needed in the distant future for distributed working, I doubt it somehow. My guess is that this will never be needed.

Section 5 – Functions awaiting specification.

Some of the following require thought as to what the function prototype should actually be and what the routine does, exactly. Others I just haven't got round to thinking about yet. They all have code to execute something relevant, however.

field extend (bloat)
row extract
subtract scalar