Meataxe-64
Pcrit.
Richard Parker 9.12.2017

Section 1 – Introduction

The pcrit routines of meataxe64 are a collection of functions which are worth implementing in assembler for performance reasons.

The routines are implemented for x86-64 only, and meataxe64 classifies such computers into broad classes labelled with the letters a-j, where a is the oldest and j represents a computer with AVX-2, and several routines have been implemented several times so that they run faster on more modern machines.

It is expected that higher level software calls the mactype routine, and that the remaining routines are only called if the "class" of the machine is appropriate.

Section 2 – Machine Type.

The function mactype is used to determine the class of the machine, along with an indication of the size of the "intermediate" cache. Further bytes are not used, and set to the character '0' for future use.

void mactype(char mact[8]) to populate the 8 characters of the provided mact array with details of the machine that the software is currently running on. The idea of this routine is to answer, as simply as possible, the questions that the meataxe64 application needs answers to - basically which routines to call, and how big to make things so they are suitable for cache. By far the most important is the first byte - the class.

mact[0] - the class. The first byte is the "class", as described below, aimed at the choice of routines to call. In principle it could be advantageous to write a separate routine for each class, but in practice, for a particular job, many classes are equivalent as new instructions available are not useful. Hence, for example, the mod-2 HPMI routine exists for "legacy" SSE (class 'a'), VEX-encoded SSE (class 'g'), AVX-2 (class 'j') and probably soon AVX-512.

Class 'a'. This must work on every x86-64 computer there ever was, though whether the "c" compiler and the libraries will is another matter. None of Intel's earlier notebook CPUs (Core Duo, Pentium M, Celeron M, Mobile Pentium 4) implement Intel 64, so they do not have a class at all, but very early chips did not implement the LAHF/SAHF and CMPXCHG16 instructions, and SSE3 also came later. Most processors from 2003 - 2004 and many in 2005 will need this class.

Class 'b'. The use of CMPXCHG16 and LAHF/SAHF is allowed, as are all the SSE3 extensions. Needs the following three flags (else class is 'a')
lahf_lm (LAHF in long mode) 8000001 ecx bit 0 value 1
cx16 (CMPXCHG16) %ecx bit 13 value 0x2000
pni (SSE3 - Prescott new instructions) %ecx bit 0 value 1.
Hence the programmer of a class 'b' machine may additionally use the following instructions.
LAHF, SAHF, CMPXCHG16, FISTTP LDDQU ADDSUB HADDPS MOVDDUP
MOVDDUP is a double-precision broadcast, so will be needed for the HPMI if it uses double-precision.

Class 'c'. The additional use of the SSSE3 instructions are allowed.
ssse3 (SSSE3 extensions) %ecx bit 9 value 0x200
Again, all fairly specialized instructions. The extra instructions available are . . .
PSHUFB PALIGNR PHADD/SUB PMULHRSW PMADDUBSW PABS PSIGN
I believe the VIA Nano 2000 is in this class.
AMD chips 2007-2009 seem to be in this class.
AMD low-power Bobcat is in this class.

Class 'd'. The additional use of the SSE4.1 instructions are allowed.
sse41 (SSE4.1 extensions) %ecx bit 19 value 0x80000.
This is a large set of important instructions, including the PMULDQ used in the reduction of 10-bit fields (primes 17-61) in the AS HPMI. It is the class
MOVNTDQA PACKUSDW PMOV(S/Z)X PBLENDVB PBLENDW PCMPEQQ
PINSRB/D/Q PMULLD PMULDQ PMIN/PMAX(S/U)(B/W/D)
PHMINPOSUW MPSADBW PTEST
I believe the VIA Nano 3000 and Intel Nehalem is in this class.

Class 'e'. The additional use of the SSE4.2 instructions are allowed.
sse42(SSE4.2 extensions) %ecx bit 20 value 0x100000
popcnt (POPCNT) %ecx bit 23 value 0x800000
The extra instructions available are . . .
POPCNT CRC32 PCMPGTQ PCMPESTRI etc. (Intel Manual Section 4.1)
I believe the Intel Westemere is in this class.

Class 'f'. This class allows the use fo the CLMUL instruction.
clmul (PCLMULQDQ) %ecx bit 1 value 2
The extra instruction available is just PCLMULQDQ.
This class is needed for the routines for large fields of characteristic 2.
It appears that the new low-end Intel pentium/celeron chips are in this class.

Class 'g'. This class allows the additional use of AVX instruction set, and ideally all routines using the SSE vector registers should be rewritten for this class, as it allows the VEX-encoded 128-bit instructions (rather than the "legacy" ones), as well as the three-operand versions (avoiding the occasional copying). Also allows the use of the 256-bit registers for floating point use (only).
avx (AVX-1) %ecx bit 28 value 0x10000000
The AMD Bulldozer is in this class.
The Intel Sandy/Ivy Bridge are in this class.

Class 'h'. Previously called PILedriver. The BMI1 instructions are new in this class. This is the class of lovelace and babbage.
ANDN BEXTR BLS(I/MSK/R) TZCNT
bmi1 (BMI1) 07 %ebx bit 3 value 8
The AMD Piledriver and Steamroller are in this class
The AMD low-power Jaguar is in this class.

Class 'i'. The BMI2 instructions are new in this class.
BZHI MULX PEXT/DEP RORX SARX SHRX SHLX
bmi2 (BMI2) 07 %ebx bit 8 value 0x100
I believe the AMD Excavator is in this class.

Class 'j'. Previously called HASwell. This class includes the AVX-2 instruction set, allowing the use of 256-bit registers for integer use.
avx2 (AVX-2) 07 %ebx bit 5 value 0x20
movbe (MOVBE) %ecx bit 22 value 0x400000
There may be some Intel Haswell, Broadwell and Skylake in this class as may be AMD Ryzen. Don't know which are 'j' and which 'k'.

Class 'k'. Not yet implemented. Includes the use of Fused Multiply-Add, doubling the speed of floating point matrix multiplication..
Need to find out which bits to test. fma

Further classes are expected in future to control the use of AVX-512 etc..

mact[1] - the seccache - secondary cache indicator.

This field is used only to decide the "recbox" parameter - the number of rows of matrix C that should be deal with at once.

It takes one of three values, and is used to guide the use of second-level cache.

seccache '0'. This indicates that the use of 128K (per thread) of second level cache is OK.
seccache '1'. This indicates that the use of 256K (per thread) of second level cache is OK.
seccache '2'. This indicates that the use of 512K (per thread) of second level cache is OK.

Section 3 – Non-HPMI routines.

These routines are of general purpose applicability, but designed primarily for use from the "field" module. They exist to speed up those areas of the field module that warrant it, as assembler implementation is usually faster than in "c".

void pcaxor(Dfmt * d, const Dfmt * s1, const Dfmt * s2, int nob). Class 'a'.
void pcjxor(Dfmt * d, const Dfmt * s1, const Dfmt * s2, int nob). Class 'j'.
This routine performs an 'exclusive or' of a string of bytes (described as Dfmt which is a unint8_t) d = s1 ^ s2 of length 'nob' bytes. The implementations use vectorization where possible (SSE for a, AVX-2 for j) and are tuned for cases where nob is fairly large but not divisible by a large power of two, and the areas are not assumed to be aligned in any way. These routines are used in the FIELD routines DAdd and DSub in characteristic 2, and indirectly from DSMad if the scalar is 1. They are also used for populating the brick (making the grease table) in the HPMI mod 2, for which they are not perfectly designed but adequate. They are not used for the real heart of the HPMI in characteristic 2, for which pcab2/pcjb2 are appropriate.

void pcunf(Dfmt * d, uint64_t nob, uint8_t * t1) Class 'a'.
This routine takes each byte of the string d, looks it up in the table t1, and replaces the input byte by the result. The implementation works 1 byte at a time at the moment . . . some inprovement would be possible by fetching and storing the results in larger chunks. It is only used for DSMul at the moment, though the routine may have more general applicability.

void pcxunf(Dfmt * d, Dfmt * s, uint64_t nob, uint8_t * t1) Class 'a'.
This routine takes each byte of the string s, looks it up in the table t1, XORs the result into the corresponding byte of the string d, and replaces that byte into the string d. The length of the strings is given by the 'nob' parameter. The implementation works at 8 byte length for as much of the string can be processed that way, and then does the bytes singly. The routine is only used in the DSMad routine of the field module in fields {4,8,16,32,64,128,256} when the scalar is neither 0 nor 1.

void pcbif(Dfmt * d, Dfmt * s1, Dfmt * s2, uint64_t nob, uint8_t * t2) Class 'a'.
This routine takes the two bytes, one from s1 and one from s2, looks up 256*s1+s2 in the table t2 and puts the result in the string d. All three strings are nob bytes long. The implementation works four bytes at a time except for the last 0-3, which are done singly. The routine is used heavily to add in Dfmt in fields of odd characteristic 3-251.

void pcbunf(Dfmt * d, Dfmt * s, uint64_t nob, uint8_t * t1, uint8_t * t2) Class 'a'.
This takes pairs of bytes, one from s and one from d, with 'nob' pairs of bytes processed. Firstly the s byte is looked up in the table t1, and then the result and the byte from d looked up in the table t2. It is the result of the first table look-up that is shifted 8 places, though in all the applications so far the table t2 is anyway commutative. The implementation unrolls the loop 8 times. It is used in the DSMad routine for fields of odd characteristic when the multiplier is neither 1 nor -1.

void pccl32 (const uint64_t * clpm, uint64_t scalar, uint64_t noc,
        uint32_t * d1, uint32_t * d2) Class 'g'
void pccl64 (const uint64_t * clpm, uint64_t scalar, uint64_t noc,
        uint64_t * d1, uint64_t * d2) Class 'g'
These routines do a DSMad of noc words for characteristic 2 fields of order 217 - 263 using the "carryless multiplication" instruction as available if the class of the machine is at least 'g'. It takes words (either 32 or 64 bits, depending on which routine is being discussed).

Section 4 – pcmex.

This routine is used to extract multiple entries from a vector and combine them into a single uint64_t.

uint64_t pcmex(uint32_t mex, Dfmt * a)

The first word of mex is used as a major steering word to choose between a fairly large number of cases which are probably only of major interest when studying its partner routine MakeMex, as it is the combination of both routines that are usually used to perform entry extraction from Dfmt input.

The first batch of cases have mex[0] = {0,1,2,3}. mex[1]=q (the multiplier) mex[2,3,4,5] are ix0,ix1,ix2,ix3 and the return is
mex[0]=0 return a[ix0]
mex[0]=1 return q.a[ix0]+a[ix1]
mex[0]=2 return q2.a[ix0]+q.a[ix1]+a[ix2]
mex[0]=3 return q3.a[ix0]+q2.a[ix1]+q.a[ix2]+a[ix3]
Notice that mex[1] must be present but is not used if mex[0]=0 - i.e. ix0 is still in mex[2].

Section 5 – HPMI routines.

Characteristic 2.

There are two routines involved in the HPMI in characteristic 2, both performing the same function but using different technology.

void pcab2(uint8_t *a, uint8_t * bv, uint8_t *c) Class 'a'.
void pcjb2(uint8_t *a, uint8_t * bv, uint8_t *c) Class 'j'
This is the main BrickMad routine for characteristic 2, taking an Afmt string in 5-byte blocks (skip/termnate then eight nybbles), a populated brick work area of 8 x 16 128-byte rows, and a chunk of Cmft consisting also fo 128-byte rows to add the answers into. It is not expected that this routine be called outside the HPMI. The 'a' version uses legacy SSE to perform the XOR operations, whereas the 'j' version uses AVX-2. The Afmt is accessed, for speed, as 8-byte (uint64_t) values even though only five bytes are used and, if the first byte is the terminate byte, the other seven bytes may be scratch. It is therefore necessary that the Afmt allocation is at least seven bytes larger than is needed to hold the actual Afmt data.

------------------------Routines still to be documented. -----------------------------------

extern void hpmiset(FIELD * f);
extern uint64_t pcstride(uint64_t s);
extern uint64_t pcpmad(uint64_t p,uint64_t a,uint64_t b,uint64_t c);
void pcad3(const uint8_t *a, const uint8_t *b, uint8_t * c);
void pcab3(const uint8_t *a, uint8_t * bv, uint8_t *c);
void pcjb3(const uint8_t *a, uint8_t * bv, uint8_t *c);
void pcaas(const uint8_t *a, uint8_t * bv, uint8_t *c,
        const uint64_t * parms);
void pcdas(const uint8_t *a, uint8_t * bv, uint8_t *c,
        const uint64_t * parms);
void pcjas(const uint8_t *a, uint8_t * bv, uint8_t *c,
        const uint64_t * parms);
void pcjat(const uint8_t *a, uint8_t * bv, uint8_t *c,
        const uint64_t * parms);
void pcdasc(const uint8_t *prog, uint8_t * bv, const uint64_t * parms);

=================== End of editing =============================

The rest of this document is out-of-date junk.

Section 2 – AS primes routines.

There are two routines specifically produced to service the primes that are done in the HPMI using AS-type codes - pcchain and pcbmas. The pcchain routine is designed to compute addition chains as a subroutine to BGrease, and is designed for considerably more general cases than pcbmas, which is probably limited to primes less than 181.

Both routines take an array, normally living in the FIELD structure, containing a collection of necessary uint64_t values, and a pointer to this array (called parms) is passed to both of them. The elements of the parms array are . . .

parms[0]	The characteristic of the field - equal to f->charc.
parms[1]	A shift value S. This is used in both routines, and in different ways.
The more stringent requrement comes from pcbmas, where it must be the
shift needed to convert the masked value into the units position. In the
case of pcchain, it needs to be a shift within the bit-length of the values,
and such that 2S > characteristic.
parms[2]	The mask used in pcbmas. This must have all the bits set within the bit-
length of the values from 2S upwards. For pcchain, all that is needed is
that the 2S bit is set, and all lower bits unset.
parms[3]	2S − p. This is used only in pcchain, and is added to a value so that the
2S bit is set if and only if the value was p or greater.
parms[4]	cfmtcauld - the number of bytes in a cauldron in Cfmt. At present this
value must be 128 for both routines.
parms[5]	Slots - the number of code words for each slice. This value may be
larger than the actual number of code words - it is used to determine
where the next slice starts.
parms[6]	Slices. At present this is not used by pcbmas as it is assumed to be 7.
It should be set to 7 for future compatibility. It is used in pcchain and
must be correctly set for that routine.
parms[7]	2S % p. This is the multiplier, used only in pcbmas, to convert the
shifted masked bits into the number to add on to the lower bits.
parms[8]	Bias. This is the

void pcchain(uint8_t * prog, uint8_t bwa, uint64_t * parms) to compute the addition chain as specified in the program prog. Many of the details needed are in the parms routine, which is constant for any given field (as is the prog, as a rule!).

The central idea is to interpret the string of bytes (in prog) as a set of instructions to compute the chain by adding two already computed multiples and then reducing modulo the prime.

The byte-code.
At the start of interpreting a byte, the following state is held.
The accumulator - a cauldron, held in vector registers.
The destination slot.

At the start, the accumulator is loaded with slot number 1 (which is always seeded by BSeed) and the destination slot set to 2.

The interpretation of the prog bytes is given below.

0-79 add the slot of that number into the accumulator, store the result in the destination slot, and increment the destination slot. For star chains, or for parts of the computation that can be done by a star chain, these (and stop!) are the only codes needed, and they are expected to form the commonest instructions by some margin.
80-159 load the accumulator from the slot number 80 less than the byte-code.
160-239 set the destination slot to be 160 less than the byte code
240-254 Unused and reserved for future use.
255 stop - the program has completed.

As an example, take P=71
Slot	0 1 2 3 4 5 6 7 8 9 4 7
AS-code	0 1 2 3 [4] 8 12 [14] 24 25 39 53
byte-code	1 1 1 4 4 2 86 6 1 164 7 167 7 255

Reduction (of a number known to be less than 2p) is done by the following method. Bear in mind that all these operations are done to 64-bit chunks that may well contain more than one entry each.

Firstly a number 2S−p (provided in the parameters) is added, where S is chosen so that 2S > p. The result has the 2S bit set if and only if the result was p or larger.
Secondly a logical 'and' is done with 2S to keep this bit only. higher bits may be set in the mask, as they will not be set in the value after 2S−p has been added.
This bit (1 if reduction required, 0 if not) is then shifted into the units position (the original is retained as well.
The the shifted bit is subtracted from the unshifted bit to make a number that is either all 1 (if subtraction of p is wanted) or all zero otherwise.
A logical AND is then done between p and this result. This is then p if subtraction is required and 0 otherwise.
All that remains is to subtract this value from the original one.

void pcbmas(uint8_t *a, uint8_t * bv, uint8_t *c, uint64_t * parms)
Parameter a is the Afmt, which is a string of bytes treated as a string of uint64_t internally to pcbmas. Parameter bv is the brick work area, and parameter c is the Cfmt area to be added into. parms is as described above, containing the information, constant for the field, needed to perform the operation.

Section 3 – Characteristic 2 DSMad assistance.

void pccl32 ( uint64_t * clpm, uint64_t scalar, uint64_t noc,
        uint32_t * d1, uint32_t * d2)

does a multiply-and-add of the vector at d1 by scalar into the vector at d2, noc values long. The scalar is left-justified, so that the X^(d-1) term is the most significant bit.

The parameters must be

clpm[0] e = X2d / p left-justified, with X^d (not d-1) the most significant bit.
clpm[1] p (including Xd term) left justified - X^d (not d-1) the most significant bit.
clpm[2] shift = 64 - degree

------ end of editing - - - - all the rest is unchecked and probably useless -----

Section 2 – Specifications of pcrit routines.

uint64_t pcpmad ( uint64_t p , uint64_t a , uint64_t b uint64_t c) to multiply a by b, add c, and reduce mod p. This uses the 128 / 64 division routine to reduce modulo p, and needs no preparation. It is used for the largest primes that meataxe64 is designed for, and can take around 70 clock cycles (20 nSec) in these cases. To multiply-and-subtract, just give p-c instead of c, which works in all cases.

extern uint64_t pcpmul(uint64_t p,uint64_t a,uint64_t b);
extern void pcxor(Dfmt * d, const Dfmt * s1, const Dfmt * s2, int nob);
extern void pcbif(Dfmt * d, const Dfmt * s1, const Dfmt * s2,
        uint64_t nob, const uint8 * t);
extern void pchset(HPMI * hp, const FIELD * f);
extern uint64 pcinfocauld(uint64 fdef);
void pcbm2(const uint8 *a, uint8 * bv, uint8 *c);
void pcad3(const uint8 *a, const uint8 *b, uint8 * c);
void pcbm3(const uint8 *a, uint8 * bv, uint8 *c);

// void pcb64p(uint64_t q,uint64_t * dd);
// uint64_t pcb64(uint64_t a, uint64_t m);
// void pcb128p(uint64_t q,uint64_t * dd);
// uint64_t pcb128(uint64_t a,uint64_t m1,uint64_t m2);
//

void pcxor(Dfmt * d, const Dfmt * s1, const Dfmt * s2, int nob) to perform an exclusive-or of a string of data d = s1 ^ s2 of length 'nob' bytes. The implementation uses vectorization where possible, and is tuned for cases where nob is fairly large but not divisible by a large power of two, and the areas are not assumed to be aligned in any way - MOVDQU is the key instruction used in pcrit1. pcxor is used from the FIELD routines DAdd and DSub, and indirectly from DSMad, but will not be part of the main performance-critical multiply routine in characteristic 2, which will use further routines that are not yet specified.

void pcbif(Dfmt * d,const Dfmt * s1,const Dfmt * s2, int nob,const uint8 * t,int m) to apply the binary function t to the bytes of s1 and s2, and put the resulting looked-up byte into d, with nob bytes being processed. If a1 is the byte fetched from an s1 location, and a2 comes from s2, the byte placed in d is t[a1*m+a2]. So far I have seen no way to use vectorization, and the performance of this, although the best I can manage, is not that great. It is used primarily for adding and subtracting in odd characteristics where there is more than one entry in each byte.

extern void pchal(int * gen, int * subgen);
extern void hpmiset(FIELD * f);
extern uint64_t pcstride(uint64_t s);
extern uint64_t pcpmad(uint64_t p,uint64_t a,uint64_t b,uint64_t c);
extern void pcxor(Dfmt * d, const Dfmt * s1, const Dfmt * s2, uint64_t nob);
extern void pcbif(Dfmt * d, const Dfmt * s1, const Dfmt * s2,
        uint64_t nob, const uint8_t * t2);
extern void pcbunf(Dfmt * d, const Dfmt * s, uint64_t nob,
        const uint8_t * t1, const uint8_t * t2);
extern void pcxunf(Dfmt * d, const Dfmt * s, uint64_t nob,
        const uint8_t * t1);
extern void pcunf(Dfmt * d, uint64_t nob, const uint8_t * t1);

void pcbm2(const uint8_t *a, uint8_t * bv, uint8_t *c);
void pcad3(const uint8_t *a, const uint8_t *b, uint8_t * c);
void pcbm3(const uint8_t *a, uint8_t * bv, uint8_t *c);