Meataxe-64
Recursive Echelize.
Richard Parker 23.12.2017

Section 1 – Introduction.

This document is a third stab at the design for the recursive echelize. This design is based around the idea of a four-phase echelization, where the first phase produces the column select, the row select, the rank and the determinant, after deciding between three strategies - just doing it in Dfmt, chopping horizontally or chopping vertically, and in the latter two cases, also deciding how to chop. The next two phases produce the remnant and the cleaner, and may be done in either order. The last phase produces the multiplier, and relies on all the previous phases being done.

At the lowest level, when the matrix is small enough (perhaps around 100 x 100) the whole job is done in Dfmt. The main idea here is to process rows in turn by clearing all previous pivots and then looking for a pivot in the row (the selects are both standard) until a "batch" can be collected, after which the rest of the matrix is cleared with the pivots of the batch. This enables a modicum of grease to be used, and is also a bit more cache-friendly. It is hoped that this lowest level can be tuned so that it is appropriate for larger sizes also, but this will depend on experimentation once the system is complete and working. The transformation matrix is processed at the same time (with columns added as new rows containing pivots are discovered) so that the cleaner is in fact available at the end of the first phase. Similarly the back-cleaning does also the multiplier, so that in Dfmt there are only two phases that actually do any work.

The horizontal chopping is very similar to the five-author paper, and should not be too hard to produce.

The vertical chopping version is essentially the transpose of the horizontal chop, but requires a couple of new primitives - notably column riffle.

Section 4 – Vertical chop strategy.

When the matrix has a lot more columns than it has rows, it becomes sensible to chop off the first columns (probably a few more columns than there are rows) in the hopes that the echelization will result in a matrix (M) which can be used to multiply the remaining columns using the HPMI. This requires the combination (UNH) of rows from the two halves in general, which implies a column riffle on the transformation matrix.

1. CHV. Chop vertically. The input matrix C is chopped into two parts C1 and C2.

2. ECH. Perform a full echelization on C1, yielding rs1 cs1 R1 K1 M1.

At this stage we have . . .

M1 0 C1 = -1 R1
K1 1 0 0

3. REX. rs1 and C2, yielding S2 and N2.

so that C2 = S2
        N2

4. MUL. S2' = M1* S2.

5. MAD. Compute N2' = N2 + K1 * S2 to get the extensions of the zero rows.

At this stage we have . . .

M1 0 C1 C2 = -1 R1 S2'
K1 1 0 0 N2'

6. ECH. Perform a full echelization on N2' yielding rs2 cs2 R2 K2 M2.

M2 0 N2' = -1 R2
K2 1 0 0

The next few steps complete the echelization of the top half, consisting of C1 and C2, and putting things together as if we had echelized the matrix [C1 C2].

7. BSJ. Bit-string join. Concatenate cs1 and cs2 to get the combined cs.

8. UNH. This is applied to rs1 and rs2 to get rs and rf12.

The remnant needs a bit more work. At the moment our matrix is

-1 R1 - S2' -
 0 0 -1 R2

9. CEX. Using cs2 on S2' to give P2 and Q2.

-1 R1 P2 Q2
 0 0 -1 R2

10. MAD. Q2' = Q2 + P2 * R2

-1 R1 0 Q2'
 0 0 -1 R2

11. AUT. Assemble Upper Triangular.
Assemble the matrix R from the components. I believe this is simply a cut-n-paste operation with no riffles involved anywhere.

R = R1 Q2'
       0 R2

12. REX. Applying rs2 to K1 giving K1s and K1n.

1 0 0 M1 0 0 = M1 0 0
0 M2 0 K1s 1 0 M2K1s M2 0
0 K2 1 K1n 0 1 K1n+K2K1s K2 1

13. MUL. M4 = M2K1s

14. MAD. K4 = K1n + K2K1s.

So now our transformation matrix is

M1 0 0
M4 M2 0
K4 K2 1

15. ???. Need to think what riffles, if any, are needed to make

M = M1 0
        M4 M2

16. ???. And similarly we need to combine the K matrices

K = K4 K2.

===================================================================

Section 2 – Overall design.

echs * rech1(Dfmt * c, uint64_t nor, uint64_t noc)

  The previous idea of having several stages did not seem to work out well, since it gave inefficiencies when multiplying by matrices that were upper triangular, and also computing a remnant that had to be stashed away. Indeed it seems that it is quite hard to break things up without causing inefficiencies of several types, so I have abandoned the idea, aiming instead to start with everything using full echelize, looking to see what can be released early and what work can be postponed without any impact on efficiency. The old version of the document is stashed away in "obsolete" in case it turns out to be nearer the mark than it currently appears to be.

Instead I propose to do a chop in both directions as the recursive step, except that the bottom half is "chopped" by a column-select rather than a simple chop. To provide the early release, the top software level does things in a careful order, but calls a full echelize on the parts, with a view to looking at the sub-sections in due course to see if things can be released yet earlier. Nevertheless, the pressures for early release do not seem to warrant anything particularly stringent since the main critical path needs the multiplier - necessarily the last part to emerge.

The idea, then is to take the input matrix and chop first horizontally, and then chop the top half (only) vertically also, so that the matrix is of the form, with C3 stretching right across.

  C1 C2
  - C3 -

We first perform a full echelize on C1, then do the same row operations to C2 and echelize the non-selected rows. There is then new functionality to combine the pivots and matrices so that the effect is that the top half has been echelized. The pivots from C3 are then extracted and cleared and the rest echelized,from which the row and column selects for the top level are produced and released, so that the row and column extracts can get going.

The next thing released is the remnant. It is far from clear to me whether the cleaner or the remnant should be produced next, so I have gone for the remnant as it completes the work on the matrix, leaving only the transformation matrix outstanding.

The cleaner is produced next, and then some further work is needed to complete the multiplier - the last part to be released.

Hence the overall structure is of four parts, leaving whatever intermediate data structures may be necessary to do the rest with full efficiency, but doing things in such an order that the first part releases rs and cs, the second part releases R, the next releases K, and the last part produces M.

Section 2 – An attempt at the algorithm.

Issues.
Sort out the riffles.
Where is the determinant?
Work out all the routines needed - e.g. concatenate matrix right, bottom, bitstring . . .

1. Chop the input matrix C into top half C12 and bottom half C3, then chop C12 further into left and right halves, so that the result is (as previously stated)
C1 C2
- C3 -

2. ECH. Perform a full echelization on C1, yielding rs1 cs1 R1 K1 M1. It may be that some of this is not needed, but we'll look at that later.

At this stage we have . . .

M1 0 C1 = -1 R1
K1 1 0 0

3. REX rs1 and C2, yielding S2 and N2.

so that C2 = S2
        N2

4. MUL S2' = M1* S2.

5. MAD. Compute N2' = N2 + K1 * S2 to get the extensions of the zero rows.

At this stage we have . . .

M1 0 C1 C2 = -1 R1 S2'
K1 1 0 0 N2'

6. ECH. Perform a full echelization on N2' yielding rs2 cs2 R2 K2 M2. I doubt if we'll need K2, M2 for a while, but we're ignoring this aspect at the moment.

M2 0 N2' = -1 R2
K2 1 0 0

The next few steps complete the echelization of the top half, consisting of C1 and C2, and putting things together as if we had echelized the matrix [C1 C2].

7. BSJ. Bit-string join. Concatenate cs1 and cs2 to get the combined cs12.

8. UNH. This is applied to rs1 and rs2 to get rs12 and rf12.

The remnant needs a bit more work. At the moment our matrix is

-1 R1 - S2' -
 0 0 -1 R2

9. CEX using cs2 on S2' to give P2 and Q2.

-1 R1 P2 Q2
 0 0 -1 R2

10. MAD Q2' = Q2 + P2 * R2

-1 R1 0 Q2'
 0 0 -1 R2

11. AUT Assemble Upper Triangular.
Assemble the matrix R12 from the components. I believe this is simply a cut-n-paste operation with no riffles involved anywhere.

R12 = R1 Q2'
        0 R2

We now proceed to operate on C3.

12. CEX cs12 and C3 yielding S3 and N3.

13. MAD N3' = N3 + S3 * R12.

14. ECH N3' -> rs3 cs3 R3 K3 M3.

We are now in a position to release the rs and cs for the entire job.

15. rs is simply a concatenation of rs12 and rs3.

16. UNH is applied to cs12 and cs3 to give cs and rf123.

The next objective is to produce the remnant.

Our next objective is to compute the overall remnant R. At the moment we have

-1 - R12 -
 0 -1 R3

17. CEX applying cs3 to R12 giving S12 and N12.

18. MAD N12' = N12 + S12 * R3.

19. RRF using rf123 to combine N12' and R3 to give R.

We now turn to the transformation matrix. First objective is to make the cleaner K, but before getting on with that, we need to combine the work done on C1 and C2 to get M12 and K12.

20. REX applying rs2 to K1 giving K1s and K1n.

1 0 0 M1 0 0 = M1 0 0
0 M2 0 K1s 1 0 M2K1s M2 0
0 K2 1 K1n 0 1 K1n+K2K1s K2 1

21. MUL M4 = M2K1s

22. MAD K4 = K1n + K2K1s.

So now our transformation matrix is

M1 0 0
M4 M2 0
K4 K2 1

23. Need to think what riffles, if any, are needed to make

M12 = M1 0
        M4 M2

24. And similarly we need to combine the K matrices

K12 = K4 K2.

This completes the combinations of the parts from C1 and C2 making C12. We have achieved

M12 0 C12 = -1 R12
K12 1 0 0

Now we must return to consider the transformation matrix in its entirety.

1 0 0 M12 0 0 C12 C12 = 1 0 0 -1 R12 = -1 R12
 0 1 0 K12 1 0 C12 C12 0 1 0 0 0 0 0
S3 0 1 0 0 1 S3 N3 S3 0 1 S3 N3 0 N3'

So our transformation matrix is, so far . . .

25. MUL S3' = S3 * M12.

  M12 0 0 = M12 0 0
  K12 1 0 K12 1 0
S3M12 0 1 S3' 0 1

We then applied the row-select rs3 to N3', so we must apply it also to S3'

26. REX rs3 to S3' giving P3 (selected) and Q3 (non-selected).

After that we multiplied by

M3 0
K3 1

1 0 0 0 M12 0 0 0 = M12 0 0 0 = M12 0 0 0
0 1 0 0 K12 1 0 0 K12 1 0 0 K12 1 0 0
0 0 M3 0 P3 0 1 0 M3P3 0 M3 0 M3' 0 M3 0
0 0 K3 1 Q3 0 0 1 K3P3+Q3 0 K3 1 K3' 0 K3 1

27. MUL M3' = M3P3.

28. MAD K3' = Q3 + K3P3.

29. We are now in a position to assemble K from the components.

K = K12 0
       K3' K3

Finally we want to complete the transformation matrix

1 S12 M12 0 = M12 S12M3 = M12 M5
0 1 M3' M3 M3' M3 M3' M3

30. MUL. M5 = S12M3

31. Finally we need to combine the four Ms (M12 M5 M3' M3) into the output M.

Step	Job	Inputs	Outputs
1	CHH CHV	C	(C12) C1 C2 C3
2	ECH	C1	rs1 cs1 R1 K1 M1
3	REX	rs1 C2	S2 N2
4	MUL	M1 S2	S2'
5	MAD	K1 S2 N2	N2'
6	ECH	N2'	rs2 cs2 R2 K2 M2
7	BSJ	cs1 cs2	cs12
8	UNH	rs1 rs2	rs12 rf12
9	CEX	cs2 S2'	P2 Q2
10	MAD	P2 R2 Q2	Q2'
11	AUT	R1 Q2' R2	R12
12	CEX	cs12 C3	S3 N3
13	MAD	S3 R12 N3	N3'
14	ECH	N3'	rs3 cs3 R3 K3 M3
15	BSJ	rs12 rs3	rs
16	UNH	cs12 cs3	cs rf123
17	CEX	cs3 R12	S12 N12
18	MAD	S12 R3 N12	N12'
19	RRF	rf123 N12' R3	R
20	REX	rs2 K1	K1s K1n
21	MUL	M2 K1s	M4
22	MAD	K2 K1s K1n	K4
23
24
25
26
27
28
29
30
31

======================== Junk from here ==============================

cs 20 cs12 cs3.
rs 19 rs12 rs3
cs3 18 N3'
N3' 17 N3 S3 R12
S3 16 cs12 C3
cs12 6 cs1 cs2
cs1 2 C1
cs2 5 N2'
C1 1 Input C.
N2'
N3
R12
rs12
rs3

This document is an initial stab at the design of the recursive echelize function. The idea is to provide service for the larger-scale multi-core "mech" function (as well as other, cut-down versions), so one key requirement is early release. Hence the work of the recursive echelize is broken into four parts.

Stage	Needs	Job	Work	Inputs	Result	Other outputs
EC1	-	Forward clean	33%	C	cs, rs	A, B
EC2	EC1	Forward clean trafo	17%	A rs	K cleaner	L
EC3	EC1	Back clean	0%	B	Remnant	-
EC4	EC2	Back clean trafo	50%	B L	Multiplier	-

Here C is the input matrix, B is an upper-triangular matrix, L is a lower triangular matrix, and A forms a record of the operations done.

The first two issues are to build this functionality by chopping the matrix horizontally/vertically and using the various other utility functions. The remaining issue is to consider how to perform this functionality when the matrix is too small to chop, and how to decide which method is appropriate. First, however, we give a detailed description of the data packages.

Section 2 – Data Packages

C The input matrix. This is an nor x noc matrix. The first stage finds all the pivots without back-cleaning at which point the rank, cs and rs are known.
rs The row-select. This document assumes that standard rows must be selected. This is a bit-string with nor bits of which rank are set.
cs The column select. Again we assume here that these are standard. This is a bit-string with noc bits of which rank are set.
A The notebook of the row operations done to put the matrix into (non-reduced) echelon form. The nature and format of this data set is a major outstanding issue. In principle it consists of a nor x rank matrix, where the rows correspond to the input rows and the columns correspond to the selected rows (only). The selected rows of this virtual matrix A consists of the multiplier, as far as it has got. The non-selected rows consist of the cleaner. The conversion of the notebook A into a real matrix is the job of the EC2 procedure, which also separates the selected and non-selected rows to make the cleaner and the matrix L.
B This consists of a rank x noc matrix, being the selected rows after they have been put into (non-reduced) echelon form. For each row of B, the pivot is 1, and all the entries below it are zero. As this matrix is used twice (by EC3 to make the remnant and by EC4 to finish off the multiplier) it is possible that a pre-processing step be done to B to avoid duplication of work.
K - the "cleaner". This consists of a matrix with nor-rank rows (the non-selected ones) and rank columns, corresponding to the selected rows. It expresses how the non-selected rows were made from the selected ones.
L This is a rank x rank matrix, giving the row operations done to convert the selected rows into the (non-reduced) echelon form matrix B.
R The remnant. This gives the non-selected columns on the selected rows, completing the Negative Reduced Echelon Form. It has rank rows, corresponding to the selected rows, and noc-rank columns, corresponding to the non-selected columns.
M The multiplier. This is a rank x rank matrix specifying how the selected rows are put into NREF. The rows correspond to the selected columns, and the columns correspond to the selected rows.

Section 3 – Chop Vertically.

In this section we assume that the matrix C has been chopped vertically into C1 | C2 .

Program for EC1.
  1. EC11 on C1, producing rs1 cs1 A1 B1
  2. EC21 on A1 rs1 producing K1 and L1
  3. REX using rs1 on C2 producing S2 and N2
  4. MAD N2' = N2 + K1 * S2
  5. EC12 on N2' producing rs2 cs2 A2 B2
  6. cs = concat(cs1 , cs2)
  7. UNH(rs1 , rs2) -> rs, rf (notice that rf is not mentioned anywhere yet!)
  8. MUL B' = L1 * S2
  9. Concatenate matrices B = (B1 B') , (0 B2)
10. A is a list containing rs1 K1 L1 rs2 A2 as it stands at the moment. Perhaps we should run
       EC2 on rs2 A2 to make K2 L2 to make A a bit more uniform.

Section 4 – Chop Horizontally.

In this section we assume that the matrix C has been chopped horizontally, with C1 the upper block and C2 the lower one.

Program for EC1.
  1. EC11 on C1, producing rs1 cs1 A1 B1
  2. EC31 on B1 producing the remnant R1 (This work seems to be wasted)
  3. CEX using cs1 on C2, producing S2 and N2
  4. MAD N2' = N2 + S2 * R1
  5. EC12 on N2' producing rs2 cs2 A2 B2
  6. rs = concat(rs1 , rs2)
  7. UNH(cs1 , cs2) -> cs, rf (to be used somewhere)
  8. CRZ cs1 B2 to make B'
  9. Assemble matrix B from B1 , B'
10. A is a list containing rs1 A1 rs1 A2 as it stands at the moment. Again one is tempted to do a
       bit more processing on this, but this requires further investigation.

Section 5 – Preliminary Analysis.

13:30 Morgen Nachmittag.

Our main interest here is concurrency and babies. The above analysis has so far concentrated on the concurrency, aiming at early release. We must now look more closely at the babies aspect, and in particular to try to make the multiplications as large as possible.

Vertical Chop. This has a multiply at program steps 4 and 8.

Step 4. This one is already flat and dense, consisting of the cleaner K1 being multiplied by the selected rows S2 and added into the non-selected ones N2.

Step 8. This requires attention. It is doing the linear operations on the rest of the pivotal rows from C1 to complete the upper-triangulation of the matrix B. The left-hand multiplier is upper triangular, so that economy here will be important. There is a compromise between not multiplying by zeros and having babies for the multiplication.

Horizontal Chop. This has just a multiply at program step 4 (have I missed something?) and is again flat and dense in general.

One idea is that matrix B always consists of the identity plus a rectangular matrix above the diagonal, so that the multiplication in step 8 of vertical is economical. The pressures for early release do not seem to warrant any sort of inefficiency, so there is no obvious reason to avoid this. This requires us to do some more work at step 9 in both recursive versions, and requires further investigation.

==================Even more junk from here onwards ================

EC1. The first step is to call EC1 on C1, producing cs1, rs1, A1, B1. We are going to need the cleaner too, so we run EC2 on A1 to get K1 and L1. We then apply rs1 to C2 to get Xs and Xu. We then multiply K1 by Xs and add to Xu giving Xv. Finally we apply EC1 to Xv, giving A2, B2, and also cs2, rs2. The output cs is simply the concatenation of cs1 and cs2. The output rs is the UNH of rs1 and rs2, and presumably the riffle rf will be needed at some point in the future.

n for, and noticing that the echelize proggy does not release its bit-strings early as it should, and with the imminent rewrite of slab echelize, it has become clear that a full review of the implementation of Gaussian is overdue.

Firstly, here are the user-level functions that I propose to service :-

- Find the rank of a matrix
- Put a matrix into row-echelon form.
- Invert a matrix
- Find the standard independent rows of a matrix
- Find the determinant of a matrix

At the bottom level, the Gaussian routine may need to produce some or all of the following . . .

- A column select bit-string specifying the chosen pivotal columns. This may or may not be required to be the standard pivots - choosing the first column as a pivot all the time.
- A row-select bit-string specifying the chosen set of linearly independent rows. Again these may or may not need to be standard.
- The remnant - the non-pivotal columns on the final echelon form
- The multiplier - a square matrix multiplying the selected rows to put the matrix into echelon form.
- The cleaner - what multiples of the selected rows must be added to the non-selected rows to make them zero. This may be needed in terms of the selected rows before or after multiplication by the multiplier, though the latter is a simple column-extract on the original matrix.
- The rank of the matrix.
- The determinant of the matrix.

Since we wish to utilize the methods of "chopped-up Gaussian" in the larger cases, we need to understand in detail what the requirements of the top-level are, and how that propagates downwards to determine the requirements on the lower levels, and onwards.

Section 2 – Top-level requirements.

The list of the top level requirements is given in the introduction . . . here I consider this list in greater detail.

Rank. Here the output is a single integer, and it is far from clear, in principle, that the methods of Gaussian elimination are needed at all. One can imagine some magical-wand based methods that come up with the rank in some completely different way, and although Gaussian methods may well, in practice, always be involved, it is perhaps appropriate that the interfaces to not assume this.

Determinant. Again, the output is a single integer and the use of Gaussian may well be just one of several methods available, though at present I can't think of any others. In any case, the input matrix will usually be square - a feature that is not shared by some of the other top level requirements. Lower down we may need to specify what determinant we are talking about when the input is rectangular, as there should be no requirement that we chop our matrix up into square pieces, and even if we do, there is no guarantee that any of the pieces will have full rank.

Echelon Form. The output from this consists of a column select and a remnant. It is, I think, an important observation that no row-select is produced by this - perhaps the most important of the functions. Whether the column-select is required to be standard is an interesting question - so far I know of no use-case that requires it, and no implementation that does not produce it, so the question is currently up-in-the-air with no obvious pressures in either direction.

Invert. Here the input is again square, and a transformation matrix is required. Since only non-singular matrices have inverses, there is no need for a rank, row-select, column-select, cleaner or remnant output - only the multiplier and possibly the determinant are useful.

Standard rows. This function is needed by the standard-basis procedure. In many cases it is probably sensible to compute the row-echelon form at the same time as computing the standard row select, but perhaps we should consider whether there is a place for knowing the standard rows without an echelon form.

This all leads us to wonder whether we can dream up algorithms that compute some of these things in ways that we have not yet considered. For example, rip-off methods may enable us to check that rows are linearly independent without considering the entire row very often, leading us to wonder whether it may be useful sometimes to compute standard rows without computing the echelon form.

Section 3 – Concurrency issues.

For a square, random NxN matrix over a large enough field, there are a total of N3 elementary operations to do to perform a full echelize, and we can use this measure to quantify the work of the various stages.
The first stage is to "clean down". In some order, the obvious algorithm finds a pivot in each row and adds a suitable multiple of that row to all later rows on those columns not yet treated. This does (N-i)(N-i) units of work for each row, or N3/3 - 33%. This stage already finds out the pivotal columns and rows, so can output cs and rs. The other two outputs are notes (A1) of the row operations done, and the resulting matrix B which is, in some sense, upper-triangular.
Another stage, which does not necessarily need to be done at the same time, or next, or indeed at all, but I will still call it the second stage, is to mimic the same row operations on the identity matrix. This involves i(N-i) operations, or N3/6 - 17%. It inputs the notes A1 of the row operations done and does them to an identity matrix resulting (abstractly) in a lower-triangular matrix which is, however, held in two parts - the selected and non-selected rows being held separately as the partially complete multiplier M1 and the completed cleaner, which can be output at the end of this stage.
The third stage is to back-clean the original matrix. This produces a lot of column-extracted data A2, but does a minimal amount of work since the matrix operated on is only the remnant which has (in some sense) zero columns. This work is therefore estimated as 0% in the simplification adopted here, so that there is a pressure to do this stage earlier as it produces further output with no further work.
The fourth and final stage is to apply the column-extract data to the transformation matrix, and this involves N(N-i) units of work for the i'th row, or N2/2 = 50%. . . the largest chunk.

Stage	Job	Work	Inputs	Result	Other outputs
1	Forward clean	33%	C	cs, rs	A1, B
2	Forward clean trafo	17%	A1	Kleaner	M1
3	Back clean	0%	B	Remnant	A2
4	Back clean trafo	50%	A2 M1	Multiplier	-

The nature and format of the input matrix C and result objects cs, rs, K, R, M are already clear. The nature and formats of the "Other outputs" is not so clear, and one major purpose of this document is to consider and determine what these formats are. We already have two implementations, namely chopped-up Gaussian and slab echelize (simplistic though it currently is) to look at to give us guidance on these topics.

Before we go any further, however, it is pertinent to consider what happens in other circumstances. The N3 value used above is an oversimplification if the matrix is rectangular and/or has surprisingly low rank. Perhaps we should fill in some details, and consider the matrix to be A x C of rank R to see what the "Work" column is in greater generality.
Firstly the forward clean. We are only going to find R rows to clean with, so the work is the sum, over i from 1 to R, of C-i.A-i, or CA-iA-iC+i2 which comes to

Work = RCA - R2(A+C)/2 + R3/3.

Case 1. A small, R=A. Work is A2C/2, but we can get the rs and cs and A1 (well-conditioned) in A3/2 by using rip-off methods. It is only B that requires A2C/2 steps.
Case 2. C small, R=C. Work is C2A/2, but we can get the rs, cs and B (well-conditioned) in C3/2 by terminating when we have found a pivot in every column. In this case we wish the cleaner were in terms of the adjusted rows (not the original ones) as there is then no further work to do.
Case 3. A=C but R small. Work is RC2 but we get the rs, cs and B in R2C except that we have not proved that there are no further pivots to be found, and we need RC2 of work to be sure of any of them.

Conclusion.

Algorithm 1. For normal (balanced) use. Do standard methods until it is clear that no further pivots will be found, either because all columns already have a pivot, or because all the rows have been processed. At the end, rs, cs and B are output, and there may be some rows, ideally untouched, that remain to be cleaned by column-extract and multiply-and-add methods, and some rows that are partially or fully cleaned. TBD needs further investigation.

Algorithm 2. For use when there are few rows and a lot of columns. Select a (random?, initial subset?) set of "special" columns and do Gaussian on these columns only. If this results in a pivot in every row, we can output the rs, cs and A1, and all that remains is to multiply the remaining columns by A1 to obtain the matrix B. If this does not result in a pivot on every row, we need to take more columns, and TBD again, further investigation is needed.

In both cases, the algorithm seems to fall into separate parts, with some parts releasing certain outputs early.

Section 4 – The Mimic data A1.

In the current, simplistic implementation of slab echelize, the mimic data is utilized as it is produced and only a single local variable (called "fel" - a field element in slab.c) holds the passing A1, being used immediately to update the transformation matrix. Here is its use.

    DSMad(&dsk,fel,1,vk,k+j*dsk.nob);

We see that the "fel" multiple of vector vk is being added into the j'th row of matrix K.

In the mezzanine "mech" there is a whole great data structure for A1, called an STA structure in the program . . .

    MOJ A; // pivotal matrix to clean with old B
    MOJ M; // matrix to multiply new rows by
    MOJ K; // cleaner to take new rows out of remaining ones
    MOJ rs; // row-select bitstring for new pivotal rows
    MOJ E; // clean old B with new rows
    MOJ rf; // riffle to put new rows into B

It is used to update the row of the transformation matrix, which (in mech) is made significantly more complex to save the space and work of dealing with matrices (or indeed parts of matrices) known to be zero or known to be the identity matrix. We may need to get involved with these complexities later, but for now it seems best to give the "update row" procedure, which applies it to the original matrix, held more simply, thereby illustrating more clearly what is going on.

void UR(int pri, MOJ fmoj, STA * A, MOJ * B, MOJ * C)

    MAD(pri, fmoj, A->A, *B, *C, Z);
    REX(pri, fmoj, A->rs, Z, V, W);
    MUL(pri, fmoj, A->M, V, X);
    MAD(pri, fmoj, A->E, X, *B, S);
    RRF(pri, fmoj, A->rf, S, X, *B);
    MAD(pri, fmoj, A->K, V, W, *C);

Section 5 – The first part of the echelize procedure.

It seems that there are several distinct ways of approaching the start (forward cleaning) of echelization. For example we could use rip-off methods or auto-grease - but this section considers only the simple, direct approach.

The input is a matrix with, say, A rows and C columns. Assuming that we wish to cater for the job only partially done (not at all clear at this stage) what would the output be?

There would be several types of rows.

1. Rows that have not yet been touched.
2. Rows in which all pivots (type 3.) have been cleared.
3. Rows in which a pivot has been selected.
4. Rows in which no pivot is available - the row is now zero.

We would need to know which columns were selected as the pivots for the rows in type 3, and for type 2, which linear combination of the type 3 rows was used.

For this algorithm, we can probably insist that the rows of type 1 are specified as being the trailing list (i.e. we process the rows in order).

One idea is just to keep a lab notebook. Next row cleaned (linear combinations given) and either found to be zero or a pivot selected. It then becomes an interesting question as to whether we are allowed to add rows into other rows arbitrarily . . .

Let's look at the lab notebook idea a bit. What sorts of entries might we need?

MAD ( λ , i , j) C(i) += λ.C(j)
MUL ( λ , i ) C(i) *= λ
PIV( i , k ) The pivot in C(i) was selected to be column k
ZER( i ) The row C(i) was inspected and found to be zero

The vast majority of the entries in the notebook will be of the first (MAD) kind, and it probably makes some sense to compress this data a bit somehow.

The idea then would be that the production of the transformation matrix would take the notebook as input. This leads us to wonder what rules would make this production faster, but at first sight, at least, it feels like the rules themselves wouldn't help - a production program may run faster with certain kinds of notebooks, but I doubt if a production program that only works with certain types of notebooks could be much faster.

The basic idea is that the notebook processor keeps a list of rows that have been "used" and therefore necessitate a column in the transformation matrix. A little thought, however, makes it clear that the transformation matrices has both rows and columns indexed by the rows, and we need to know what the row has been used for - does it need a row, a column or both in the transformation matrix?

The transformation matrix starts off as the identity - T(i,j) is 1 if (i==j) and 0 otherwise. We therefore hold the partial matrix K(i,j) so that T(i,j) is K(i,j) if such exists, and 1/0 otherwise.