Meataxe-64
Field Specification.
Richard Parker 5.10.2017

Section 1 – Introduction

This document specifies the workings of the field module, which performs arithmetic with field elements, vectors and matrices over all fields of order less than 264. Although the HPMI (High Performance Meataxe Interface) handles the key matrix multiplication, it is the "field" module that performs all the main functionality, in much the same way as in all previous meataxe versions since the "arithmetic" subroutines evolved in the 1980's.

The internals of the field structure are fixed and publicized so that any software wishing to advance beyond what is provided here can at least utilize everything that is here. The definition of the interfaces is therefore fairly long and complex, since so much of it is public.

As well as describing what the "field" module does, this document also goes into significant detail as to how it does it.

As far as use (in the "c" language) is concerned, a FIELD is a fixed-length structure, but it is always followed by various look-up tables whose availability, structure and length depends on the field in use. For example for fields of order less than 256 of odd characteristic there is a uint8_t lookup table for addition called add8, and occasionally a program other than the field module itself may also wish to use it. When allocating memory for the FIELD structure, it is therefore FIELDLEN (defined in "field.h") bytes that must be allocated, not sizeof(FIELD), and similarly FIELDLEN bytes should be copied, and though I am not sure whether moving it about in this way has been tested, it should work. Once set, however, it is read-only.

The "pcrit" module provides some functions that are used in critical places in the field module. As a typical example, the multiply-and-add function DSMad y += λx calls an assembler subroutine to do the main function at vector length via table lookup, though the tables are constructed in the field module itself.

Section 2 – field.h and the data structures.

The field.h header file starts with the #define lines, and some typedef's of uint64, uint32, uint16 and uint8 as unsigned integral types of the specified size in bits. These are gradually being phased out, as <stdint.h> does this job perfectly well.

A FELT is a field element, typedef'd in field.h. In meataxe-64 this is always a uint64_t, but the programmer is encouraged to use a FELT for a field element for programming clarity.

The FIELD structure is a public, defined structure (see below for more details), though frequently its internals are not of interest.

Once set, this data structure is read-only, and may be safely passed around to threads. The setting of the structure can take some time (less than 10 mSec in most cases), and unnecessary repeated setting should be avoided.

field.h also typedef's Dfmt to be a uint8_t. Again the programmer is encouraged to use this whenever the data pointed to is indeed Dfmt.

====================================================================

Section 3 – The field module interfaces.

int FieldSet(uint64 fdef, FIELD * f, int flags) to set the FIELD structure f to work in the field specified by fdef. The fdef is an unsigned integer giving the order of the field. If fdef was a prime-power, a positive number is returned (2 if the HPMI is available and 1 if it is not) and if the fdef is invalid (not a prime power), -1 is returned. The area f provide here must be at least the size given by LenField (NOT sizeof(FIELD)!). The "flags" field must currently take the value zero.

TBD the current "trial division" factorization of fdef and fdef-1 means that FieldSet can take up to a minute or so for fields nearing 264. Values of the "flags" parameter may later be used to skip some of these tests, leaving the caller responsible that this is OK.

TBD also better factorization methods could be implemented, including checking if fdef is a perfect power, Pollard-rho and faster primality proving.

The following six functions do not check their parameters. A FELT is always in the range 0 . . . (fdef-1).

FELT FieldAdd(const FIELD * f, FELT a, FELT b) to add the field elements together in the field specified in the FIELD structure, so a+b is returned.

FELT FieldNeg(const FIELD * f, FELT a) to return the negative of the field element a in the field specified in the FIELD structure.

FELT FieldSub(const FIELD * f, FELT a, FELT b) to return the element a−b in the field specified in the FIELD structure.

FELT FieldMul(const FIELD * f, FELT a, FELT b) to multiply the field elements together in the field specified in the FIELD structure.

FELT FieldInv(const FIELD * f, FELT a) to return the inverse of the element a in the field specified in the FIELD structure. The FELT a must not be zero.

FELT FieldDiv(const FIELD * f, FELT a, FELT b) to return a/b in the field specified in the FIELD structure. The FELT b must not be zero.

Section 4 – The DSPACE routines.

These routines provide for the normal manipulation of vectors (and, in some cases, matrices) packed in D-format. These routines are not designed for the highest performance, and should not be considered suitable for “cubic” work unless the HPMI routines are not available. The DSPACE structure itself is of constant size and can just be declared, though it is a pointer to it that is used by the routines.

It should be noted that D-format in memory is completely defined, and that there is no need, in principle, to use these routines. Sometimes their performance is inadequate and the program needs to handle the data directly, in which case any tables used internally by the field routine are fully specified and available. It should be noticed that, in all fields, binary zero of the correct length is always the zero vector. The reader wishing for more details is referred to the field specification.

These routines work on valid input vectors only, and uninitialized memory may not be valid. The output of DAdd, DSub, DCpy and DCut may be uninitialized (somewhat heroically in the latter case), but DPak and DPaste must have a valid vector to put entries into. memset(ptr,0,bytes) is recommended to clear an area initially if it is to be populated with DPak or DPaste.

void DSSet(const FIELD * f, uint64 noc, DSPACE * ds) to set the DSPACE structure ds ready for working in a vector space of dimension “noc” over the given field.

size_t DSiz(const FIELD *f, uint64 nor, uint64 noc) to return the (minimum) number of bytes that must be allocated to hold the Dfmt of a nor x noc matrix.

FELT DUnpak(const DSPACE * ds, uint64 col, const Dfmt * d) to return the element in the specified column of the row pointed to by d in the specified space.

void DPak(const DSPACE * ds, uint64 col, Dfmt * d, FELT a) to insert the given element a into the specified column of the row pointed to by d in the specified space.

void DAdd(const DSPACE * ms, uint64 nor, const Dfmt * m1, const Dfmt * m2, Dfmt * m) to add the matrix m1 and the matrix m2 (each nor rows in length) in the specified space and put the result into m. This routine is specified as being of “good” performance, suitable for Strassen. Any or all of the areas m, m1 and m2 may be the same, but they must not otherwise overlap.

void DSub(const DSPACE * ms, uint64 nor, const Dfmt * m1, const Dfmt * m2, Dfmt * m) to subtract the matrix m2 from the matrix m1 (i.e. compute m1−m2) in the specified space and put the result into m. This routine is specified as being of “good” performance, suitable for Strassen. Any or all of the areas m, m1 and m2 may be the same, but they must not otherwise overlap.

void DSMad(const DSPACE * ds, FELT a, uint64 nor, const Dfmt * v1, Dfmt * v2) to adds the scalar multiple of the "nor" vectors at v1 by a into v2. This is done at reasonable performance.

void DSMul(const DSPACE * ds, FELT a, uint64 nor, Dfmt * m) to multiply the matrix pointed to by m by the scalar (field element) a. This is done “in situ”, and at reasonable performance.

uint64 DNzl(const DSPACE * ds, const Dfmt * v) to return the column number of the first non-zero entry in the vector. ZEROROW (#defined in field.h) is returned if the row is entirely zero.

void DCpy(const DSPACE * ms, const Dfmt * m1, uint64 nor, Dfmt * m2) to move nor rows of the matrix m1 to m2 in the specified space. The areas m1 and m2 may not overlap in any way (memcpy is used). m1 is left unchanged.

void DCut(const DSPACE * ms, uint64 nor, uint64 col, const Dfmt * m, const DSPACE * cbs, Dfmt * cb) to take a section of columns of Dfmt matrix m, starting at the stated (col) column number and put them into the clipboard space cb. The selected columns are taken from the first nor rows of m, and the number of columns taken is specified by the dimension of cb (in cbs). If more columns are requested than exist in m, the surplus columns are set to zero in cb.

void DPaste(const DSPACE * cbs, const Dfmt * cb, uint64 nor, uint64 col,
const DSPACE * ms, Dfmt * m) to take nor rows from the clipboard matrix cb and paste them starting at column col into the matrix m. If more columns are supplied than exist in m, the surplus columns are discarded.

void PExtract(const DSPACE * ds, const Dfmt *mq, Dfmt *mp, uint64_t nor,
 uint64_t psiz) to extract a matrix in Dfmt in the space "ds", consisting of nor rows over an extension field into N matrices over the ground field. The ground-field matrices must all be in one memory block, separated by "psiz" bytes. Special code copes with q={4,8,9,16}, and with characteristic up to 19 using Barrett extraction. The default, used for p>=23, uses division to get each element out.

void PAssemble(const DSPACE * ds, const Dfmt *mp, Dfmt *mq, uint64_t nor,
uint64_t psiz) to assemble N matrices over the ground field into one matrix over the extension field - the reverse operation to PExtract. Again special methods are used for q={4,8,9,16} but otherwise the generic multiplication method seems adequate.

Section 9 – The FIELD and DSPACE data structures.

The data items in the FIELD object are listed in the table below.

Type	Name	Description
uint64	fdef	The order of the field in use
uint64	charc	The (prime) characteristic of the field
uint64	pow	The power of the prime. TBD should this be int?
uint64	step	Used in multiply to deal with overflow
uint64	conp	The Conway Polynomial (xpow = conp) for all fields.
uint64	qstep	fdef/charc = p ^(n-1)
uint64	bar41	41-bit Barret multiplier for charc = 2^41 / charc (rnd up)
uint64	sqpower	charc ^ spaclev
uint64	sqpower2	charc^(2*spaclev) for adding in three chunks (case 14)
int	paktyp	How FELTS are DPak/DUnpak'd into Dfmt.
uint64	entbyte	number of entries that a byte can affect in format D
uint64	bytesper	bytes per storage unit in format D
uint32	dbytevals	number of values in a byte (only for q<=256)
uint32	qminus1	fdef−1.
int	addtyp	How to do adds and subtracts
int	multyp	How to do multiplies and divides
int	dsmadtyp	How to do a DSMad TBD add int pmat.
int	spaclev	Power of charc that can be added with spac/sqid
uint32	p32	Characteristic in 32 bits for faster reduction.
uint16	spaczero	x − y = sqid16[f->spaczero + spac16[x] − spac16[y]].
uint16	spacneg	-a = sqid16 [ spacneg - spac16[a] ]
int	gpaktype	characteristic paktype
uint64	gentbyte	characteristic entries per byte
uint64	gbytesper	characteristic bytes per entry.
uint64	linf	Number of matrices in L/B/Rfmt
int	hpmiflag	0 no hpmi/linf 1 hpmi+linf OK
uint64	cauldron	number of colums in a cauldron for this characteristic
uint64	cauldbytes	bytes in a cauldron. Usually 128.
uint64	alcove	number of rows/columns in an alcove for this characteristic
uint64	zeroword	Word to be put into Cfmt to represent zero
uint64	afmtalcovelen	Bytes of Afmt for one row of one alcove (e.g. 5).
void *	ftable	first byte available for other tables.
uint16 *	log16	Conway logarithm loge(x) q<=65536
uint16 *	alog16	Conway antilogarithm ex q<=65536
uint16 *	spac16	for many moderate fields
uint16 *	sqid16	a+b = sqid16[ spac16[a] + spac16[b] ]
uint16 *	zech16	Zech log = log(1+ex) q<=65536 TBD replace by spac16 and sqid16.
uint16 *	rdlg16	Reduce mod q−1 (for use with logs)
uint16 *	red16	Reduce mod the characteristic,
uint8 *	add8	byte + byte. q<256 not charc=2
uint8 *	sub8	byte − byte
uint8 *	mul8	elt * byte q<=256
uint8 *	inv8	Inverse
uint8 *	late8	Shift bytes to be later in vector (right in vector, left in byte)
uint8 *	early8	Shift bytes earlier in vector (left in vector, right in byte)

The DSPACE is a “c” structure of fixed size with the following elements.

Type	Name	Description
FIELD *	field	The field in use.
uint64	noc	The dimension of the space.
uint64	nob	Number of bytes for a row in D-format

TBD update for sqrt16

Section 10 "field" format and Format D in memory.

Meataxe-64 finite field formats are defined for all fields of order up to (but not including) 264. The first format defined is the "field" format, used for holding single field elements in a FELT (field element - actually a uint64). It expresses all elements of such a field as polynomials modulo the Conway polynomial, where a polynomial anxn + ... + a0 is held as the integer obtained by replacing the indeterminate x in the expression by p - the characteristic. Hence, for example, 3x+4 over a field of characteristic 7 is held as 3.7+4 = 25.

Format D is specified in terms of the field format. For fields of order 17 or greater, each FELT is stored in the smallest of uint64, uint32, uint16 or uint8 that can hold every element of the field. In memory (in principle) these are held in machine-endian form, but in practice the code only works on little-endian machines so the statement is currently rather academic. For fields of order q < 17 the entries are packed such that a uint8 holds as many as possible with the first vector entry added to q times the second, added to q2 times the third (q < 7) added to q3 times the fourth (q<5) etc.
Hence the entries are packed into bytes in a little-endian form. For example, a byte containing 11 over the field of order 3 represents the vector [2 0 1] (2.1+0.3+1.9).
Hence, for the field of order 9, for example, each byte holds a number in the range 0-80, each representing two consecutive vector entries - the first plus 9 times the second. The Conway polynomial is x2 + 2x + 2 for the field of order 9, and so the vector [ x+1 , 2x ] is converted first to the "field" format, yielding [ 4 , 6 ] and then to format D, yielding 58.
A vector then consists of the minimum number of entries needed to hold it, with zero elements appended to complete the last integer (uint8 for fields up to 256, uint16 up to 216, uint32 up to 232 or uint64 for the remainder) but no integers are stored unless there is at least one valid entry in it. Hence, for small fields, a vector may consist of any number of bytes, so that each vector of dimension 12 over GF(3) occupies three bytes.
(Format E is used in files, which is defined elsewhere in terms of format D. It is always subject to error detection and the compression of runs of zeros).

Section 11 - The 16-bit look-up tables

For all fields of order up to 65536 there is a set of 16-bit 1-dimensional look-up tables available to speed things up in various ways. The format and values of these tables are fixed, and the use of these tables as an alternative to calling the subroutines in this module is explicitly allowed.

TBD need sqrt16 table? If not it doesn't need computing unless degree is 4.

For every field, the Conway polynomial selects a fixed particular primitive root which is called "e" here, mainly to make the formulas look intuitive. Hence every non-zero element x of the field has a unique z with 0 ≤z≤p−2 such that ez = x. We refer to this z as the log(x) and the function ez is called the alog(z). The use of these tables enables faster multiplication, particularly for composite fields.

log16. This table is present for all fields of order q ≤ 65536. If z = log16 [ x ] for x ≠ 0 then ez = x. The arbitrary value q−1 is stored in log16 [0]. The element e is the smallest primitive root for prime fields and the indeterminate x of the Conway polynomial C(x) otherwise. This table has a uint16 for each element, so the table can be as large as 131072 bytes long for the field of order 65536. For x ≠ 0, 0 ≤ log16 [ x ] ≤ q−2.

alog16. This table is present for all fields of order q ≤ 65536, and gives ex for all for all 0 ≤ x < 2q, where e is as above.

The following two tables are designed to assist with addition and subtraction in odd characteristic at most 157 when the Dfmt has more than one entry mod p in the same integer.
    Addition	x + y = sqid16[spac16[x] + spac16[y]]
    Subtraction	x − y = sqid16[f->disp16 + spac16[x] − spac16[y]].
The spac16 table goes up to 37, 55, 74, 113-233 and 292-1572, and the sqid16 table goes up to the same power of (2p−1) Hence for example for p=19, the sqid16 table goes up to 393. Hence the table exists for all fields of characteristic 157 or less except the prime fields of order 17 or more.

spac16. This table is present for odd composite fields of order greater than 256 and characteristic p at most 251. Define z = 2p−1 and h = −1/2 as the number mod p such that h+h+1=0 mod p. Then spac16[a+bp+cp2 . . .] = (a+h)' + (b+h)'z + (c+h)'z2 . . . where ()' denotes reduction modulo p.

sqid16. This table is present for odd composite fields of order greater than 256 and characteristic p at most 251. Define z = 2p−1. Then sqid16[a+bz+cz2 . . .] = (a+1)' + (b+1)'p + (c+1)'p2 . . . where ()' denotes reduction modulo p.

red16. This table is present for all prime fields between 256 and 65536. It gives the reduction of numbers in the range 0 ≤ x ≤ 2.p (mod p) for use with addition. This table is not used by DSMad (which uses %charc for this purpose) but is used by DAdd and is of some significance as a result. Notice that this table gets rather large towards 65536, but it is only present when the log/antilog tables are absent, so the space usage is thereby in balance. TBD at present subtract must work as red8[p+a-b]. It seems better to allow for negative indices into this table to avoid the addition of p. A minor change to be done under regression later.

Section 12 - The 8-bit look-up tables

For fields of order up to 256, it is possible to store 2-dimensional arrays of table data for multiplication and addition and still have them fit in L2 cache. Hence the operations for fields of this scale are noticeably faster than for larger fields.

add8. This table is only present for fields of odd characteristic, order less than 256, and of composite order if q > 16. Hence it is present only for fields of order
{ 3, 5, 7, 9, 11, 13, 25, 27, 49, 81, 121, 125, 169, 243 }.
The data is stored so that there are no gaps in the table, and the number of values stored for each value of x is held in the variable dbytevals in the FIELD structure. The table is a dbytevals * dbytevals in size, and takes two uint8 Dfmt bytes x and y, where
z = add8 [ x * dbytevals + y ] is the Dfmt byte containing the sum of the corresponding values of x and y. For characteristic 2, the XOR procedure is faster, and for primes that can be readily extracted (which for q<256 means there is only one in a byte) it is faster to add them and use the red8 table to reduce. The add8 table is used in the DSMad routine for the fields where it exists, so is one of the performance-critical tables in those cases since again the cleaning in Gaussian uses it. The whole table may be up to 65536 (for GF(256)) and is usually fairly large. Its access pattern is, in general, random, meaning that it will frequently need a fetch from L2 cache (which is why adding and using red8 is faster for primes 17-251).
TBD should consider whether it is better to use shifts rather than multiplies.

sub8. This table is only present for fields of odd characteristic, order less than 256, and of composite order if q > 16. Hence it is present only for fields of order
{ 3, 5, 7, 9, 11, 13, 25, 27, 49, 81, 121, 125, 169, 243 }.
The data is stored so that there are no gaps in the table, and the number of values stored for each value of x is held in the variable dbytevals in the FIELD structure. The table is a dbytevals * dbytevals in size, and takes two uint8 Dfmt bytes x and y, where
z = sub8 [ x * dbytevals + y ] is the Dfmt byte containing the difference x − y of x and y.

mul8. This table is present for every field up to order 256, and in such cases multiples a field element x in the range 0 - (q-1) by a byte (uint8) y, which may contain more than one field element if the field order is 16 or less, to give the D-format uint8 result z i.e. z=x.y. The data is stored so that there are no gaps in the table, and the number of values stored for each value of x is held in the variable dbytevals in the FIELD structure above. Hence the value for z is
z = mul8 [ x * dbytevals + y] . The value of dbytevals is defined as q for q≥ 16, and for the smaller values takes these values . . .
16(256), 13(169), 11(121), 9(81), 8(64), 7(49), 5(125), 4(256), 3(243), 2(256).
The table entries for x=0 and x=1 are provided for uniformity, though it is freqently worth testing x for these values and taking special (simpler and faster) action in these cases. The mul8 table is used in the DSMad routine for the fields of order 3-256, so is one of the performance-critical tables since the cleaning in Gaussian uses it. In its use in DSMad and also DSMul, the x is constant for the whole vector so only one row of the mul8 tables is accessed, fitting easily into L1 cache since it is at most 256 bytes long. The whole table may be up to 65536 bytes long (for GF(256)) but is considerable smaller for most fields - already for q=191 it only occupies 36,481 bytes.

inv8. This table is available for all fields of order 2-256, and gives, for 1 ≤ x ≤ (p-1) the number z = inv8 [ x ] which is the multiplicative inverse in the field. The entry inv [ 0 ] is zero and is not, of course, the inverse. Although this table is used in Gaussian Elimination, it is not of the greatest significance in terms of performance since it is not used very often. It is only used in the FieldInv and FieldDiv routines, and not in any vector-based operations, but is anyway only (at most) 256 bytes long so is probably just about worth having.

The naming of the following tables is relative to the vector. Notice that, because we use little-endian technology throughout, right shifting in the byte makes it earlier in the vector which one might consider a left shift in the vector, making left and right too confusing to contemplate.
It is best not to think of what happens in the byte. Concentrate on the vector.

late8. This table is available for all fields of order up to 16, and allows for the left-shifting of entries within a byte. The table consists of a collection of dbytevals entries, the first shifting left one place, the second two (only for 2,3,4,5) the third shifting three places (only for 2,3,4), the fourth for four places (2,3) and 5, 6 and 7 for GF2 only. Notice that the shifts are in entries as needed for cut and paste.

early8. Exactly similar to late8, except that the shift is in the opposite direction. To combine the result of two shifts in opposite directions they should be added - in odd characteristic bitwise OR or XOR are no good!

Section 13 - Some general points

The Barrett reduction bar41 is used here to obtain h and k from a number of the form x = hq+k (where k<q) without doing a division. Instead the number b = 241/q (rounded up) is computed in advance, and xb computed and right-shifted 41 places to obtain h. The rationale for this is that xb/221 = (hq+k)[241/q] is indeed approximately h and the difference can be estimated and bounded. Hence we can compute when it works in advance.

The spic/sqid scheme can add/subtract vectors of dimension 6 (resp 5,4,3,2) in characteristic 3 (resp 5, 7, 11-19, 23-127) by means of simple table-lookups and addition/subtraction. It is therefore useful to know the boundaries of the bar41 scheme in some detail so that addition schemes for higher degrees in these characteristics can be devised.

Barrett 41 and spac/sqid table

char	spaclev	limit	spac/sqid	Barrett multiplier
3	6	320	36	3 016 492 806
5	5	513	55	703 687 442
7	4	712	74	915 878 074
11	3	119	113	1 652 158 720
13	3	138	133	1 000 920 918
17	3	177	173	447 592 766
19	3	196	193	320 604 062
23	2	237	232	4 156 943 773
29	2	296	292	2 614 772 005
31	2	316	312	2 288 265 615
37	2	376	372	1 606 298 945
41	2	415	412	1 308 163 746
- - -	2	- - 5	- - 2	- - - - - -
59	2	595	592	631 721 706
61	2	614	612	590 976 420
- - -	2	- - 4	- - 2	- - - - - -
127	2	1274	1272	136 339 715
131	1	1314	-------	16 786 437 066
- -	1	- - 4	-------	- - - - - -
199	1	1994	-------	11 50 368 119
211	1	2113	-------	10 41 911 164
- -	1	- - 3	-------	- - - - - -
1277	1	12773	-------	1 722 022 910
1279	1	12792	-------	1 713 969 802
- -	1	- - 2	-------	- - - - - -
13339	1	133392	-------	164 856 681
13367	None	None	-------	None.

Section 14 - The main algorithms used.

DSMad. This is the most performance critical routine in the field module, since it is used in the layer-2 echelize proggy to do the cleaning. Nevertheless the main work of the layer-4 echelize is done by using the hpmi interface, so that no long-running program should be spending much of its time in this routine. Nevertheless there is no need to be slack!

dsmadtyp=1 for { 2, 4, 8, 16, 32, 64, 128, 256 }
If the multipler is zero, just return, and if the multiplier is 1, a call to DAdd is made. Notice that for the field of order 2 these are the only possibilities. Otherwise the multiplier is converted into a pointer to the beginning of the row of mad8 for that multiplier. Each uint8 is then extracted, looked up in this table (in L1 cache), then the resulting byte and the byte in the answer vector are XOR'd together to produce the answer byte.
dsmadtyp=2 for { 3, 5, 7, 9, 11, 13, 25, 27, 49, 81, 121, 125, 169, 243 }
For these fields, DSMad is implemented by initially inspecting the multiplier, and if it is zero just return, and if it is 1 a call to DAdd is made (q.v.). Otherwise the multiplier is converted into a pointer to the beginning of the row of mad8 for that multiplier. Each uint8 is then extracted, looked up in this table (in L1 cache), then the resulting byte and the byte in the answer vector are looked up in the add8 table - a look-up which may somewhat exceed the capacity of L1, especially for fields of order 3 and 243.
dsmadtyp=3 for primes 17-251
If the multipler is zero, just return, and if the multiplier is 1, a call to DAdd is made. Otherwise the multiplier is converted into a pointer to the beginning of the row of mad8 for that multiplier. Each uint8 is then extracted, looked up in this table (in L1 cache), then the resulting byte and the byte in the answer vector are added together, and then looked up in the red8 table (again in L1 cache) to produce the answer byte.
dsmadtyp=4 for primes 257-65521
Despite the availability of log, zech and even reduction tables, I believe that the simple (a*b+c)%p is the fastest way of doing this case. It is probably important too that the work is done with uint32, since the 64-bit division would usually be considerably slower. TBD I am not convinced. I suspect log for multiply would be better.
dsmadtyp=5 for odd composites 289-4200
The multiplier must be tested for zero, and a return made if so. I am not clear whether a test for 1 is worthwhile. The log16 of the multiplier is then found. For each coordinate, the entry from the first vector is extracted, and this must also be tested for zero (and pass on to the next coordinate if so). Otherwise the log16 of this is also found and added to the previous one. This is then reduced modulo q-1 using rdlg16. The other entry is fetched and again a test for zero made (alog the other entry and store it if so) before looking this up also in the log table. The difference between these two log values is then computed and reduced mod q-1 (rdlg16 again), after which the result is looked up in zech16. Yet a further test for zero (stored as q-1 in the zech16 table) must be made (just store zero if so) before adding the log back in, reducing mod q-1 (third use of rdlg16) then using alog to finally produce the answer.
dsmadtyp=6 for even characteristic between 512 and 4096
The multiplier must be tested for zero, and a return made if so. I am not clear whether a test for 1 is worthwhile. The log16 of the multiplier is then found. For each coordinate, the entry from the first vector is extracted, and this must also be tested for zero (and pass on to the next coordinate if so). Otherwise the log16 of this is also found and added to the previous one. This is then reduced modulo q-1 using rdlg16 and then alog16 of this looked up. The other entry is fetched and their XOR put back into the answer vector.
dsmadtyp=7 for odd composites 4200-65536
The processing for this case is identical to that for dsmadtype=5, except that the three reductions modulo q-1 are done using %qminus1 instead of using the rdlg16 table.
dsmadtyp=8 for even characteristic between 8192 and 65536
The processing for this case is identical to that for dsmadtype=6, except that the three reductions modulo q-1 are done using %qminus1 instead of using the rdlg16 table.
dsmadtyp=9 for primes between 65527 and 232.
(a*b+c)%p is used for each entry, like dsmadtyp 4 except that uint32* must be used for the pointers. The code takes care that although the numerator is 64 bits, the denominator is only 32 bits. Current x86 processors seem unable to use this fact, but it may become useful on later processors.
dsmadtyp=10 for odd composites between 65527 and 232.
This case is implemented by simply calling qmul and qadd. I suspect that this case could be improved considerably if it were considered important. For example an array could be made of the coefficients of the polynomial of the multiplier, the multiplication can be subjected to Karatsuba, and the reduction speeded up in the (frequent) case where xn is the sum of only two terms in the Conway Polynomial.
dsmadtyp=11 for even characteristic between 217 and 232.
This case is implemented by calling qmul and then XOR. Again improvement could be made if considered useful.
dsmadtyp=12 for odd characteristic (primes and composites) between 232 and 264.
This case is implemented by simply calling qmul and qadd. Clearly room for improvement here also.
dsmadtyp=13 for even characteristic between 233 and 264.
This case is implemented by calling qmul and then XOR. Improvement possible.

DAdd/DSub. These routines are used for the Strassen add/subtract and are under considerable performance pressure. The addtyp indicator used here is also used in FieldAdd, FieldSub and FieldNeg.

addtyp=1 for all characteristic 2.
For both DAdd and DSub, the routine XORs "ds->nob" bytes, using uint8 or uint64 depending on the worst congruence of the pointers and the length. FieldAdd, FieldSub both do XOR in this case, and FieldNeg merely returns its input. TBD it is probably possible to improve on this to do things at 64-bit length more. What are the alignment requirements these days?
addtyp=2 for { 3, 5, 7, 9, 11, 13, 25, 27, 49, 81, 121, 125, 169, 243 }.
In these cases the add8 table is used to add the entries together and the sub8 table similarly for subtraction. The field operations are done exactly similarly.
addtyp=3 for primes 17-251.
These use addition followed by the red8 table to do the reduction. Subtraction and negation work by computing p+x-y or p-x and looking the result up in red8.
addtyp=4 for primes 257-65536.
These use addition followed by the red16 table to do the reduction. Subtraction and negation work by computing p+x-y or p-x and looking the result up in red16. At the extreme level (65521) the red16 table will pretty-much fill L2 cache at 256K.
addtyp=5 for odd composites 36,54-55,73-74,113,133,172-173,192-193,232-1272. The actions performed are x + y = sqid16[spac16[x] + spac16[y]] and
x − y = sqid16[f->spaczero + spac16[x] − spac16[y]]. See the descriptons of these tables to see what they contain and how they work.
addtyp=6 for prime-squares too large for spac/sqid, namely 1312 up to 2512. Done using Barrett and then adding and using red8 to reduce.
addtyp=7 for primes 65536 - 232.
These use addition followed by some sort of branch-free conditional to do the reduction.
addtyp=8 for odd composites 65536 - 232 where addtype=11 does not apply.
These just use qadd. This could be improved if required. See also addtyp11.
addtyp=9 for primes 232 - 263
These use addition followed by some sort of branch-free conditional to do the reduction.
addtyp=10 for odd composites above 232 and primes bigger than 263.
These just use qadd. This could be improved if required.
addtyp=11 for 32-bit composites that can be split into two parts each within the range of spac/sqid. Hence pow is at most 2*spaclev and spaclev is at least 2.
addtyp=12 for 16-bit composites too large for a single spac/sqid, so Barrett is used once to break it into two parts that are still composite, then spac/sqid is used on both parts.
addtyp=13 for 32-bit fields of degree 2 where the characteristic is at most 13339. Done using Barrett and then adding and using red16 to reduce.
addtyp=14 for 32-bit fields of degree 3 where the characteristic is between 256 and 1277. It is done much like addtyp 13, except, of course, it is cubic.

DSMul. Although not normally considered a performance-critical routine, there is, as usual, no need to be slack. The multyp indicator is also used in FieldMul, FieldInv and FieldDiv.

multyp=1 for all fields of order 256 or less.
DSMul and FieldMul operate by looking up the byte-pair in the mul8 table. Invert uses the inv8 table, and divide uses inv8 and then mul8.
multyp=2 for prime fields 256-65536
DSMul and FieldMul simply compute (a*b)%charc, taking care to use 32-bit objects. Invert just uses pinv, and divide uses pinv followed by (a*b)%charc. TBD I suspect it will be faster to use logs. Also it is not clear whether invert modulo p warrants an inverse table inv16.
multyp=3 for composite fields 256-4200
All the functions use log16, rdlg16 and alog16 with appropriate tests for zero.
multyp=4 for composite fields 4200-65536
All the functions use log16, %qminus1 and alog16 with appropriate tests for zero.
multyp=5 for prime fields 65536 - 232
DSMul and FieldMul simply compute (a*b)%charc. Invert just uses pinv, and divide uses pinv followed by (a*b)%charc.
multyp=6 for composite fields 65537 - 232
These just operate using qmul, qinv and qdiv.
multyp=7 for all fields 232 - 264
These also just operate using qmul, qinv and qdiv.

DPak and DUnpak. These two routines both use the paktyp paramter to determine which of 9 algorithms are in use for compressing a vector of field elements into Dfmt.

paktyp=0 for uint64 elements each holding one field element. 232 < q < 264.
paktyp=1 for uint32 elements each holding one field element. 216 < q ≤ 232.
paktyp=2 for uint16 elements each holding one field element. 257 ≤ q ≤ 65536
paktyp=3 for uint8 elements each holding one field element. 17 ≤ q ≤ 256.
paktyp=4 for uint8 elements each holding two field elements. These are held as a + fdef*b for the vector [a,b] (notice - little-endian). q is one of { 7, 8, 9, 11, 13, 16 }
paktyp=5 for uint8 elements each holding three field elements. These are similarly held little endian (a+qb+q2c for [a,b,c]) and the paktyp is only used for the field of order 5.
paktyp=6 for uint8 elements each holding four field elements. These are similarly held little endian and the paktyp is only used for the field of order 4.
paktyp=7 for uint8 elements each holding five field elements. These are similarly held little endian and the paktyp is only used for the field of order 3.
paktyp=8 for uint8 elements each holding eight field elements. These are similarly held little endian and the paktyp is only used for the field of order 2.

For the small fields, and particularly 3,5,7,9,11,13 where divisions are involved, it seems highly likely that skillful application of look-up tables would make a positive improvement to performance. I am currently not convinced of the need for this.

DNzl. This routine is, as far as I know, not particularly performance critical, so it works by first looking through up to nob bytes to find the first non-zero byte, and then uses paktyp to determine what it now knows. For paktyp 0-3 a computation on the byte number (divide by 8, 4, 2 or '1') gives the column number. Otherwise the byte number is multiplied by entbyte and the DUnpak routine called repeatedly to get the exact index. Of course this latter step could be streamlined with lookup tables, but there seems to be no need.

DCut This routine, which is under some performance pressure, is designed to use memcpy and memset wherever possible. There are look-up tables early8 and late8 that are used to "shift" the data since, in odd characteristic ordinary bit shifts are not appropriate. The routine first computes a few data items about what it is going to do, and then come the 12 cases depending on whether there are bytes to zeroize, shifts to do in general and many special cases.

Matrix is [ col columns ignored ] [ movecols columns moved ] [ remaining columns ]
..........................................................................................lbmbits

Clipboard is [ movecols columns moved ] [ possibly some columns to zeroize ]
.....................< outbyte >< clearbytes >
....................................................lbcbits

TBD This needs checking against the code to see if any bugfixes require this documentation to be changed. Also look through JGT emails for the same purpose.

The first four cases cover all cases where the input and output are in registration so that, for the initial bytes at least, memcpy is OK. This is tested by checking if (gshift=col%entbyte) is 0.

Case 1 covers all cases where clearbytes is not zero. In this case even if the last input byte is incomplete it must be correctly zero-padded, so can just be moved.

Case 2 deals where the moved data is an integral number of bytes. This is the performance case for chopping etc. done simply by moving bytes with memcpy. This is tested by checking if (lbcbits=movecols%entbyte) is zero or uptoend==1, so that we end on a byte boundary either truthfully, or we might as well assume so since we are taking it all anyway.

Case 3 then allows for a partial last byte, carefully zeroizing the unwanted columns (at least one) since this is known to be needed.

Case 4 is similar, but there is only one byte of output so nothing to memcpy.

Otherwise we are not in registration, so must compute the general shift tables, where ges is applied the first byte, gls to the second byte and the results added. Notice that the cases from here on can only occur if the field has order 16 or less.

We now disjoin on the sizes of lbcbits and lbmbits - the number of (real) bits in the last byte output and input respectively. Notice that these cannot be equal now, because in this case gshift would be zero - a situation dealt with by cases 1-4.

Firstly if lbmbits is zero, our input ends on a input byte boundary. We may or may not have full bytes to zeroize giving us two cases.

Case 5 has no bytes to zeroize

Case 6 has at least one byte to zeroize.

Secondly it may be that lbcbits is zero, so that our output ends on a byte boundary. In this case the last byte of output needs no special treatment, and the cases, as for lbmbits, are merely to avoid performance cost of the call to memset with a zero length.

Case 7 has no bytes to zeroize

Case 8 has at least one byte to zeroize.

The third major shifting section is where lbmbits > lbcbits. In this case the last byte has few bits, all coming from one byte of the input. Again the loop is duplicated to avoid the overhead of a call to memset with zero length. The last byte must be shifted entbyte-lbmbits to clear the last entries, then entbyte-lbcbits to put them into the correct registration.

Case 9 has no bytes to zeroize

Case 10 has at least one byte to zeroize.

The last case is where lbmbits<lbcbits. Here the last output byte is assembled from two parts. The first part is simply the normal ges shift of the first input byte. The rest is obtained by shifting late the input byte entbyte-lbmbits to clear the last entries, and then shifting that early by entbyte-lbcbits as usual to put it into registration. Again, as usual, twp cases to avoid call to memset when clearbytes is zero.

Case 11 has no bytes to zeroize

Case 12 has at least one byte to zeroize.

DPaste This routine is also under some performance pressure, and many of the comments in DCut apply also to DPaste. In particular it uses memcpy and memset where possible, and the early8 and late8 lookup tables for shifting. An important variable for case disjunction is called wlong, which takes the value 1 if the matrix row extends beyond the pasted part, value 2 if the very last entry in the clipboard row is going to the very last entry in the matrix row, and value 3 if the cliboard row extends beyond the end of the matrix row so that some of it must be discarded.

Clipboard is [ movecols columns moved ] [ possibly some columns to ignore ]
.....................< inbyt >< ................ >
......................................................lbcbits

Matrix is [ col columns ignored ] [ movecols columns moved ] [ remaining columns ]
........................................................................................lbmbits

TBD This needs checking against the code to see if any bugfixes require this documentation to be changed. Also look through JGT emails for the same purpose.

The first three cases cover the situation where the input and output are in registration so that, for the initial bytes at least, memcpy is OK. This is tested by checking if (gshift=col%entbyte) is 0.

Case 1 covers all the cases where memcpy can do all the work. This requires the start of the clipboard row to be going to the start of a matrix byte, and the last entry to either come from the last entry in a clipboard byte (and hence be going to the last entry in the matrix byte also) or to be the very last entry in both rows (i.e. wlong==2)

Case 2 covers the registration case where all of the cliboard is being pasted into the middle of the matrix (wlong==1). In this case the last byte is already followed by zeros, but further entries from the matrix must be put in.

Case 3 covers the registration case where some of the clipboard row is being discarded. In this case it is necessary to clean out the unwanted entries from the clipboard byte, but there are no entries coming from the matrix.

Similar to DCut, the remaining operations are primarily disjoined on how the last byte is made, depending on lbmbits (last byte of matrix bits) and lbcbits (last byte of clipboard bits). These cannot now be equal because that would imply col%entbyte is zero, which has already been treated in cases 1-3. The remaining cases can only occur for fields of order at most 16. They all require the patching in of the first byte using fls to shift the first matrix byte temporarily into the registration that the clipboard has. Not that if lbmbits>lbcbits, neither zero, we must cater specially for the case of a single byte getting its data from matrix, clipboard, matrix.

Case 4 covers case of lbmbits==0, where the end of the patch comes nicely at the end of a matrix byte. The first byte is patched, but all others (if any) come entirely from the clipboard.

Case 5 covers case of lbcbits==0, where the end of the patch comes exactly at the end of a clipboard byte. The first byte is patched, and the end of the last byte of matrix comes from the matrix (shifted by fes) not the clipboard if wlong==1 (so there is some more matrix).

Case 6 covers the same situation as case 5, but optimizes for the case where the matrix row has anyway ended so there is no need to patch matrix entries in at the end

The next three cases cover lbmbits < lbcbits so that the last byte of m is just more of the last byte of cb that we already used. We can be certain that there are two affected byte of the matrix in this case.

Case 7 covers case wlong==1, so we are inserting the end of a clipboard row into the middle of the matrix. There is therefore no need to clear the end of the last clipboard byte (it is already clear).

Case 8 covers case wlong==2, so we are inserting the end of a clipboard row at the end of the matrix row. This is therefore even simpler, since there is also no matrix entries to patch in.

Case 9 covers case wlong==3, so we are inserting some of the clipboard at the end of the matrix row.

The final cases cover lbmbits > lbcbits. Again we disjoin according to wlong, but if wlong==1 we need to take care that the first and last byte may be the same, giving four cases.

Case 10 covers wlong==1 when inbyte is 1. The single output byte is therefore made up of three parts - matrix, clipboard, matrix.

Case 11 covers wlong==1 when inbyte is greater than 1. The first byte is therefore patched together as usual, and the last byte comes from two bytes of clipboard with some remnamnant of the original matrix after that.

Case 12 covers case wlong==2, so we are inserting the end of a clipboard row at the end of the matrix row. This is therefore very simple, where the last byte is no different from the rest.

Case 13 covers case wlong==3, inbyte==1, so we are inserting some, but not all of a single clipboard byte into the middle of a matrix byte.

Case 14 covers case wlong==3, inbyte>1, so we are inserting some of the clipboard at the end of the matrix row so the last byte of the clipboard needs to be cleaned, but that this is not the first byte as in case 13.
Section 15 - Other functions.

uint8 * AlignMalloc(size_t bytes) allocates memory aligned to the cache-line. If this routine is used to allocate memory, the following routine must be used to free it.

void AlignFree(uint8 * ptr) frees memory that was allocated by AlignMalloc