Meataxe-64
HPMI specification.
Richard Parker 11.10.2017

Section 1 – Introduction

This document specifies the High Performance Meataxe Interface (HPMI). It is the result of my work in August-October 2017 to restructure it with a view to simplifying its implementation for new characteristics, new technologies (e.g. Ryzen and AVX-512) and new applications - particularly the upcoming "slab echelize".

The document is intended to serve two distinct purposes, namely the use of the HPMI as described in section 2, and the implementation of new technologies and/or characteristics as described in section 3.

The HPMI works only over prime fields, and at present only 2 and 3 are implemented. Extension fields are handled at a higher level using Albrecht-style methods in the "linf" module.

The primary objective of the HPMI is to achieve the fastest possible matrix multiply-and-add, for which the BrickMad function is used to perform C += A x B for a particular size and shape - namely alcove x cauldron - chosen by the HPMI - of a brick of matrix B, and though the number of rows (a box) of A/C may vary, there is a number recbox that is recommended by the HPMI so that matrix C can be expected to reside in a suitable cache level - usually L2.

The overall objective is to multiply matrices held in the general-purpose format called Dfmt, but to do so at top speed, it is usually best to do some reformating (an operation of quadratic complexity) to minimize the work done at cubic complexity. The HPMI assumes that this is always done, and in no case so far has this proved inappropriate. In particular, handling padding (at the left-hand and bottom of the matrix) and sparsity seems worthwhile even when avoiding the "move" might otherwise seem worthwhile.

Therefore, the HPMI converts matrix A into a suitable format (Afmt), matrix B into another suitable format (Bfmt), computes the result of C+=AxB in a third format (Cfmt) and provides routines for performing the necessary format conversions - the idea being that the format conversions are done to relatively massive matrices, so that the conversion time becomes relatively negligible compared to the (cubic) multiplication time. As an aside, it is usually better to do large-scale additions in Dfmt rather than doing the (anyway as yet unimplemented) conversion from Dfmt to Cfmt to avoid it.

The principle is that to compute C = A x B we . . .

DtoA	Convert A from Dfmt to Afmt
DtoB	Convert B from Dfmt to Bfmt
CZer	Zeroize C
BrickMad	Do all the multiply-and-adds
CtoD	Convert C from Cfmt to Dfmt.

A programmer wishing to implement a characteristic in a technology typically first writes BrickMad to work as fast as possible on that machine, thereby defining Afmt, Bfmt and Cfmt, and then writes the conversion programs.

For implementation purpose only (with the possible exception of a user wishing to keep a small number of seeded/greased bricks), BrickMad itself consists of three phases . . .

BSeed	to put the vectors of B into the Brick Work Area (BWA).
BGrease	to compute all the linear combinations necessary
BwaMad	to actually perform the work.

The latter is almost always written in assembler, and is the performance-critical heart of meataxe64. For small characteristics, anyway, the BGrease operation can also be of some importance in the performance sense.

Two further routines, DtoC and PivC will soon be provided for use in Gaussian elimination to enable this process also to rely primarily on BrickMad to do most of the work.

All these routines are specified, with performance as the only objective, leaving extension fields, memory allocation etc. to the calling functions. In meataxe64 these are handled my linf and slab.

Section 2 – Using the HPMI

Section 2.1 - Using the HPMI

It is not really expected that the HPMI be used very much on its own. Matrix multiplication is handled over the ground field by the "pmul" module, over extension fields by the "linf" module, and usually the yet-higher "slab" module is used to handle matrix multiplication over arbitrary fields, including those that where the HPMI and/or the linf implementations are not yet available.

Nevertheless some upgrades of all these modules are anticipated in future, particularly in the area of Gaussian and the better use of cache, so it seems appropriate to get the use of the HPMI documented, partly to facilitate these upgrades and partly to highlight any remaining difficuties with its use.

The routine hpmiset must be called first. This is usually done by calling FieldSet (in the "slab" module). It sets a collection of public variables, and also some "private" variables and tables for use only by the hpmi module which are documented in section 3.

void hpmiset(FIELD * f) to set (in the given field) the public and private variables for the HPMI to work in the characteristic of the given field. If there is not an HPMI implementation available, the "cauldron" variable is set to zero.

The HPMI works by dividing matrix B (the right-handmultiplier) into bricks which consist of an alcove x cauldron rectangle of the matrix. A right-hand multiplier always consists of complete bricks, so that frequently extra zero columns are added to the last brick of a row, and extra zero rows added to the bottom of the matrix to ensure this.

The conversion routines all take a DSPACE parameter, to specify the field, and also how many columns there are. CtoD is expected to take an entire matrix of "slab" scale. DtoA is expected to take slab-scale columns but only "box" rows. DtoB takes a single brick except at the right and bottom margins of the matrix. It is possible to break these expectations in some ways, and the exact nature of what is and is not allowed is described in Appendix 1, although except possibly for doing only some of the columns of matrix A, it is hard to see why this might be useful, as DCut/DPaste can be used to do do the chopping effectively in Dfmt. The description here assumes that the conversions be done in the expected way.

The hpmiset routine sets the following "public" variables. They are all uint64_t.

alcove	The number of columns (in A) or rows (in B) of an alcove.
cauldron	The number of columns (in B and C) in a cauldron.
bbrickbytes	The maximum number of bytes in a brick in Bfmt
cfmtcauld	The number of bytes in a cauldron in Cfmt.

dfmtcauld	The number of bytes in a cauldron in Dfmt
alcovebytes	The number of bytes in an alcove in Afmt inc. skip/term.
recbox	The recommended number of rows (box) of A/C to do at once
bwasize	The number of bytes to allocate for a BWA

The user must also allocate and initialize a BWA (of a size specified in bwasize) and allocate an array of uint64_t values (called ix) of length the maximum number of alcoves that will be used in any call to DtoA. The ix array does not need to be initialized. The HPMI itself does no memory allocations.

extern void BwaInit(const FIELD *f, uint8_t *bwa) to initialize the given bwa (Brick Work Area) to be suitable for working over the given field. This typically sets the vectors to zero that will need to be zero for every possible brick.

Second only to Dfmt (upon which all the functions of the field module can operate) Cfmt is, in some sense, the main format for the HPMI. Conversion to Dfmt is already provided, and the reverse (DtoC) is expected in due course, as it is needed for HPMI-Gaussian. There is a function (CZer) to set a Cfmt matrix to zero, and (again in due course) a function to extract pivots directly from Cfmt into Dfmt will also be needed for slab Gaussian. A nor x noc matrix in Cfmt consists of noc/cauldron (rounded up) blocks of nor rows each consisting of cauldbytes bytes of data. This overall structure can and must be understood by the caller. In particular, the entire matrix for the first cauldron comes first in memory, followed by the second cauldron . . . the matrix is partially transposed!

A pointer to a Cfmt matrix should be aligned to 64 bytes, but there is no guarantee that cauldbytes will be divisible by 64 bytes, in which case a lesser alignment will be tolerated. In other words if X is 64-byte aligned, then X + N.cauldbytes is acceptably aligned for all values of N.

The last cauldron may be incomplete, in which case all unused columns must contain zeros.

Section 2.2 - DtoA

void DtoA(DSPACE * ds, uint64_t * ix, Dfmt *d, Afmt *a,
uint64_t nor, uint64_t noc)

Afmt conversion is designed to take an integral number of Dfmt bytes at a time. The number of rows (the box) may be any value, but it is recommended that recbox be used except for the last box (which will be smaller) so that the cache be appropriately used for the Cfmt. The ix array must be of a size sufficient to hold all the alcoves, and the correct size is noc/alcove (rounded up) uint64_t variables, or 8*(noc+f->alcove-1)/f->alcove) bytes. The stride parameter is the number of bytes in a full row and is there to allow partial conversions - see appendix 1.

Many alcoves are, in general, converted by this call, so that the output needs a rigidly defined memory layout. The Afmt area must be allocated by the caller as a collection of alcoves numbering noc/alcove (rounded up), where each alcove consists of 1 + nor * alcovebytes. In fact, the total allocation must be at least eight bytes longer than this to allow for 8-bytes loads.

The output of the j-th alcove therefore starts at a + (j * [1 + nor*alcovebytes]). If there is considerable sparsity, it may well be that the output for some alcoves is considerably less than 1+nor*alcovebytes in length, but no mechanism is provided to salvage this space, though this would in principle be possible - perhaps by providing a function "how long is this chunk of Afmt".

There is a parameter "recbox" which is provided by the HPMI in the FIELD structure as being a suitable value for the number of rows to use for this call, and it is recommended that this be used for all but the last chunk of rows. The HPMI chooses this with regard to the size of L2 cache (so that maxbox cauldrons of Cfmt live comfortably in L2) and also with regard to the L1 cache structure for the DtoA call.

As a rule, DtoA is implemented by processing each row in turn, appending the Afmt to each alcove as it goes. This would thrash the cache if maxbox*alcovebytes were, for example, 4096 or very close, but hpmiset has enough information to make a good choice and avoid this problem.

There is no need to align the Afmt in any way, though it is best aligned at least 8 bytes (which malloc does anyway). There may also be a small performance improvement for some future characteristics if it is allocated to a cache-line boundary, but even pmul does not do this at the moment.

Section 2.2 - DtoB

uint64_t DtoB (DSPACE * ds, Dfmt * d, Bfmt * b, uint64_t nor, uint64_t noc)

This function produces one brick of Bfmt from the input Dfmt. The input starts at the pointer d, which is typically in the middle of a row. The cauldron is defined to be an integral number of bytes, available in f->dfmtcauld, so this is viable. Since a brick has many rows, the routine also needs the length of the row and this is taken from the DSPACE supplied. nor is expected to be <alcove> and noc is expected to be <cauldron>, but either, or both, may be smaller to convert bricks at the right-hand end and/or the bottom of the matrix. The output is at most f->bbrickbytes long, but may be smaller. It is not unreasonable to simply treat the Bfmt as a collection of bricks each of exactly that size, but the actual size of the conversion is returned (the uint64_t return value) so that any wasted space (due to sparsity in matrix B) can be salvaged.

Again, refer to appendix 1 if more detailed knowledge of the use of nor or noc is required.

There is no function to convert Bfmt back into Dfmt.

Section 2.3 - CZer

void CZer(DSPACE * ds, Cfmt *c, uint64_t nor) is used to set a complete matrix to (Cfmt) zero. It should not be assumed that binary zero will do this, as - more often than not this is not the case. Mod 3, for example, zero is all 1 in binary. Also there will frequently be a bias.

Section 2.4 - BrickMad

For normal use, the simplest way to do the key brick-multiply-and-add is to use the BrickMad function.

void BrickMad(FIELD *f, uint8_t * bwa, Afmt *a, Bfmt *b, Cfmt *c) to get the Bfmt brick b into the bwa and grease it, and then to multiply it by the Afmt string a (of arbitrary length), adding the result into the Cfmt block c (of the "same" length).

The number of rows of A/C is specified implicitly by the Afmt, and the other two dimensions are fixed - alcove and cauldron.

As mentioned in the introduction, BrickMad internally consists of three component subroutines - BSeed, BGrease and BwaMad. There is usually no need to understand these three components. They are there partly to clarify implementation, and partly to allow for the possibility that repeated BSeed and BGrease calls can be avoided, though this is normally counter-productive since usually more time will be lost moving the data around (the BWA is often considerably larger than the Bfmt brick) than will be saved.

The documentation of BSeed, BGrease and BwaMad are therefore included in section 3 (Implementing the HPMI) since they exist mainly for that purpose.

Section 2.5 - CtoD

void CtoD(DSPACE * ds, Cfmt *c, Dfmt *d, uint64_t nor) is used to convert a complete matrix in Cfmt into Dfmt. Notice that ds.noc may not be an integral number of cauldrons, so this routine must cater for partial extraction from the last cauldron.

A pointer to a Cfmt matrix should be aligned to 64 bytes, but there is no guarantee that cauldbytes will be divisible by 64 bytes, in which case a lesser alignment will be tolerated. In other words if X is 64-byte aligned, then X + N.cauldbytes is acceptably aligned for all values of N.

The reverse function is probably only useful to use the HPMI for Gaussian elimination and is not of great importance for performance. In any case . . .

DtoC HAS NOT YET BEEN IMPLEMENTED

void DtoC(DSPACE * ds, Dfmt *d, Cfmt *c, uint64_t nor) will be used to perform the reverse operation - to convert Dfmt to Cfmt. Again there is a need to cater for the case where ds.noc is not divisible by <cauldron>, in which case (Cfmt) zero entries are appended.

PivC HAS NOT YET EVEN BEEN SPECIFIED

There will also be a PivC function to extract columns from a Cfmt matrix directly into Dfmt, for use in slab-scale Gaussian. The exact nature of this has not yet been designed, as it is probably useful to have a field-independent way to assist the performance extraction of multiple adjacent columns.

Section 3 – Implementing in the HPMI

Section 3.1. Strategy for writing an HPMI implementation.

At the very heart of the drive for performance in meataxe64 is the BwaMad routine, and the initial design effort naturally starts here. A value for <alcove> and <cauldron> chosen so that the Brick Work Area (BWA) is of a size appropriate to the expected placement in cache (usually L1). The second consideration is to design BSeed and BGrease to populate the BWA with the intended structure, taking into account the intended grease code. It can easily happen that computing the greased vectors, which is done frequently, threatens to swamp the time taken for BwaMad, making an otherwise good scheme less attractive. Also, there is often a compromise to strike between leaving too much work to the BSeed routine versus increasing the size of the brick in Bfmt. After this, the job of converting writing DtoA, DtoB and CtoD are often fairly routine.

In addition to the public variables, there are eight compulsory private ones that must be supplied by hpmiset. These are AfmtMagic, BfmtMagic, CfmtMagic, SeedMagic, GreaseMagic and BwaMagic, which are used to decide which functions to exectute, and czer to hold the value to initialize a Cfmt matrix to zero (in Czer) and bzer to hold the value to initialize the BWA. There may also be tables (computed by tabmake.c) of which the current ones are

Thpv	To deal with Dfmt -> bit values for characteristics 3-13
Thpa	To assist with Afmt conversion - typically a grease code table
Thpb	To assist with Bfmt conversion
Thpc	To assist with Cfmt -> Dfmt conversion.

At present, these are only used in characteristic 3.

Section 3.2. Variables and tables set (in FIELD) by hpmiset

Firstly there are the six "Magic" numbers, used to switch the stated routine between various algorithms. These are described below

AfmtMagic	DtoA
BfmtMagic	DtoB
CfmtMagic	CtoD (and maybe later DtoC)
SeedMagic	BSeed
GreaseMagic	BGrease
BwaMagic	BwaMad

czer	The value put in all words of Cfmt to set it to zero
bzer	The value put in all words of the bwa to initialize it
bfmtcauldbytes	The number of bytes in a cauldron in Bfmt

Thpv
Thpa
Thpb
Thpc

So far, the only implemented versions are for characteristic 2 and 3. Nevertheless some generalizations can be seen, and these are described here.

Firstly the CZer function currently sets every word to be the czer value, and the BwaInit sets every word to the bzer value. There are currently no "Magic" values for either of these two routines, but in principle they may be needed later.

Section 3.3. DtoA

The overall control of this routine is provided by the AfmtMagic parameter in the FIELD structure

If AfmtMagic==1, further detail provided by the alcovebytes parameter, so that each block of Afmt is alcovebytes long, consisting of a 1-byte skip/terminator value and (alcovebytes-1) bytes of Dfmt data, except if all those bytes are zero it is treated as sparsity as described below ("Skip/Terminate).

If AfmtMagic==2, each block of Afmt is 8 bytes long, consisting of the skip/terminate byte and seven bytes produced by looking up a byte of Dfmt in the ??? table. If all seven input bytes are (Dfmt) zero, it is treated as sparsity as described below ("Skip/Terminate). Not yet written.

If AfmtMagic==3, at present it converts batches of 12 entries into one skip/terminate and three Afmt bytes converted for use in characteristic 3 only. This may need to be revisited and generalized later. It is currently fixed at 3 slices of grease level 4 with a particular layout of the BWA assumed. The Thpv and Thpa tables are used for this conversion.

The Skip/Terminate byte is used in all the above methods. Before each alcove of Afmt data (3 or 4 bytes) comes a byte that specifies how many zero alcoves have been skipped. This may take any value up to (and including) 250. If more than 250 zero alcoves are encounterend, 250 are skipped but then one is actually output as zero, thereby allowing another up-to-250 zero rows to be skipped. This byte takes the value 255 to indicate that there are no more (non-zero) rows, and the detection of this value terminates the BwaMad.

In principle there are no restrictions on the designer, apart from being able to give a reasonable maximum size in "alcovebytes". Sparsity detection is not compulsory.

Section 3.4. DtoB

The operation of this routine is controlled by the BftmMagic variable

If BfmtMagic==1 the Bfmt consists of Dfmt, with <alcove> rows of <bfmtcauld> bytes taken (with edge and bottom protection) from the input Dfmt matrix and put (starting at the second byte, leaving room for the sparsity indicator) into the Bfmt. If the Dfmt is entirely zero, the first byte is set to 0 and the length returned as 1. Otherwise the first byte is set to 1 and the length returned as 1 + alcove*bfmtcauld.

If BfmtMagic==3, A conversion specific for characteristic 3 is performed. This includes converting the matrix into the logic-6 bit-slice format using the Thpb look-up table to convert Dfmt bytes into logic-six-like format.

There is no function to convert Bfmt back into Dfmt.

The programmer should note the following when considering Bfmt.

1. There should usually be a fast-path for the case of a full-sized brick. Typically 95% of the calls to DtoB will be full-sized, so that tests for the exceptional smaller cases should ideally be excluded from the inner loops in the fast-path.

2. Nevertheless the routine must cater for the case of fewer rows, fewer columns or (typically 0.04% of the calls) both, padding out the resulting Bfmt with zero columns and/or rows to make the output brick of standard size.

3. Notice that the BSeed routine has an opportunity for further processing, so that Bfmt is truly a format private to the HPMI. Bfmt itself is chosen to do as much of the conversion work as possible, subject to not expanding the data size too much (for memory bandwidth reasons). Typically the BGrease does the computation of the extra rows needed for grease - it being faster to recompute them each time than to fetch them from memory.

4. In principle Bfmt can be chosen freely. In practice it is common to use the first byte as a flag (0 means the whole brick is zero, 1 means it is non-zero) to gain time when matrix B is very sparse.

5. If the number of columns (noc) does not specify an integral number of bytes, the DtoB routine may assume that the remainder of the last byte of Dfmt is zero. Hence, DtoB may only be called with noc not divisible by pentbyte at the right-hand end of the row.

Section 3.5. CtoD

The overall control of this routine is provided by the CfmtMagic parameter in the FIELD structure

If CfmtMagic==1, the data (typically dfmtcauld bytes long) is simply copied out of the bwa into the correct position in the Dfmt matrix.

If CfmtMagic==2, the data is extracted as uint16_t from the Cfmt, bar48 used to reduce it, and the data is then put as a uint8 into the receiving Dfmt.

If CfmtMagic==3, the Thpc table is used to convert from a logic-6 format back into Dfmt. This is specialized for characteristic 3 use.

Section 3.6. BSeed

The overall control of this routine is provided by the SeedMagic parameter in the FIELD structure

If SeedMagic==1, the vectors (depending on slots and slices) are put into the correct positions by loading as uint8_t and storing as uint16_t.

If SeedMagic==2, the vectors are memcpy'd into the correct positions in the BWA for characteristic 2 use, going to positions 1,2,4,8,17,18,20,24,33,34, . . .

If SeedMagic==3, the vectors are similarly memcpy'd into the correct positions for characteristic 3 use, namely 1,2,5,14,42,43,46,55,83,84,87,96

If SeedMagic==4, the vectors are converted from 8 bits to 10 bits, putting three in each 32-bit word. The cauldron must be divisible by 3.

Section 3.7. BGrease

The overall control of this routine is provided by the GreaseMagic parameter in the FIELD structure.

If GreaseMagic==1, the pcchain routine is used to make all the greased multiples.

If GreaseMagic==2, the pcxor routine is used to make all (8x11) further rows needed in the grease table for characteristic 2.

If GreaseMagic==3, the pcad3 routine is used to make all (3x36) further rows needed in the grease table for characteristic 3.

Section 3.8. BwaMad

At the very heart of the drive for performance in meataxe64 is the BwaMad routine.

void BwaMad(const FIELD *f, uint8_t * bwa, int sparsity, Afmt *af, Cfmt *c) to do C += A x B, where A is the <box> x <alcove> matrix encoded by the Afmt in af, B is the <alcove> x <cauldron> matrix held (and usually greased according to the sparsity value) in the brick work area bwa, and C is the <box> x <cauldron> Cfmt matrix at c. The values of <alcove> and <cauldron> are constants determined by the HPMI (and set by hpmiset into the FIELD structure) but the value of <box> can vary, though it often takes the recommended value <recbox> suitable for the processor.

In principle, the DtoB routine (convert to Bfmt) may inspect the brick and select a <sparsity> value suitable for that particular brick, allowing the BSeed and BGrease complete freedom as to how the bwa is populated. Notice that the Afmt and Cfmt cannot depend on the brick, so the scope here is limited. In practice, so far sparsity is either zero (brick is zero) or 1 (brick is non-zero).

The overall control of this routine is provided by the BwaMagic parameter in the FIELD structure.

If BwaMagic==1, the pcbmas routine (in pcrit) is used to perform the operation. Note that this needs the "parms" are to be correctly set up.

If BwaMagic==2, the pcbm2 routine (in pcrit) is called to perform the operation

If BwaMagic==3, the pcbm3 routine (in pcrit) is called to perform the operation.

Appendix 1 – Exact rules for noc.

DtoA. If the noc parameter is divisible by the number of entries in a byte (pentbyte) there is no difficulty. If it is not divisible, however, the remainder of columns in the last byte must be zero. This will be the case at the end of a row, but will not, in general, be true otherwise. Hence if it is required to convert partial rows into Afmt (not a common requirement) all partial rows except the last must consist of a number of columns divisible by pentbyte. This will anyway be needed so that the next part starts on a byte boundary. It would also be efficient if each part were an integral number of alcoves, so that no time is wasted adding in needless zero vectors.

DtoB. Again the noc parameter must either be divisible by the number if entries in a byte (pentbyte) or the remaining columns in the last byte must be zero. As a rule, all but the last brick will anyway be <cauldron> columns wide, and it is guaranteed that cauldron is divisible by pentbyte (in contrast to the situation in DtoA).

CtoD. Here there is no choice. The matrix given to CtoD must be a complete matrix, and DCut/DPaste used to make smaller matrices if this is required.

Appendix 2 – Characteristic 3.

In may ways, characteristic 3 is exceptional. In particular a block of Afmt is not an integral number of bytes of Dfmt, and the bit-slice nature of operations necessitates several features that are not needed in any other characteristic. In particular there are four look-up tables needed.

Thpv is a table to convert mod-3 Dfmt, with five entries per byte, into a 10-bit field with two bits per entry. The conversion is little-endian to little-endian, so that the "first" entry of the Dfmt ends up in the bottom two bits after lookup. Thpv consists of 243 16-bit integers. Its use is to enable

Thpa is used to convert into Afmt. It is a byte->byte table converting quadruples of numbers mod 3 in a format where each entry occupies 2 bits (as emergest from Thpv) into their position in the grease table . . . either 0 or and even number 2-80 being a vector whose first entry is 1, and the next being its negative. Hence the semantics is

0000 0000 0001 0002 0010 0020 0011 0022 0012 0021 0100 0200 0101 0202 . . .

but the table is the inverse - given the four-entry vector, where does it appear in this list. This table is very specific (at the moment anyway) to a grease level of four.

Thpb is used to convert from Dfmt into Bfmt. It is a table converting a five-entry Dfmt byte into a 64-bit field, where bottom five bits of the top 32-bits are 1 unless the corresponding entry is 1, and the bottom five bits are 1 unless the corresponding entry is 2. Bfmt can then be made by processing chunks of data five bits at a time.

Thpc is used to convert from Cfmt into Dfmt, and does the reverse computation, except that the input is only 10 bits long instead of 64.