Meataxe-64
Linear Functions.
Richard Parker 5.10.2017

Section 1 – Introduction

This is the documentation of the "linear forms" module linf. Its main use is to perform Albrecht-style expansion and liner forms to multiply matrices over an extension field. Not all extensions are currently implemented. At present, all quadratic extensions of the ground field, along with q=8 and q=16 are implemented.

It has only three functions, namely . . .

void linftab(FIELD * f) to check whether linear forms are available for this field. It sets f->linfscheme to 0 if they are not, and to 1 if they are available. If the field is a ground field, linfscheme is set to 0.

void LLMul(const FIELD *f,const Dfmt *a,const Dfmt *b,Dfmt *c,
        uint64_t nora,uint64_t noca, uint64_t nocb) to multiply a by b giving the answer c of the stated shape. It calls the PLMul function (in pmul) to do the multiplications over the ground field.

void CExtract(DSPACE * dq, const Dfmt *mq, uint64_t nor, Dfmt *mp) to convert the given extension field matrix into a collection of matrices suitable for conversion into Cfmt. I don't think this routine has been tested yet, as it is only needed for slab echelize, which has not yet been written.

Section 2 – Extension field matrix multiplication.

The first stage is to run the "extract" subroutine of linf to extract all the correct linear forms ready to multiply. Then PLMul is called to multiply the matrices pairwise, and finally the assemble routine is called to compute the appropriate linear forms and make the resulting extension field matrix.

The extract routine works one row at a time, even though PExtract can do multiple rows. I believe this is better, since it is more cache-friendly. The target size of a matrix in "slab" (which is the main - indeed currently only - place it is used) is for matrices where a row is around 8 kilobytes. I have not experimented to check, however. Its job is to take a matrix over an extension field of order q = pd and producing d matrices over the ground field, being the coefficients of 1, x, x2 etc. in the original matrix, and then to use "runlf" (again one row at a time) to compute the extra linear functions.

The assemble routine takes the output matrices and runs another set of linear functions using runlf to produce the d matrices (q=pd) needed, after which PAssemble is used, all one row at a time, to produce the final rows in Dfmt over the extension field.

The runlf routine is therefore the heart of this module. It takes an input program and interprets it. I can't help feeling that this process would be faster done more rows at a time, though the job of keeping it cache-friendly will make this a bit of a compromise, and as these routines are anyway a fairly small part of the run-time, its probably not of high priority. Nevertheless this should at least be checked by doing some profiling.

The interpreted programs, which all appear at the top of the linf source, have the following structure. All operands are a single uint8_t. Further instructions can readily be added to this system as it develops. If the tables get too large, they should probably be cut out into a separate file, or indeed generated at field-set time.

"opcode" parameters	meaning
      0	stop
      1	m1	m2	copy m1 to m2
      2	m1	m2	m3	m3=m1+m2
      3	m1	m2	m3	m3=m1−m2
      4	m1	m2	m2 = m2 + α.m1
      5	m1	m2	m2 = m2 + (β−1).m1
      6	λ	m1	m1 = λ.m1
      7	λ	m1	m2	m2 = m2 + λ.m1
      8	m1	m1 = 0

α is the last coefficient in the Conway polyomial written as xd = <higher terms> + α. Hence for odd degree it is the smallest primitive root, and for even degree it is the negative of the smallest primitive root.
Similarly β is the coefficient of x. In the case of quadratic extensions of the ground field (the only case that uses these so far) the Conway polynomial is x2 = β.x + α, or x2 − β.x − α.

There are three sorts of program, called A, C and Z. The A-programs are used to extract for the purposes of multiplication, and the C programs to reassemble the results to enable the extension field answer to be computed. The Z-programs are for future use in slab echelize to convert Dfmt into Cfmt. It should be noticed that these are not obviously available from the other two.

It should also be noticed that the same linear forms program is used for both A and B - the system is symmetric. Should I become aware of an asymmetric system that needs fewer matrix multiplications over the ground field, it would not be to hard to change the program to use it, but I am not aware of any such case, and it seems better to stick with symmetric forms until the need actually arises. In any case, I expect the vast majority to be symmetric.

Section 3 – Theory.

It is a very difficult research project to find, for each extension field, the minimum number N of matrices that must be multiplied over the ground field in order to determine the product of extension field matrices. The problem is equivalent to finding two sets of vectors Vi and Wi in d dimensions whose tensors Ti span a particular d-dimensional subspace consisting, in some sense, of the coefficients of the product. Except for small cases, however, there are far too many sets of vectors to try them all.

The first assumption (as mentioned above) is that in all known cases (as far as I know, anyway) the minimum known N can be achieved with a symmetric system - i.e. Vi = Wi for all i. This assumption is made in meataxe64, though it could readily be removed if the need arose.

A second assumption often made is that the space is not just sufficient to compute the product, it is in fact sufficient to compute the product of the polynomials.

There is a method (called interpolation) that finds the best solution provided d ≤ 1 + p/2. This uses the vectors V∞ = [0,0,...,1] and Vx = [1,x,x2,...], and provided enough different x can be found, the tensors span all reverse-diagonal matrices and hence satisfy both assumptions and enable a system to be found. It is a theorem that, if d ≤ 1 + p/2 then N=2d-1 and this method cannot be beaten.

An extension of this idea, for use when the ground field is too small (otherwise said - the degree too large) is to use interpolation over an extension field, using already known methods to multiply in that extension field. There is no theorem that this provides the best solution, and indeed for q=16 it gives a system with 10 multiplications whereas in fact it can be done in 9 (using an iterated Karatsuba). Nevertheless it does give very good methods in the majority of cases, and the search space is now so small that it can be investigated exhaustively.

Section 4 – The alb program.

I found it quite a slog to find the linear forms needed to make the answer from the tensors, and wrote a little program to assist. I called it alb.c (Albrecht) and its purpose it to check that a given set of tensors spans the space needed to generate the product, and then to compute the program, ready for putting is as a "C" type program into linf.c.

The key routine is mkprog, which starts off with the matrix that it needs to reduce to the identity on the first rows and zero on the rest. It tries to do this with the minimum number of steps. It considers various "moves" that try to improve things.

The first move it considers is when the first entry of a row is in the correct position for the identity, but it isn't 1. In this case the move is to scale it, but it gives a very low value to this move . . . nor - i, making it the least valuable move.

The second move it considers is to add a multiple of row j into row i when row j has its first entry in the i'th column and row i is zero up to and including that column. In that case suggests adding a multiple of the j'th row into row i so that the first non-zero entry of row i is in the i'th column and is 1. This gets a value of 10000-i (very high).

The third move it considers is to add row j into row i when j has its first entry later than row i does, and the top entry of row i is already 1 and all the entries in between are zero. In that case it counts the number of extra zeros it has made, counting roughly 3000 for each.

The final move it considers is when i and j start at the same position. In that case it considers adding a scalar multiple of row j to row i .