Meataxe-64
Pcrit.
Richard Parker 5.11.2017

Section 1 – Introduction

The pcrit routines of meataxe64 are a collection of functions which are either worth implementing in assembler for performance reasons, or need to know things about the technology to set things up correctly.

There are currently four implementations of pcrit.

HAS for x86-chips with AVX-2, designed to run on Haswell and later. This is also the correct version to use on the Ryzen chip, though I suspect that a new ZEN version should really be produced and optimized for this.
NEH is for x86-chips predating Haswell. It uses SSE-2 for vectorized work and has HPMI for characteristics 2 and 3 also, where it is approximately a factor of two slower than HAS.
GEN is a “c” implementation. It is currently lagging behind a bit, but could be brought back with a day or two’s work and a lot of testing.
PIL is for the AMD Piledriver chip (the St. Andrew’s lovelace and babbage), where the NEH code was changed specifically to allow for the shared decode, which proved a bottleneck for HPMI. It was therefore re-coded to have fewer instructions. There are no long-term plans to maintain this version at present.

Future versions expected include ZEN for the AMD Ryzen chip, and V64 to make use of AVX-512. Neither project has been started as of today (21.9.17).

Section 2 – AS primes routines.

There are two routines specifically produced to service the primes that are done in the HPMI using AS-type codes - pcchain and pcbmas. The pcchain routine is designed to compute addition chains as a subroutine to BGrease, and is designed for considerably more general cases than pcbmas, which is probably limited to primes less than 181.

Both routines take an array, normally living in the FIELD structure, containing a collection of necessary uint64_t values, and a pointer to this array (called parms) is passed to both of them. The elements of the parms array are . . .

parms[0]	The characteristic of the field - equal to f->charc.
parms[1]	A shift value S. This is used in both routines, and in different ways.
The more stringent requrement comes from pcbmas, where it must be the
shift needed to convert the masked value into the units position. In the
case of pcchain, it needs to be a shift within the bit-length of the values,
and such that 2S > characteristic.
parms[2]	The mask used in pcbmas. This must have all the bits set within the bit-
length of the values from 2S upwards. For pcchain, all that is needed is
that the 2S bit is set, and all lower bits unset.
parms[3]	2S − p. This is used only in pcchain, and is added to a value so that the
2S bit is set if and only if the value was p or greater.
parms[4]	cfmtcauld - the number of bytes in a cauldron in Cfmt. At present this
value must be 128 for both routines.
parms[5]	Slots - the number of code words for each slice. This value may be
larger than the actual number of code words - it is used to determine
where the next slice starts.
parms[6]	Slices. At present this is not used by pcbmas as it is assumed to be 7.
It should be set to 7 for future compatibility. It is used in pcchain and
must be correctly set for that routine.
parms[7]	2S % p. This is the multiplier, used only in pcbmas, to convert the
shifted masked bits into the number to add on to the lower bits.
parms[8]	Bias. This is the

void pcchain(uint8_t * prog, uint8_t bwa, uint64_t * parms) to compute the addition chain as specified in the program prog. Many of the details needed are in the parms routine, which is constant for any given field (as is the prog, as a rule!).

The central idea is to interpret the string of bytes (in prog) as a set of instructions to compute the chain by adding two already computed multiples and then reducing modulo the prime.

The byte-code.
At the start of interpreting a byte, the following state is held.
The accumulator - a cauldron, held in vector registers.
The destination slot.

At the start, the accumulator is loaded with slot number 1 (which is always seeded by BSeed) and the destination slot set to 2.

The interpretation of the prog bytes is given below.

0-79 add the slot of that number into the accumulator, store the result in the destination slot, and increment the destination slot. For star chains, or for parts of the computation that can be done by a star chain, these (and stop!) are the only codes needed, and they are expected to form the commonest instructions by some margin.
80-159 load the accumulator from the slot number 80 less than the byte-code.
160-239 set the destination slot to be 160 less than the byte code
240-254 Unused and reserved for future use.
255 stop - the program has completed.

As an example, take P=71
Slot	0 1 2 3 4 5 6 7 8 9 4 7
AS-code	0 1 2 3 [4] 8 12 [14] 24 25 39 53
byte-code	1 1 1 4 4 2 86 6 1 164 7 167 7 255

Reduction (of a number known to be less than 2p) is done by the following method. Bear in mind that all these operations are done to 64-bit chunks that may well contain more than one entry each.

Firstly a number 2S−p (provided in the parameters) is added, where S is chosen so that 2S > p. The result has the 2S bit set if and only if the result was p or larger.
Secondly a logical 'and' is done with 2S to keep this bit only. higher bits may be set in the mask, as they will not be set in the value after 2S−p has been added.
This bit (1 if reduction required, 0 if not) is then shifted into the units position (the original is retained as well.
The the shifted bit is subtracted from the unshifted bit to make a number that is either all 1 (if subtraction of p is wanted) or all zero otherwise.
A logical AND is then done between p and this result. This is then p if subtraction is required and 0 otherwise.
All that remains is to subtract this value from the original one.

void pcbmas(uint8_t *a, uint8_t * bv, uint8_t *c, uint64_t * parms)
Parameter a is the Afmt, which is a string of bytes treated as a string of uint64_t internally to pcbmas. Parameter bv is the brick work area, and parameter c is the Cfmt area to be added into. parms is as described above, containing the information, constant for the field, needed to perform the operation.

Section 3 – Characteristic 2 DSMad assistance.

void pccl32 ( uint64_t * clpm, uint64_t scalar, uint64_t noc,
        uint32_t * d1, uint32_t * d2)

does a multiply-and-add of the vector at d1 by scalar into the vector at d2, noc values long. The scalar is left-justified, so that the X^(d-1) term is the most significant bit.

The parameters must be

clpm[0] e = X2d / p left-justified, with X^d (not d-1) the most significant bit.
clpm[1] p (including Xd term) left justified - X^d (not d-1) the most significant bit.
clpm[2] shift = 64 - degree

------ end of editing - - - - all the rest is unchecked and probably useless -----

Section 2 – Specifications of pcrit routines.

uint64_t pcpmad ( uint64_t p , uint64_t a , uint64_t b uint64_t c) to multiply a by b, add c, and reduce mod p. This uses the 128 / 64 division routine to reduce modulo p, and needs no preparation. It is used for the largest primes that meataxe64 is designed for, and can take around 70 clock cycles (20 nSec) in these cases. To multiply-and-subtract, just give p-c instead of c, which works in all cases.

extern uint64_t pcpmul(uint64_t p,uint64_t a,uint64_t b);
extern void pcxor(Dfmt * d, const Dfmt * s1, const Dfmt * s2, int nob);
extern void pcbif(Dfmt * d, const Dfmt * s1, const Dfmt * s2,
        uint64_t nob, const uint8 * t);
extern void pchset(HPMI * hp, const FIELD * f);
extern uint64 pcinfocauld(uint64 fdef);
void pcbm2(const uint8 *a, uint8 * bv, uint8 *c);
void pcad3(const uint8 *a, const uint8 *b, uint8 * c);
void pcbm3(const uint8 *a, uint8 * bv, uint8 *c);

// void pcb64p(uint64_t q,uint64_t * dd);
// uint64_t pcb64(uint64_t a, uint64_t m);
// void pcb128p(uint64_t q,uint64_t * dd);
// uint64_t pcb128(uint64_t a,uint64_t m1,uint64_t m2);
//

void pcxor(Dfmt * d, const Dfmt * s1, const Dfmt * s2, int nob) to perform an exclusive-or of a string of data d = s1 ^ s2 of length 'nob' bytes. The implementation uses vectorization where possible, and is tuned for cases where nob is fairly large but not divisible by a large power of two, and the areas are not assumed to be aligned in any way - MOVDQU is the key instruction used in pcrit1. pcxor is used from the FIELD routines DAdd and DSub, and indirectly from DSMad, but will not be part of the main performance-critical multiply routine in characteristic 2, which will use further routines that are not yet specified.

void pcbif(Dfmt * d,const Dfmt * s1,const Dfmt * s2, int nob,const uint8 * t,int m) to apply the binary function t to the bytes of s1 and s2, and put the resulting looked-up byte into d, with nob bytes being processed. If a1 is the byte fetched from an s1 location, and a2 comes from s2, the byte placed in d is t[a1*m+a2]. So far I have seen no way to use vectorization, and the performance of this, although the best I can manage, is not that great. It is used primarily for adding and subtracting in odd characteristics where there is more than one entry in each byte.

extern void pchal(int * gen, int * subgen);
extern void hpmiset(FIELD * f);
extern uint64_t pcstride(uint64_t s);
extern uint64_t pcpmad(uint64_t p,uint64_t a,uint64_t b,uint64_t c);
extern void pcxor(Dfmt * d, const Dfmt * s1, const Dfmt * s2, uint64_t nob);
extern void pcbif(Dfmt * d, const Dfmt * s1, const Dfmt * s2,
        uint64_t nob, const uint8_t * t2);
extern void pcbunf(Dfmt * d, const Dfmt * s, uint64_t nob,
        const uint8_t * t1, const uint8_t * t2);
extern void pcxunf(Dfmt * d, const Dfmt * s, uint64_t nob,
        const uint8_t * t1);
extern void pcunf(Dfmt * d, uint64_t nob, const uint8_t * t1);

void pcbm2(const uint8_t *a, uint8_t * bv, uint8_t *c);
void pcad3(const uint8_t *a, const uint8_t *b, uint8_t * c);
void pcbm3(const uint8_t *a, uint8_t * bv, uint8_t *c);