Meataxe-64
HPMI based on PMULUDQ.
Richard Parker 23.10.2017

Section 1 – Introduction

This document is a fairly serious attempt to specify an HPMI implementation based on the pmuludq instruction. This vector instruction (AVX-2) multiplies four pairs of 32-bit numbers to produce a 64-bit result, and by accumulating these, and doing occasional adequate reduction, an implementation good up to about 28-bit primes, executing about four elementary operations per clock on AVX-2, should be possible.

More specifically, the BwaMad routine multiplies two 64x64 matrices of 32-bit numbers, adding the result into a 64x64 result matrix. Much of the general scheme is now clear, but the following issues remain outstanding.

- It is best to store the result in 64-bit integers (thereby saving the time to reduce the result down to 32-bits) or is it better to perform this reduction (thereby saving the memory bandwidth and cache-space).
- It it possible to take advantage of sparsity (large blocks of zeros in A or B or both) to reduce the amount of work to be done without too much loss of time recovering from mispredicted branches.

This latter question is of fundamental importance to the design, and must be resolved before things can progress much further.

Section 2 – Sparsity in matrix A.

In the case of smaller primes, there is a "skip/terminate" byte used to increment the C-pointer and to tell when the block is completed. The expected organization of this HPMI implementation is different, in that the same block of C is used for a large number of A-blocks, so the skip/terminate must be added to the "B" pointer, not the "C" one. Nevertheless it seems that (with this change incorporated) the same sort of trick is available, with the unpredictable branch at the end of the string only. Let's look at this in a bit more detail.

The block multiply taking place (in AVX-2 anyway) is of a 4x2 block of A, times a 2x8 block of B adding into a 4x8 block of C. The next block will be the next 4x2 block of A (to the right of the previous one) times the next 2x8 block of B adding into the same 4x8 block of C. Hence if the A-block is zero, we can skip some B-blocks.

This implies that, for the expected type of Aftm, the shape of the A-block (4x2) is fixed, and different technologies (NEH, CAN) would only be able to vary the number of columns of the block of B/C (the number 8 in the previous description).

Hence we begin to see that Afmt can usefully be a skip/terminate byte (or word if we want to keep things aligned) followed by the next non-zero 4x2 block.

As a block multiply is 4x2 X 2x8 -> 4x8, this is about 16 clocks, and there would be 32 of these along the row. This is only about 500 clocks, so the misprediction of the branch is about 4% - within the acceptable range, but only just. It would be preferable if the rows of A were a bit longer.

Another annoying feature is that, in the HPMI spec as it is at present, the Afmt must be able to handle an arbitrary number of rows. NZ0 is allowed to take any integral value, so that we must somehow be able to manage fewer than four rows of A/C without reading or writing outside the area of Cfmt.

Section 3 – Sparsity in matrix B.

The sparsity of matrix B can be used to some extent. We may prefix a complete column of B (of 2x8 blocks, hence a 64x8 block in all) by a skip/terminate word specifying how many blocks of C (also 64x8) to skip.

Section 4 – BwaMad.

As always, we start the design process with the BwaMad routine. Our aim is that the very core of the loop consists of a PMULUDQ instruction (P0, latency 5, reciprocal throughput 1 on Haswell) and a PADDQ (P15 latency 1, reciprocal throughput 0.1) to accumulate the results. As the PMULUDQ instruction actually takes 32-bit inputs suitably spaced out, we must consider whether the Afmt is 32-bit or 64-bit, whether the BWA has 32 or 64-bit values, and whether we are going to reduce the result sufficiently to store Cfmt in 32-bits at the end. As grease is not in use, there is the opportunity to use the many AVX (or SSE) registers to avoid many of the loads, so that once a register is loaded it is used several times. Yet a further question is whether a single PMULUDQ is pertaining to one or many entries for matrix C. We are clearly going to need to answer these questions before we can get much further, and the choice between them seems like a well-defined question - for which method does BwaMad run fastest?

We probably also want to look ahead to Skylake (where PMULUDQ is P01 latency 5 reciprocal throughput 0.5 and PADDQ is P015 latency 1 reciprocal throughput 0.33) and AVX-512 (with 512-bit registers, and 32 of them) as these are substantial differences, making the i9 a very good target for this system.

Section 5 – First Shot - a Straw Man.

Assume

- the BWA is a 64x64 array of 32-bit numbers.
- Afmt is also a list of 32-bit numbers
- Cfmt is a list of 32 or 64-bit numbers
- We duplicate an A-entry across the vector register

We can use every load three times (so perhaps we work with 63x63 matrices!)
This needs nine registers for C, three for B and one for A.

111 112 113 211 212 213 311 312 313

This needs 12 bytes of Afmt and is doing nine multiplies and nine additions. We'd probably like to keep the Afmt in cache, so it makes sense to do something like a 63x63x63, with matrices 16+16+32K (fitting easily into L2).

So . . . how do we get 4 bytes of matrix A into alternate positions in the registers? It looks like the answer is going to depend on whether we are using AVX-2.

With AVX-2 there are several options.

The fastest is probably to use VPBROADCASTQ straight from memory (P23, latency 5, reciprocal throughput 0.5), but this requires Afmt to be 64-bits, which may be an issue for cache-usage and memory bandwidth.
Another idea is to use VPERMQ (P5 latency 1 reciprocal throughput 1) to fetch any one of four words at 64-bit length from an already loaded register containing four of them. This register could be loaded using VPMOVZXDQ (P5 latency 1 reciprocal throughput 1) to get four of them from 32-bit Afmt.

With SSE, PSHUFD (P05, latency 1 reciprocal throughput 0.5) can be used much like the VPERMQ, and the PMOVZXDQ (P05, latency 1 but reciprocal throughput 1).

Another issue is that we'd ideally like to keep the data for adequate reduction in registers. In pcbmas there are four of these - shift, mask, bias and 2^S % p - but if we want to use the 3x3 method, this uses 9 for C, 3 for B, 1 for A and 1 for the result of each multiplication making 14 so far, and there are therefore only two left. However, we are only adding, not subtracting, so there is no need for a bias, and the PSRLQ instruction actually saves a mu-op and a register, but requires the shift to be constant (which is probably OK). We therefore need to choose a global shift (and hence also mask) that allows the prime to be as large as possible, but we first need to know how often we are performing adequate reduction. Nevertheless it seems clear that we can hold the mask in one spare register and 2^s % p in the other one, fully utilizing all 16 registers. Hopefully the need for another one won't arise!

Let's now get a first feel for the memory access requirements. A 64x64x64 is (AVX-2) doing 216 vpmuludq instructions and needs to access at most 64K, or 64 multiples per cache-line.

Section 6 – Partial blocks in Afmt.

At present, the HPMI specifies that the Afmt for a column of nor alcoves shall occupy at most 1+nor*alcovebytes of space, and this is not very suitable for a design where rows are put into blocks of four. We must clearly have alcovebytes to be at least nine, as each 4x2 block needs at least 33 bytes - 32 bytes for the data plus one for skip/terminate - so that an alcovebytes of 8 is not enough. I think we need to specify four different terminate bytes, depending on whether the last block is 3, 2, 1 or 0 rows long. Hence the DtoA and also the BwaMad need to handle these tricky end-of-matrix cases. Let's check to see if there is an alternative. The "natural" way to do Afmt would be to have each alcove being from a single row. That way we would have to load the chunk of matrix B for every row of A, so that the minimal core operation would increase from (say) 2.5 mu-ops to 3 mu-ops, being P23, P0 and P15 on Haswell. We could readily increase the number of registers of B/C done for each piece of A, but the result would be something like 1/8 + 1/1 rather than 1/4 + 1/2 (or even 1/3 + 1/3). This would not be terrible, but it would be nice to know how to do better. Suppose we tried to process two rows of Afmt at once? No . . . I can't see how to do that.

In any case, our objective is to do as much work as possible at Afmt conversion time, and if we want (as we ideally do) to have Afmt as a collection of 4x2 blocks, we can rely on the misaligned efficiency of modern chips and have the four terminate-byte values done properly - 255 means end, 254 means one row then end, 253 2 rows and 252 three rows.

A more serious problem is that the data is in the wrong order!