Meataxe-64 Use of Barrett.
Richard Parker 12.8.2016

Section 1 – Introduction

Elements in Dfmt for the field of order q = pd are held in the form of a single integer, where a0 + a1x + a2x2 . . . ad-1xd-1 (modulo the Conway polynomial) is represented by

a0 + a1p + a2p2 + . . . + ad-1pd-1

In several places in meataxe64, there is a need to extract the coefficients ai from this integer. This is needed in the basic “four functions” calculations in the FIELD module, but also (under performance pressure) when using the Albrecht methods for matrix multiplication. This document looks at how the Barrett technique can be used to do this at fairly high performance.

More specifically, we are given an integer x = d.a + b where d is known in advance (i.e. we will use it for many x in turn), and where b < d. Our task is then, as fast as possible, to compute a and b given x. I am assuming thoughout this document that we are working on an x86-based machine no earlier than core-2, and working in 64-bit mode.

The simple-minded approach is to use the divide instruction. If we divide x by d, the result is a quotient of a and a remainder of b. In “c”, I’m not clear how this can be done with a single divide, even though the machine code does provide both quotient and remainder, but this issue is probably not worth considering since the divide instruction is anyway so slow that the “divide” method is never going to be the fastest solution.

The same problem occurs in a wider setting. For example if one needs an array of 21-byte structures, access would be faster if three were put into each 64-byte cache line, wasting one byte every three structures. Given an index x into this array, we need to extract a and b from x = 3.a + b whence 64.a+21b will be the location of the element whose index is x. Division by 3 is not the performance answer!

I will describe the Barrett technique first for the “N = 64” bit case. We compute from d the quantity K = 264/d rounded up to the next integer. Given x, we then compute (as a 128-bit number) x.K. The hope is that the top 64 bits is indeed a, and we can then compute b as x – a*d. This is reasonable since K = 264/d + e with e < 1 we have, in exact real numbers . . .

x.K/264 = (d.a+b)(264/d + e)/264 = (d.a+b)(1/d + e/264) = a + b/d + (d.a+b).e/264.

The key question for this document is to bound the error in the above equation, and in particular to determine conditions when it is certain to be less than 1. Of course the term b/d is bounded by (d–1)/d and as we are interested in certainty, we might as well assume that b=d–1 since that will be the worst case. The other term may be better described as x.e/264 – so we see that the maximum value of x that we wish to process is entering into the calculation also. The third component is ‘e’, which measures the rounding up that was done. If 264/d is close to, but less than an integer, e will be small and the range correspondingly greater. Hence the simple-minded computation assumes e=1 and works out from this when the computation obviously works. There will then be a range where the exact value of e matters, so that some d work even though some slightly smaller d do not.

If we assume (pessimistically) that e = 1 and b=d–1, and taking A = max(a)+1 the condition becomes d2A<264, which is a sufficient condition for the method to get a exactly right every time. This can be seen by taking 264[ b/d + (d.a+b).e/264] <=
264[(d–1)/d+d.A/264] <= 264[(1–1/d)+d.A/264] <= 264 – 264/d + d.A and we see that
264 > 264 – 264/d + d.A <=> d.A < 264/d <=> d2A < 264.

Let’s prove . . .
Theorem.
If d2A < 264, then b/d + (d.a+b).e/264 < 1.
Proof.
b/d <= (d–1)d and (d.a+b).e/264 < dA/264 = d2A/(d.264) < 1/d
hence b/d + (d.a+b).e/264 < (d–1)d + 1/d = 1.

Section 2 – The 64-bit case.

There seems little point in computing cases less than 64 bits, since the multiply instruction 64 x 64 → 128 is basically no slower than shorter ones on any current chip.

chip	64 x 64 → 128 / mu-op lat’y t’put	64 x 32 → 64 / mu-op lat’y t’put
Core-2 Merom	3 7 4
Core-2 Wolfdale	3 7 4
Nehalem	3 3 2
Sandy Bridge	2 3 1
Ivy Bridge	2 3 1
Haswell	2 3 1
Broadwell	2 3 1
Skylake	2 3 1

sadfsdfds