Meataxe-64
Field and HPMI structure.
Richard Parker 21.7.2014

Section 1 – Introduction

The "field" module is often used in its ancient and well-understood way of dealing with field elements and vectors for the purposes of meataxe64, usually at tolerable but not excellent performance. Before these functions can be used, the FieldSet routine must be called to set up all the data structures and look-up tables needed to perform these functions.

In fact, the operation of the FieldSet routine is considerably wider than this, and the data structures and look-up tables are defined and available for other functions to use. One purpose of this document is to describe the syntax, semantics and usage of the resulting FIELD * data.

Moreover there is an additional structure (HPMI) which contains a wealth of information about the matrices being worked on, which is set by a call to the hpmiset routine. This in turn calls the pchset routine, so that the HPMI variables are set with a knowledge of the underlying technology.

================ end of new pass of editing =====================

It is not intended that the "field" structure be accessed directly except from "c". The data items (and particularly some of the look-up tables) however may well be passed to assembler subroutines, and hence these are defined "to wire level". In these cases, the usage may sometimes be limited to the x86.

Section 2 – The individual data items.

uint64 fdef Field definition. An unsigned integer giving the order of the field. This must be a prime power, and must be less than 264.
uint64 charc Characteristic. This is the prime that fdef is the power of.
uint64 pow Power, or degree. fdef = charcpow. The degree of the field extension over the ground field.
uint64 conp Conway polynomial. Xpow = conp. For prime fields, this is the smallest primitive root. It is a heroic fact that this is always correct.
uint64 qstep charc(pow-1). Used internally in the field module to do arithmetic on FELT objects (in extension fields).
uint64 dbytevals The number of different values that can occur in a byte. This field is only defined for fields of order up to 256 - where each byte consists of one or more field elements.

Section 3 – The Look-Up tables.

The look-up tables start a number of bytes up on the start of the FIELD structure indicated in the relevant variable. Hence, for example, the 16-bit antilogarithm table Talog16 can be found as . . .
    uint16 Talog16;
    . . . .
    Talog16 = (uint16 *) ((uint8 *)f + f->Talog16);

Tadd8 Byte addition table. This table is populated only for fields of odd characteristic and order less than 256. In position X.(f->dbytevals) + Y is the byte for X+Y, however many entries this may contain. TBD Ultimately this should be changed so that it handles addition in the prime field - i.e. it is the add8 table for the prime field whenever the characteristic is small, not the field order. Also there is a lot to be said for populating it even if the characteristic is two, just for uniformity.

As there seems to be no obvious place in the documentation to note the meanings of Afmt in characteristic 3, they are noted here. The even numbered Afmt are give here. The negatives of the vectors given are the odd numbers one higher, so that, for example 69 is 2101, the negative of ( 68 1202 )

  0 0000	12 0101	24 0121	36 1011	48 1101	60 1121	72 1211
  2 0001	14 0102	26 0122	38 1012	50 1102	62 1122	74 1212
  4 0010	16 0110	28 1000	40 1020	52 1110	64 1200	76 1220
  6 0011	18 0111	30 1001	42 1021	54 1111	66 1201	78 1221
  8 0012	20 0112	32 1002	44 1022	56 1112	68 1202	80 1222
10 0100	22 0120	34 1010	46 1100	58 1120	70 1210

Thpv A table to convert Dfmt into a form where each entry is in a separate bit field, so that it can be more readily manipulated.
char = 3	Each of the 243 possible Dfmt bytes gives a 16-bit word where the bottom
uint16	ten bits consists of five two-bit fields with the natural, binary meaning.

Thpa A table to assist in the production of Afmt.
char = 3	The input index consists of four two-bit fields with the natural, binary
uint8	meaning, giving the Afmt byte for that four-vector.

Thpb A table to assist the conversion from Dfmt to Bfmt.
char = 3	Each of the 243 possible Dfmt bytes gives a 64-bit word in the format
uint64	27 zeros, five bits U, 27 zeros, five bits T. The two five-bit fields together
give the Bfmt for the five entries in the Dfmt byte. Hence several Dfmt
bytes can be converted by looking them up, shifting them and adding them
(or OR or XOR) to make longer strings of Bftm.
Thpc A table to assist the conversion from Cfmt back into Dfmt.
char = 3	The index consists of a ten-bit field, where the first five bits are the U-bit	uint8	and the second five bits are the T bit. The result is the Dfmt byte whose
value is the same as the one given by the five Bfmt bit-pairs. If the index
does not correspond to a valid set of bit-pairs (i.e. one or more has zero in
both bit positions) the result is 243, which is not a valid Dfmt byte. It is not
expected that code tests this unless it is a genuine possibility.