Meataxe-64
Proggy Documentation.
Richard Parker 3.7.2014

Section 1 – Introduction

In meataxe64, a "proggy" is a routine that is designed to be called via the thread-farm. There are two types - "constitutive" and "dataflow" proggies. It is intended that the proggies and the top-level programs that use them be as independent as possible, so that the programmer in charge of the top-level program can use them without reference to how they are implemented. Indeed initially the proggies will be implemented in a relatively simple but inefficient way (using FIELD and Dfmt) and only later will faster versions of some of them, based on the HPMI, become available.

Section 2 – Some preliminary concepts.

The basic idea top-level program must break the problem down into smaller sub-problems, each of which can be performed by a proggy. In practice, good design of a top-level program is often a compromise between memory footprint and load-balancing.

To assist with this, the idea is to use the "Dijkstra P/V" mechanism, also known as a counting semeaphore. At present, the only application of this is that the reading of rows can be made to wait for the writing of rows. It is clear that this will need to be expanded in future.

Section 3 – Moj structures.

Dfmt Moj. This consists of two uint64 integers giving the number of rows an the number of columns. After these 16 bytes, the Dfmt data follows immediately.

Field Moj. This consists entirely of the FIELD data structure.

BitString Moj. This consists of two uint64 integers (total number of bits, and number of set bits) followed by as many 64-bit words as needed to hold the total number of bits.

Section 5 – Detail of the constitutive proggies.

MxRead(char * fname, int fdmoj, int firstmoj, int H int V, int PV) to read a matrix from the given filename, into H rows of V blocks of mojes, starting at firstmoj. A populated field moj must be provided. If the PV value is zero, reading proceeds at full speed. Otherwise it relies on that Dijkstra P-ing and V-ing value being somehow V-d, usually by MxWrite.

MxWrite(char * fname, int fdmoj, int nor, int noc, int firstmoj, int H int V, int PV) to write the matrix to the given filename, which will ultimately be nor x noc matrix (since this information must go into the header). As with the read, the matrix is provided as a contiguous set of moj numbers, being H rows of V blocks of mojes, starting at firstmoj. A populated field moj must be provided. If the PV value is zero, no Dijkstra PV variable is altered. Otherwise it V-s the given PV variable allowing one other constitutive proggy (usually the read) to proceed in tandem.

Section 4 – Detail of the dataflow proggies.

So far there are only three dataflow proggies implemented.

1 MUL. A dataflow proggy for matrix multiplication. This proggy has four moj parameters
Field	f	The field structure in use
Dfmt	A	Matrix A in Dfmt
Dfmt B	Matrix B in Dfmt
Dfmt C	The result matrix, in Dfmt, C = A x B

2 MAD. A dataflow proggy for combined matrix multiplication and addition, so computing D = C + A.B. This proggy has five moj parameters
Field	f	The field structure in use
Dfmt	A	Matrix A in Dfmt
Dfmt B	Matrix B in Dfmt
Dfmt C	Matrix C in Dfmt
Dfmt D	The result matrix D = C + (A x B)

The MAD routine is not expected to be faster than a multiply followed by an add, but the difference is that matrix C is a dependency before MAD can start, which may be preferable to control the memory footprint.

Suppose we wish to compute P.Q + R.S. Doing two multiplies and one add, the two multiplies will start immediately, and the add will run when both multiplies have completed. Using MUL then MAD, only the first multiply can run, and the MAD will only start when the MUL has completed.

Suppose we do a multiply chopped 20x20. Using MUL and ADD, it would be permissible to start all 8,000 multiplies at once, but using MAD this can be reduced to 400.

9 ADD. A dataflow proggy for matrix addition. This proggy has four moj parameters
Field	f	The field structure in use
Dfmt	A	Matrix A in Dfmt
Dfmt B	Matrix B in Dfmt
Dfmt C	The result matrix, in Dfmt, C = A + B

Section 5 – Detail of dataflow proggies for Gaussian.

3 ECH. Echelize. This proggie has six moj parameters
Field	f	The field structure in use
Dfmt H	The input matrix H
BitString R	The Row-select bit string for the row basis of H used
BitString C	The Column-select bit string for the column basis of H used
Dfmt X	The left multiplier that puts the selected rows into echelon form
Dfmt T	The remnant - the non-selected columns of the selected rows.

4 CEX. Column (pivot) extract. Parameters
Field	f	The field structure in use
BitString C	The Column select bit string
Dfmt M	Matrix M in Dfmt
Dfmt M1	Matrix M1 of selected columns in Dfmt
Dfmt M0	Matrix M0 of non-selected columns in Dfmt
Initially this will probably proceed using DPak and DUnpak, but a faster version should eventually be produced that works via DCut and DPaste, speeding up the common case where fairly long strings of columns go to the same output.

5 REX. Row extract. This proggie has five moj parameters
Field	f	The field structure in use
BitString R	The Row-select bit string
Dfmt M	Matrix M
Dfmt M1	Matrix M1 of selected rows in Dfmt
Dfmt M0	Matrix M0 of non-selected rows in Dfmt

6 RRF. Row riffle. Parameters
Field	f	The field structure in use
BitString R	The Row-select bit string
Dfmt M1	Matrix M1 of the rows, in Dfmt, supplied when the bit is 1
Dfmt M0	Matrix M0 of the rows, in Dfmt, supplied when the bit is 0
Dfmt M	Matrix M in Dfmt obtained by combining the two sets of rows.

7 PVC. Pivot combine Parameters
BitString P	The initial bit input string
BitString Q	The bits of Q correspond to the unset bits of P
BitString P1	The string P with the set bits of Q set additionally.
BitString U	One bit for each set bit in P1 - where did it come from (1=P)

8 BEX. "Both Extract" - select the non-selected rows of the selected columns. The parameters are
Field	f	The field structure in use
BitString R	The Row-select bit string
BitString C	The column select bit string.
Dfmt H	The input matrix in Dfmt.
Dfmt F	The selected columns of the non-selected rows of H.

Section 6 – Detail of further proggies in future.

10 SUB. A Dataflow proggy for matrix subtraction. This proggie has four moj parameters
Field	f	The field structure in use
Dfmt	A	Matrix A in Dfmt
Dfmt B	Matrix B in Dfmt
Dfmt C	The result matrix, in Dfmt, C = A − B

This proggy is needed, as well as ADD, to implement a Strassen-Winograd algorithm or suchlike. It is not, however, clear how the memory footprint is controlled.

11 CPY. A Dataflow proggy for copying a matrix. This proggie has three moj parameters
Field	f	The field structure in use
Dfmt	A	Matrix A in Dfmt
Dfmt B	The resulting Matrix B in Dfmt, set equal to A

No use for this proggy has been identified, though I suspect it will be needed sometime. In fact, it has more-or-less already been implemented. It needs the field as otherwise it cannot determine the length of the data.