Meataxe-64
Field Specification.
Richard Parker 21.8.2016

Section 1 – Introduction

This document specifies the functions available in the field module, and works with all fields whose order is less than 264. It works with individual field elements, and also with vectors of packed field elements (in Dfmt). It relies on a module pcrit to do the performance-critical parts, of which four versions are currently available – GEN in “c” and three version for various flavours of x86 assembler code. It also uses the conex module to “compute” the Conway polynomials in difficult cases.

The first function that must be called is FieldSet (or FieldSet1) to compute a fairly large collection of variables and tables used by the field module, but the field module also can be used by programs directly if required. FieldSet is usually the call used – FieldSet1 has additional flags and a return code to enable the setting of the field to be better controlled in special circumstances.

Section 2 – Algorithms for Vector Operations

There are four operations on vectors of performance importance – add, subtract, multiply and multiply-and-add. These are available in both the extension field and the ground field, making 8 routines in all. For higher performance, the HPMI must be used, but the routines of the field routine are still of some significance since they are used . . .

- In Gaussian Elimination, to work with small batches of vectors.
- With extension fields, to compute linear combinations of ground-field matrices.
- To perform the add/subtract operations of Strassen, although this is not (21.8.2016) implemented as yet.

In the first two cases, it is the multiply-and-add routine that comes under the greatest pressure, so I will start with that. The typical use in both cases is where the vector is a few KiloBytes long and – if the calling routine is well-designed – already in cache. We wish to take a scalar λ and two vectors W and V, and replace V by V+ λW. If the scalar λ is 0, 1 or –1, we may do nothing (0), add (1) or subtract (– 1), so none of these methods are used when the field has order 2 or 3.

Mul8/XOR method. This is used for extension fields in characteristic 2 when the multiplier is neither 0 nor 1. The simple-minded (unrolled) approach is . . .
movb	(vptr),ah	// P23
movzbq	(wptr),rcx	// P23
xorb	(mul8,rcx,2),ah	// P23 P0156
movb	ah,(vptr)	// P237 P4 (no P7 before Haswell)
On Haswell or later, this is aimed at 1.5 clocks per byte with three mu-ops to P23 and one each to P7, P0156 and P4. This will almost certainly be mu-op bound (we have to update pointers and count/termination at some point). On Sandy/Ivy bridge it will take 2 clocks as the store also uses P23.
Mul8/Add8 method. This uses a double table lookup, and is used for fields of odd order between 5 and 251 inclusive - when the Dfmt data is of byte length. This uses the routine pcubf (performance-critical unary/binary function) which is aimed at approximately 2 clocks per byte.
The simple-minded (unrolled) approach is . . .
movzbq	(vptr),rax	// P23
movzbq	(wptr),rcx	// P23
movb	(mul8,rcx,2),ah	// P23 + combination?
movb	(add8,rax),dh	// P23
movb	dh,(vptr)	// P237 P4 (no P7 before Haswell)
This leaves plenty of time for updating pointers, counts and checking termination. It may be slightly faster to load (vptr) at 32-bit length and use ah/al and shr $16 to reduce the P23 pressure, but this is likely to be marginal and an overall performance close to one byte every 2 clocks is to be expected.
Mul32/Barrett64 method. This is limited to primes between 65536 and about 2,000,000, at which point Barrett-64 ceases to work. This fetches two 32-bit words (from W and V respectively), does a multiply to make a 64-bit word. We then add in V and multiply by 264/p (rounded up). We then multiply the top word of this (the quotient) by p, subtract that off the original product and store the result.
movd	(vptr),vv	// P23
movd	(wptr),eax	// P23
mul	eax,lambda	// P1
addq	vv,eax	// P0156
movq	eax,prod	// P0156 may be elim.
mul	barrett	// P1
imul	rdx,prime	// P1
subq	rdx,prod	// P0156
movd	prod,(vptr)	// P237 P4
This code is clearly P1 bound and limited to 3 clocks per word.

Let’s consider now the use of vector arithmetic.

First consider the fetch (of W and V). The following instructions fetch data of any short length in meataxe64 and extend it (with zeros) to any other length. They first came out with SSE4.1 which seems old enough for all purposes.
PMOVZX. . .BW/BD/BQ/WD/WQ/DQ
Nehalem P2 P05 Sandy/Ivy Bridge P2 P15 Haswell P23 P5
VPMOV versions AVX-2 latency 3 instead of 1 when register-register.
Haswell/Broadwell/Skylake P23 P5

Now consider the multiplication by λ. There is a preparatory step whereby λ is duplicated to all the slots in the register.
PMULLW does 16x16→16 keeping lower portion.
PMULLD does 32x32→32 keeping the lower portion.
PMULUDQ does 32x32→64 as we need it . . . as unsigned integers.

As I understand it so far, PADDW, PADDD and PADDQ are all good for the addition step, though the PMAD might help.

What about Barrett? We want to multiply by something and get the high portion.
PMULHUW does 16x16→16 keeping higher portion unsigned. Perfect.

There is, however, no 32x32 at full power keeping the high portion. We might have to consider genuine Barrett for this case. Larger than this we will need to go scalar.

Now let’s look in detail, starting with the smallest primes.

Suppose first we have a byte-sized prime – 17-251. The two fetches 8 → 16 are OK with PMOVZXBW, after which we can multiply the W-one by λ keeping the lower portion, and then add the V-data. The result is at most 272 (p=17) to 12750 (p=251). We can’t use 24-bit Barrett as 224/p does not fit in 16 bits, but up to 131-199 we can use 23-bit. 21-bit is good from 67-127 and 18-bit from 5-61 We don’t need anything below 17 here, so 20-bit is good from 17-101, which is a good chunk.

As a digression, I observe that 16 multiplies in one go is of interest also in the HPMI. P0 latency 5 on

Section 3 – What FieldSet and FieldSet1 do.

The setting of the field is given two parameters – the order of the field required and the area (which must already be allocated by the caller as at least FIELDLEN (#defined in field.h, currently 4194304) to hold the FIELD structure.

f→fdef is set to the order of the field, as given by the caller.
f→charc is set to the characteristic. If fdef is in fact a prime-power, this is always set correctly. If an attempt is made to set a field order that is not a prime power, this will be noticed . . .
1. If the 4-bit of flags is set.
2. If the field order is divisible by a prime less than 65536.
f→pow is then computed such that (f→charc)f→pow = f→fdef
The TSqrt table is computed next (see below) as it may be needed for the computation of a quartic Conway Polynomial, which are calculated on the fly.
f→paktyp is then computed to indicate how field elements are packed in Dfmt. It takes the values 0 (64-bit), 1 (32-bit), 2 (16-bit), 3 (8 bit), 4 (2 in a byte), 5 (3 in a byte – GF(5)),
6 (4 in a byte – GF(4)), 7 (5 in a byte – GF(3)), 8 (8 in a byte – GF(2))
f→conp is then usually computed. It is computed if . . .
1. The field is of composite order
2. flags&3 is 1.
3. fdef-1 has at most one prime factor > 216 and that is < 232.

In other words it is always computed except that the smallest primitive root of large primes may not be computed if not requested and fdef-1 is not readily factorized.

The following look-up tables are computed under the conditions specified. The int in the field structure gives a byte displacement from the start of the field structure. Hence to locate the table, the field structure must be cast to an 8-bit object, the table name (e.g. f→TSqrt) added, and then, for 16-bit tables, the result cast to a 16-bit pointer. If the table is not present, the integer index (e.g. f→TSqrt) is set to zero. e.g. sqrt=(uint16_t *) (((uint8_t *)f)+f->TSqrt)

TSqrt f→charc < 65536	16-bit table indexed by 0 ≤ x < f→charc giving the smallest
positive square-root of x mod f→charc, or 0 if it has none.
Tred16 f→charc < 65536	16-bit table indexed by 0 ≤ x < 2*f→charc giving
x % f→charc
Tadd8 2 < f→charc < 256	8 bit 2-dimensional table adding two bytes. Tadd8[256*a + b]
is byte obtained by adding a and b. Not in characteristic 2 as
xor should be used. Adds packed bytes for 3,5,7,11,13 and
bytes for 17-251. Only works for bytes that can occur.
Tmul8 f→charc < 256	8-bit scalar multiplication. Tmul8[256*a+b] for a byte b and a
scalar a gives the byte representing a.b. If a < f→charc this is
always defined. If, in addition, f→fdef ≤ 256 for an extension
field, a may be in the extension field. Notice that in the area
where these requirements overlap, they agree.
===================================================================

Section 2 – field.h and the data structures.

The field.h header file starts with the #define lines that the installation may need/want to change.

field.h provides the typedef's of uint64, uint32, uint16 and uint8 as unsigned integral types of the specified size in bits. It is not expected that meataxe-64 will operate with a system where they cannot all be defined.

A FELT is a field element, typedef'd in field.h. In meataxe-64 this is always a uint64, but the programmer is encouraged to use a FELT for a field element for programming clarity.

The FIELD structure is a public, defined structure, though frequently its internals are not of interest.

Once set, this data structure is read-only, and may be safely passed around to threads. It is position-independent and can be copied and still used. The setting of the structure can take some time, and unnecessary repeated setting should be avoided. In a multi-threaded program, it usually resides in a moj - often moj 0.

field.h also typedef's Dfmt to be a uint8. Most matrices are held in Dfmt, to which all the main functions can be applied. Further formats will be defined in the HPMI.

There is also a DSPACE, which is basically a field and a dimension. A DSPACE struct can be simply declared on the stack, and set with DSSet.

Section 3 – The field module interfaces.

int FieldSet(uint64 fdef, FIELD * f, int flags) to set the FIELD structure f to work in the field specified by fdef. The fdef is an unsigned integer giving the order of the field. If fdef was a prime-power, a positive number is returned and if the fdef is invalid (not a prime power), -1 is returned. The area f provide here must be at least the size FIELDLEN. The "flags" field must currently take the value zero and is reserved for future use.

The following six functions do not check their parameters. A FELT is always in the range 0 . . . (fdef-1) and has a meaning that is absolutely defined.

FELT FieldAdd(const FIELD * f, FELT a, FELT b) to add the field elements together in the field specified in the FIELD structure, so a+b is returned.

FELT FieldNeg(const FIELD * f, FELT a) to return the negative of the field element a in the field specified in the FIELD structure.

FELT FieldSub(const FIELD * f, FELT a, FELT b) to return the element a−b in the field specified in the FIELD structure.

FELT FieldMul(const FIELD * f, FELT a, FELT b) to multiply the field elements together in the field specified in the FIELD structure.

FELT FieldInv(const FIELD * f, FELT a) to return the inverse of the element a in the field specified in the FIELD structure. The FELT a must not be zero.

FELT FieldDiv(const FIELD * f, FELT a, FELT b) to return a/b in the field specified in the FIELD structure. The FELT b must not be zero.

Section 4 – The DSPACE routines.

These routines provide for the normal manipulation of vectors (and, in some cases, matrices) packed in D-format. These routines are not designed for the highest performance, and should not be considered suitable for “cubic” work unless the HPMI routines are not available. The DSPACE structure itself is of constant size and can just be declared, though it is a pointer to it that is used by the routines.

It should be noted that D-format in memory is completely defined, and that there is no need, in principle, to use these routines. Sometimes their performance is inadequate and the program needs to handle the data directly, in which case any tables used internally by the field routine are fully specified and available. It should be noticed that, in all fields, binary zero of the correct length is always the zero vector in Dfmt.

These routines work on valid input vectors only, and uninitialized memory may not be valid. The space for the output of DAdd, DSub, DCpy and DCut may be uninitialized (somewhat heroically in the latter case), but DPak and DPaste must have a valid vector to put entries into. memset(ptr,0,bytes) is recommended to clear an area initially if it is to be populated with DPak or DPaste.

void DSSet(const FIELD * f, uint64 noc, DSPACE * ds) to set the DSPACE structure ds ready for working in a vector space of dimension “noc” over the given field.

FELT DUnpak(const DSPACE * ds, uint64 col, const Dfmt * d) to return the element in the specified column of the row pointed to by d in the specified space.

void DPak(const DSPACE * ds, uint64 col, Dfmt * d, FELT a) to insert the given element a into the specified column of the row pointed to by d in the specified space.

void DAdd(const DSPACE * ms, uint64 nor, const Dfmt * m1, const Dfmt * m2, Dfmt * m) to add the matrix m1 and the matrix m2 (each nor rows in length) in the specified space and put the result into m. This routine is specified as being of “good” performance, suitable for Strassen. Any or all of the areas m, m1 and m2 may be the same, but they must not otherwise overlap.

void DSub(const DSPACE * ms, uint64 nor, const Dfmt * m1, const Dfmt * m2, Dfmt * m) to subtract the matrix m2 from the matrix m1 (i.e. compute m1−m2) in the specified space and put the result into m. This routine is specified as being of “good” performance, suitable for Strassen. Any or all of the areas m, m1 and m2 may be the same, but they must not otherwise overlap.

void DSMad(const DSPACE * ds, FELT a, uint64 nor, const Dfmt * v1, Dfmt * v2) to adds the scalar multiple of the "nor" vectors at v1 by a into v2. This is done at reasonable performance.

void DSMul(const DSPACE * ds, FELT a, uint64 nor, Dfmt * m) to multiply the matrix pointed to by m by the scalar (field element) a. This is done “in situ”, and at reasonable performance.

uint64 DNzl(const DSPACE * ds, const Dfmt * v) to return the column number of the first non-zero entry in the vector. ZEROROW (#defined in field.h) is returned if the row is entirely zero.

void DCpy(const DSPACE * ms, const Dfmt * m1, uint64 nor, Dfmt * m2) to move nor rows of the matrix m1 to m2 in the specified space. The areas m1 and m2 may not overlap in any way (memcpy is used). m1 is left unchanged.

void DCut(const DSPACE * ms, uint64 nor, uint64 col, const Dfmt * m, const DSPACE * cbs, Dfmt * cb) to take a section of columns of Dfmt matrix m, starting at the stated (col) column number and put them into the clipboard space cb. The selected columns are taken from the first nor rows of m, and the number of columns taken is specified by the dimension of cb (in cbs). If more columns are requested than exist in m, the surplus columns are set to zero in cb.

void DPaste(const DSPACE * cbs, const Dfmt * cb, uint64 nor, uint64 col, const DSPACE * ms, Dfmt * m) to take nor rows from the clipboard matrix cb and paste them starting at column col into the matrix m. If more columns are supplied than exist in m, the surplus columns are discarded.

Dfmt * DPAdv(const DSPACE * ds, uint64 nor, const Dfmt * d) to return a pointer that is starts at the specified row of the matrix d. A matrix consists of a string of vectors, where every vector consists of precisely ds->nob bytes. Notice that nor is unsigned.

Dfmt * DPInc(const DSPACE * ds, const Dfmt * d) to produce a pointer to the next row after the one pointed to by d. This is equivalent to DPAdv(ds,1,d).

Section 5 - Other functions.

uint8 * AlignMalloc(size_t bytes) allocates memory aligned to the page - currently 4096. If this routine is used to allocate memory, the following routine must be used to free it.

void AlignFree(uint8 * ptr) frees memory that was allocated by AlignMalloc