Meataxe-64
FIELD module routines for vectors. Richard Parker 25.10.2016

Section 1 – Introduction

This document considers the performance of the FIELD module routines DAdd, DSub, DSMul and DSMad. Although the HPMI and linear forms modules are ultimately intended to form the performance heart of meataxe-64, at present they are only implemented for fields of order {2,3,4,8,9,16}, and anyway the nitty-gritty bits of Gaussian elimination, as well as the linear forms module itself, still use the vector arithmetic of the FIELD module even if the faster methods are implemented for matrix multiplication.

The routine that matters most is the DSMad routine, that multiplies a vector V by λ and adds the result into the vector W in the field F, and the methods used necessarily vary widely with the field, whose order ranges from 2 up to 1.8 x 1019. DSMul has similar requirements. The DAdd and DSub routines are somewhat different, and will be more significant if Strassen/Winograd methods are implemented. All four routines work with multiple rows if required.

It should be noted that, for primes fields up to 32 bits, the routines must provide both ground and extension field service if an extension field is set.

There is one opportunity for computation when the field is set, where the target is roughly 10 milliseconds. This allows for computation of various constants and look-up tables specific to the field, and is already used quite considerably.

For DSMad and DMul, there is a second opportunity for computation when λ is known, and in version 1, no advantage was taken of this. A considerable portion of this document is therefore devoted to addressing this - to inspect λ and to figure out how best to multiply by it.

For large primes, much of the problem revolves around the fact that division is so much slower than multiplication, so that Barrett figures largely in this. A major issue is to use Barrett to its greatest possible extent yet ensuring that the result is always correct.

Section 2 – 64-bit primes.

The first case to consider is for primes p that do not fit into a 32-bit field. For these primes, no extension fields need to be considered since any such field would have order greater than 264 and hence be outside the scope of meataxe64.

For the very largest primes, even addition c = a + b must worry about overflow, but as both a and b must be less than p, this is a fairly simple test . . . we compute c = a+b, then if c < a overflow has happend (so we must subtract p to fix it) and if c >= a it has not. We may then compare c to p, and if c >= p we subtract p and otherwise we do not. Both of these fixes can be done using the CMOVE instruction, and this is appropriately generated by the "c" compiler, so is not a worry. It may be faster to compute c = a + b - p and if c > a, add p, which works for all primes. This needs to be checked out. Subtraction is actually a little simpler . . . we compute c = a - b and if the result is bigger than a, we add p.

Multiplication, however, is certain to overflow and other methods must be used.

The simplest is to simply do the multiplication and addition using the pcrit pcpmad routine, which does a division to get the remainder. This is probably never the fastest way to do it, but has the advantage of simplicity and can certainly be used as a preliminary case.

The problem is, of course, that division is a very slow operation compared to multiplication, and various flavours of Barrett are to be considered.

It is important to realize here that, in typical usage, a substantial vector is multiplied (DSMul) or multiplied-and-added (DSMad) by the same scalar λ, so that it may be appropriate to do some work with λ before proceeding through the vector. In practice we will want to compute λ.2r/p (rounded up) for an appropriate value of r, and it is the choice of r that really needs consideration here. It is annoying that, for the largest primes we need r=129, but for meataxe64 version 2, I propose to use r=128, and if the prime is too large for this case, to default to the pcpmad division alternative. This will only affect primes above 1019 and should not be a great loss.

We must, however, consider the limits of "128-bit lambdified Barrett" very carefully to ensure that we use as often as we reasonably can, and yet still be sure of not using it if it can produce incorrect results. This is a one-off computation, which will be described here and the results given.

Our plan is to compute s = 2128/p and t = λ.2128/p as a two-word value, both rounded up, the former at FieldSet time and the latter on entry to DSMad/DSMul - when λ is known. These will be done by division. Notice that if the number of columns is very small (perhaps 1-3) it is faster to simply use pcpmad and maybe that should be done.

To compute λ.a+b (mod p) we compute m= λ.a+b as a two-word value, and also calculate k=t.a+s.b as a three-word value. We then take the top word of k (k/2128), multiply by p and subtract it from m. The result is required to be λ.a+b (mod p).

Well . . . what actually is it? Let λ.a+b = c.p+d. We require k/2128 = c.

Let S= 2128/p and T = λ.2128/p as exact real numbers.

Then Ta+Sb = a.λ.2128/p + b.2128/p = 2128/p . (a.λ + b) = 2128/p . (cp+d) = 2128.c + 2128.(d/p) so the top limb is indeed c, since d/p is less than 1.

Since s = S+ε2 and t=T+ε1 we actually compute . . .

ta+sb=(T+ε1)a+(S+ε2)b =Ta+Sb+ε1a+ε2b=2128.c + 2128.(d/p)+ε1a+ε2b.

We therefore need that

2128.(d/p)+ε1a+ε2b < 2128.

Let d = p–z. The we need 2128.([p–z]/p)+ε1a+ε2b < 2128 or ε1a+ε2b < z.2128/p. For z >= 2 this clearly holds, since z.2128/p > 2.p and ε1a+ε2b < 2.p.

For z=1 we need ε1a+ε2b < 2128/p or p.(ε1a+ε2b) < 2128. No doubt this will be OK for some larger primes also, but without extensive computations with results that would probably not help much, it seems best at this point to limit the method to cases where 2.p2 < 2128 and leave it at that. In other words, we need p < 264/sqrt(2) which is greater than 13,438,178,000,000,000,000. We will leave primes 13x1018 up to 18x1018 to use the division method!

It seems clear that this will require assembler assistance, if only to gain access to the multi-word multiplications, add-with-carry etc. to enable us to perform this work.

For smaller primes, it is possible to get away with only computing two words of ta+sb and using 285 instead of 2128. This needs c<243 and 2p2<285, and hence would be fine for primes up to 242. This is probably not too much extra programming, and perhaps a 25% speedup for primes of 32-41 bits would result.

We therefore expect three cases in the end.

DIV	use 128-bit division in assembler using pcpmad for primes of more than "63.5 bits".
B128	use 3-word lambdified Barrett 42-63.5 bit primes
B85	use 2-word lambdified Barrett 32-41 bit primes.

Section 3 – 32-bit primes.

32-bit primes are really an easier version of the 64-bit ones, and though we must now consider the case where the field is actually set for an extension field, it is the working in the prime field that is considered here.
The main workhorse for this case is Barrett-64, and the lambdified version is good except for primes greater than 232/sqrt(2). A version of B85 can be used (amended to take 32-bit inputs) for the primes larger than this.

Barrett-64.

We pre-compute s = 264/p and t = λ.264/p as a one-word value, both rounded up. Then to compute λ.a+b (mod p) we find m=λ.a+b and k=t.a+s.b as two-word values, though only the bottom word of m is used. We then take the top word of k (k/264), multiply by p (taking the bottom word) and subtract it from the bottom word of m, yielding λ.a+b (mod p).

Hence the assembler routine to do a single instance would be . . .

uint64_t bar64(uint64_t a, uint64_t b, uint64_t * stc) where stc[4] contains p,λ,s,t.

This is probably of adequate performance for DSMul, but we will probably also want a "babies" interface for DSMad, needing . . .

void bar64mad(uint32_t * a, uint32_t * b, uint64_t noc, uint64_t * stc)

Section 4 – Extension fields from 32-bit primes.

Since the prime in this case does not fit into 16 bits, the extension field is either quadratic or cubic and the field-entry itself is always 64-bits. In the cubic case (Lübeck) the coefficient of X2 is always zero.

The general plan is to compute upfront the 2x2 or 3x3 matrix for the linear map for multiplication by λ, and then to proceed through the vector, extracting the entries into 2 or 3 integers, multiplying this vector by the matrix, reducing all mod p and then re-assembling the answer. As is becoming usual, there are difficulties with overflow if the field order approaches 264 too closely, and to start with I will concentrate on cases where this does not occur.

Let's consider the quadratic extensions first. For extraction, it looks at first sight that we need Barrett96, and it is clearly annoying that 296/p is going to need two words. At the other extreme (65537) Barrett51 is sufficient, but it gains us nothing to use as few as 51 bits. We are happy to get a 2-word result, but it would be nice if the answer was all in the top word, making Barrett64 the obvious choice. It looks like one size is not going to fit all.

Barrett64 is clearly one of the cases to be implemented. This will cope with cases up to 2,642,2452 or so - must be less than the cube root of 264 though it may extend a little beyond.

The next case should ideally cope with the larger primes of 22 bits, so the natural next stage is Barrett85, so that 285/p is guaranteed to be less than 264. This is good up to the cube root of 285, which has 28 bits. We could then implement Barrett92 and get up to 30 bits, and Barrett94 to get past 31 bits, and Barrett95 to get a bit further . . . I'm not sure how sensible all this is!

There is the alternative of passing the "shift" value and using the %cl form of the right-shift. I suspect we are going to have to do this in the end, but let's move on to the cubic fields to find out what joys await us there.

For cubic fields p3 we need ap2 < 2r where a ranges up to p2, or ap4 where a ranges up to p. Which is the better approach (i.e. do we chop off the top entry or the top two)?

Section 5 – 16-bit primes.

For primes that fit into 16 bits, Barrett reduction comes within the range of AVX, and we can hope to perform Barrett32 in the SIMD registers. Let's look at this in a bit more detail.

Barrett-32.

We pre-compute s = 232/p and t = λ.232/p as 32-bit values, both rounded up. Then to compute λ.a+b (mod p) we find k=t.a+s.b as 64-bit values (needed for the addition) and the bottom 32 bits of m=λ.a+b and. We then take the top 32-bits k (k/232), multiply by p (taking the bottom word) and subtract it from the bottom word of m, yielding λ.a+b (mod p).

= = = = = = = = = = = = = End of next phase editing = = = = = = = = = = = = =

Section 2 – Fields of order up to 256.

For fields of order at most 256, where one or more field entries are held in each byte, it is considered acceptable to hold 2-dimensional look-up tables, and in particular the tables add8, sub8 and mul8 are computed at FieldSet time, so that all routines can work at a reasonable pace.

TBD document how it actually works.

Section 3 – Fields 257-65536.

For fields in this range, it is considered acceptable to have one-dimensional look-up tables, but not two-dimensional ones. In particular the log16 and alog16 tables are used (where appropriate) for multiplication. At present the Zech logarithm approach is used for multiply-and-add, but it seems likely that the spac/sqid approach will be faster. This needs to be investigated and checked.

Section 4 – 32 and 64-bit fields of characteristic 2-13.

For fields in this range, it is desirable to pack two or more entries mod p into each byte, allowing look-up (add8, sub8, mul8 etc.) to be used. Further look-up tables will almost certainly be needed, and this whole area is ripe for revisiting in its entirety.

Section 5 – 32 and 64-bit fields of characteristic 17-251.

Not really considered this case at all yet.

Section 6 – 32 and 64-bit fields of characteristic 257-65531.

Not really considered this case at all yet either.

Section 7 – 32 bit primes.

There are a fairly wide range of methods that might be appropriate here, and some experimentation is needed. The subject under consideration is the implementation of the four routines (DAdd, DSub, DSMul and DSMad) for primes in the range 65537 to 232. I consider look-up tables as being too large for this case, as they would not even fit into L2 cache. Let's first make a list of ideas. The issue to consider is the reduction modulo p.

1. For addition, we simply compare to the characteristic and subtract it if greater-or-equal. This can be done with a conditional move instruction, so is by no means as bad as an unpredictable branch.
2. Barrett41 is good for

Section 8 – 32 and 64-bit extension fields of 32-bit primes.

Not really considered this case at all yet either.

Section 9 – 64-bit primes.

Not really considered this case at all yet either.

Section 7 – Adding in moderate extension fields odd charc.

For moderate extension fields, the spac/sqid tables and the Barrett-41 schemes are as a means of adding and subtracting in moderate fields of small odd characteristic. The scheme is not entirely self-explanatory, so it is described in full here.

As an example to see the principle of spac and sqid, suppose we need to add in the field of order 25 = 52. We can’t just add the integers, since this would cause overflow from one digit to the next. Suppose, for example, we consider 3X+2 + 2X+4. These are represented by 17+14, which comes to 31. Unfortunately 3X+1 + 3X+0 comes to 16+15 which is also 31, yet the first should be 1 and the second X+1. There has been overflow from the constant term to the X term. If we consider the field 36, the situation is considerably more complicated, and as far as I can see, it is not simple to determine where the overflow has happened.

Instead we could use the spac table to “space things out a bit”. (Note – this is not exactly what it does, as it is only the principle being described here). We first look up the field entry, representing a+bp+cp2 . . . and replace p by (2p-1). Then addition can take place without fear of overflow, and we can look up the result in the sqid table to reduce each entry mod p to obtain the correct answer.

For addition, we would then add x and y by writing sum=sqid[spac[x]+spac[y]], achieving the entire addition with three look-ups. Notice that we could encode spac[x] to be x+c (mod p) for any c in each digit, provided the sqid table subtracted 2.c to correct it.

We make use of this so that we can use the same tables for subtraction. By choosing c = –1/2 (mod p) we find that we can do subtraction as diff=sqid[2c+spac[x]–spac[y]]. In the code, 2c is held in the constant spaczero.

Letting c (spaczero) = –1/2, we therefore define spac[x] as c+x (reduced mod p) in each digit, spaced out using (2p–1) and define sqid[x] as x+1 (mod p), squidged up to use p instead of (2p–1).
For addition sum=sqid[spac[x]+spac[y]] yields x+c+y+c+1=x+y since 2c+1=0.
For subtraction sqid[2c+spac[x]–spac[y]] yield 2c+x+c–(y+c)+1=x–y for the same reason.

The spac and sqid tables are 16-bits wide to save memory (actually it is cache-space that matters here) and so the method is only used for relatively small fields.

More specifically in characteristic 3, it is limited to 36. In spac we replace 3 by 5, and 57 = 78125 is too large to fit in 16 bits, so that the sqid table would need to be 78125 32-bit values, which would thrash the cache in many cases.

The exact bounds are 36 = 729, 55 = 3125, 74 = 2401, 113, 133, 173 and 193, and the squares of primes 23-127 inclusive.

For fields of higher degree, we may proceed by breaking the field entry into chunks. For example to add in 116, we break the field element into two parts each containing three ground-field values, add each of them separately as above, and then combine them to produce the answer. The Barrett-41 scheme is use to avoid the division that would otherwise be needed to produce the two chunks from the input value. To achieve this, the value of 241/113 (rounded up) is stored in the bar41 constant, and we find that (x*bar41)>>41 is always the top half, enabling the bottom half to be computed by multiplication and subtraction. Similarly for primes between 256 (below which a different method is used) and 1278, we may use Barrett-41 twice to break a cubic extension into three parts, though in this case the spac and sqid tables are not needed.

The main application of these methods is in addition and subtraction, but they also have a place is the “multiply and add” routine DSMad, which is of considerable performance importance as it is heavily used in Gaussian Elimination. Once the (extension) field is larger than 256, it is no longer practical to hold a full multiplication or addition table (which are of size around q2) and to work instead with one-dimensional look-up tables. The “Zech-log” method can achieve this, but using logs, antilogs and spac/sqid is faster, at the expense (mainly) of the size of the sqid table, which is linear but considerably larger. This is therefore only used for fields inside the “exact bounds” list above and greater than 256, namely
{ 36, 54, 55, 73, 74, 113, 133, 172, 173, 192, 193, and the squares of primes 23-127}
It is presumed to be faster to use Zech than to break the value up. I suppose I ought to check this sometime.

Section 2 – Behavior of Barrett-41.

Using the bartest.c program, which tests directly the first value of a such that a.D+b does not correctly extract a using Barret-41 for odd D, we find the following results.

Below 527, the first failure is at 223 = 8388608 and is due to overflow of the result of the multiplication. At 527 itself, however, it fails for 7948037. Already 5273 is well over 223, so Barret-41 can only be used to extract the lowest digit of four up to the fourth-root of 223 – that is to say it is OK for 53 but not for 54. For extracting the lowest digit of longer polynomials, Barret41 is entirely limited by the result fitting into 23 bits.

For extracting the bottom digit of a cubic, the first failure is at 1235, which is not a prime power. The first field order for which it fails is 1279 (a prime) – it is OK for 1237, 1249, 1259, and 1277. The largest field for which it works with cubics is 2731 – a prime. There are 162 odd numbers between 1237 and 2769 inclusive which works. I have not yet checked how many of them are field orders – presumably about 20 or so.

Moving on to separating quadratics, up to 13175 all odd numbers are OK, but 13175 is not, first failing when a is only 12670. The smallest field order for which it fails is 13367, working fine for 13177, 13183, 13187, 13217, 13219, 13229, 13241, 13249, 13259, 13267, 13291, 13297, 13309, 13313, 13327, 13331, 13337 and 13339. Hence it works for all fields up to and including 13339 but not 13367 – the next case. There are many higher primes for which it works, the largest being 154543.

Now we consider the extraction of two digits at a time from four. 121 is the first number that fails, and sadly 125 fails also. 127, however, is OK, as are 131,149, 251 – the only other three cases where a quartic can be extracted into two pairs of digits using Barrett-41.

Section 8 – Summary of addition in version 1.

Addtype	Used for
1	All characteristic 2 including PSet.
XOR using pcrit pcxor for nob bytes.
2	8 pow>1 4 char!=2 q=5,3 also PSet 3,5,7,11,13
Using add8 table and pcrit pcbif routine
3	8 pow=1 also PSet
Add and use red16, unrolled four times in “c”.
4	16 pow=1 also PSet
Add and use red16
5	16 pow<=spaclev spaclev>=2 {36 54 55 73 74 113 133 172 173 192 193 232-1272}
spac and sqid.
6	16 p2, p=131-251.
Barrett-41 to split, add each, red16, then multiply to reassemble.
7	32 pow=1 also PSet
Add, then “if>charc, subtract charc”, which compiles as a CMOVE
8	32 default 313-320 etc.etc. etc. Anything bigger than addtyp 11,13,14 can handle.
qadd Terrible performance!
9	64 pow=1, also PSet
Add, then “if>charc, subtract charc”, which compiles as a CMOVE
10	64 pow>1 odd. All 64-bit composite fields of odd characteristic.
qadd Terrible performance!

11	32 pow<2.spaclev, spaclev>1
311 312 57-510 75-78 114-116 134-136 174-176 194-196 234-1274 413-1273
Barrett-41 to chop into spaclev and the rest, then spac/sqid, then reassemble.
12	16 pow<=2.spaclev, spaclev>1 pow>spaclev 37-310 56 75 114 134 233-373
Barrett-41 to chop into spaclev and the rest, then spac/sqid, then reassemble.
13	32 pow=2, spaclev=1
Barrett-41 to chop, then add, red16 and then multiply to reassemble
14	32 pow==3 spaclev=1 charc<1278
Barrett-41 to chop into three pieces, add, red16 and reassemble.

Need to find a better way to handle very large extension fields of odd characteristic. A Barrett-96 subroutine (in pcrit) will do most of them (provided pd/2 (d/2 rounded up) is less than 232) but leaves some tricky edge cases. DSMad is, however, even worse and more important, so probably should be considered first.

Section 5 – DSMad with 64-bit primes.

With 128-bit / 64-bit division taking up to 76 clock cycles (reciprocal throughput) it seems unlikely that this simple approach will ever be the fastest. If we are to use Barrett methods, however, there is still a lot of work. λ = μ + ε

Let’s consider the simple Barrett approach to computing λ.a+b (mod p). We first compute λ.a+b by multiplying a by λ to get a 128-bit result, and to add in b (remembering to propagate the carry) so that we have λ.a+b at high speed. For the largest primes we need to use 192-bit Barrett, so must multiply this by s=2192/p which will need three limbs. We therefore have a 2 x 3 multiplication, where the answer is known to fit into 4 limbs. If λ.a+b = c.p+d, the top limb of this is c, and we must now multiply c by p (1 x 1 -> 2) and subtract from λ.a+b to get d. This is nine multiplications and around 30 additions, many of the add-with-carry.

Two things seem clear. Barrett 192 will be faster than division, but it will still be pretty slow!

Suppose we try to do some work on λ first? Let s = 2192/p. We are going to compute
(λ.a+b)s as a 4-limb quantity, and we could compute t’ = λ.s independent of a. t’ still fits in 3 limbs. As s=2192/p, if we wish we can get a bit more accuracy by computing t = λ.2192/p (rounded up) hoping to save a limb. We would then compute t.a+s.b.

Section 6 – DSMad with “lambdified” Barrett-64.

Continuing with the above theme, let’s consider smaller primes and see what the limits are. Suppose, then, we are given p at field-set time and λ at the start of DSMad. We compute

s = 264/p (rounded up) at field-set time, and
t = λ.264/p (rounded up) at the start of DSMad.

To compute cp+d = λa+b we compute ta+sb and hope that the top limb of this is c. We then compute λa+b–cp and return the result as d.

Well . . . what actually is it?

Let S= 264/p and T = λ.264/p as exact real numbers.

Then Ta+Sb = a.λ.264/p + b.264/p = 264/p . (a.λ + b) = 264/p . (cp+d) = 264.c + 264.(d/p) so the top limb is indeed c, since d/p is less than 1.

Since s = S+ε2 and t=T+ε1 we actually compute . . .

ta+sb=(T+ε1)a+(S+ε2)b =Ta+Sb+ε1a+ε2b=264.c + 264.(d/p)+ε1a+ε2b.

We therefore need that

264.(d/p)+ε1a+ε2b < 264.

The method is therefore correct for a given prime p if and only if, for all { λ, a, b } the above inequality holds.

In the worst case, d is p–1, and in this case we need that ε1a+ε2b < 264/p, which will certainly be the case (needing only that the epsilons are less than 1) if 2p<=264/p, or 2p2 < 264. This is clearly the majority of the 32-bit cases, and (if we can be bothered to use it) will in fact work for many higher primes, and even if it fails, it will fail for rather few values of λ. In fact, if d is p–2 or lower, the inequality holds for all p < 232, so we only need to check d=p–1 to see when it fails for 32-bit primes.

Multiplying through by p we get that the inequality is

264.d+ε1pa+ε2pb < 264.p and notice that ε2p is the integer δ2 = –264 (mod p) and ε1p is the integer δ1 = –λ 264 (mod p) so the inequality reads

a.δ1 + b.δ2 < 264 (p–d) where δ2 is constant (for a given p) and δ2 depends only on λ, and that
d= λa+b (mod p).

Observe also that the method translates to a 128-bit version, working for all primes where
2p2 < 2128, which again is almost all of the 64-bit primes, and can also be used to cover the 32-bit cases where lambdified Barrett-64 fails.

Section 7 – DSMad for large extension fields.

DSMad for the field 16216 currently takes 19.2 minutes per gigabyte, compared to about 2 seconds per gigabyte for small fields. This is clearly terrible! This comes to about 1200 sec/Gigabyte, or 9600 nSec per entry. Let’s consider how this should be done.

The Conway polynomial for this field is X6 + 1337.X3 + 679.X2 + 1208.X + 2, which is not very encouraging, though it is actually better than some.

One approach is to extract the coefficients into arrays of six entries mod 1621, multiply the polynomials, reduce modulo the Conway polynomial and re-assemble the answer. This clearly involves a considerable number of reductions mod 1621, and we may wish to try to avoid most of them. In any case Barrett-41 can handle this pretty well, reducing a number mod 1621 provided only that it is of the form ap+b with a < 223. In particular it can be used for extraction from three entries (i.e. from a+bp+cp2)