Meataxe-64
CPUID issues
Richard Parker 14.11.2017

Section 1 – Introduction

This document tries to work out what the real issues are with the varying sets of instructions. The existence or otherwise of various instructions is signified by various bits set by the CPUID instruction, and it makes sense to work out what is really needed for the various modules.

Section 2 – Instructions needing no bit testing.

The following instructions are all available without inspecting the CPUID bits, since they are part of the 64-bit specification. Meataxe64 uses them mainly with 64-bit operands, so all of the pcrit stuff needs 64-bit mode.

ret pushq/popq je/jne movq/cmpq/andq/addq/xorq sarq/salq

Section 3 – NEH.

HPMI in characteristic 2 Needs SSE2, first introduced with the Pentium4. Since SSE2 is part of the specification of AMD-64, I believe that any chip capable of 64-bit mode must provide these instructions.
There are only two vector instructions used, both needing SSE2.
movdqa to load and store the Cfmt.
pxor to add in a vector from the BWA.

HPMI in characteristic 3. Needs SSE2, like characteristic 2.
movdqa, pxor already covered in characteristic 2 - needing SSE2.
por is the only other instruction used. It also needs SSE2.

pcxor Needs SSE2.
There is only one further instruction needed, namely
movdqu needs SSE2.

pcbmas
pmulld SSE4.1

pcchain Needs SSE2.
paddq / psubq SSE2
psrlq %xmm %xmm SSE2
pand SSE2
pinsrq $1,16(%rdx),%xmm9 for initialization SSe2