Meataxe-64
File Formats.
Richard Parker 13.1.2019

Section 1 – Introduction

This document specifies the format of data in files. A file in meataxe64 format consists of a header with a five-word header block (with its own checksum) and then a collection of 64-byte blocks in one of two formats (63 payload bytes or 31 <zero-count, byte> pairs if there are sufficient zeros to warrant it. The last block contains the checksum of the entire file. This format is specified in detail in section 2.

The five-word header block specifies in detail the semantics and syntax of the remaining file, as described in section 3.

Section 2 – Detailed file format.

The first 64 bytes of any meataxe64 file consist of 8 (little-endian) 64-bit integers with the following semantics

word 0 - always 1.
word 1 - the file type (1=matrix, 2=bitstring, 3=map etc.) see section 3.
words 2-5 further header information as described in section 3.
words 6-7 header checksum.

All following blocks are in one of two formats.

First byte = 10, 63 data bytes follow. If there are not that many data bytes left, the trailing space is filled with binary zeros.

First byte = 11, next byte is not used and must be zero. Then follows 31 pairs, each of the form <number of zero bytes, one byte> where the number of zero bytes may be anything from 0 to 255 inclusive. If there are more than that many zeros, 255 is used and the next byte is also set to zero.

On writing, the decision between the two formats is made once 63 data bytes are known. If there are 32 or fewer zeros, format 10 is used (63 flat bytes) and with 33 or more zeros, format 11 (zero compressed) is used. Notice that with precisely 32 zeros the data could be written in either format completely filling the block, so format 10 is preferred as it will decode more rapidly.

The last block consists of a byte containing 20 followed by seven zeros, followed by the 16-byte checksum, followed by 40 zeros to make up a complete 64-byte block.

The checksum mechanism used is bespoke, and is intended to be implementable using AVX-2 to deal with 32 bytes at a time, though the two rotates must each be done by two shifts and an add (or xor). Notice that AVX-512 includes a rotate, at which point we might wish we had done things 64 bytes at a time rather than 32. In any case, the implementation is only in "c" at the moment, and compiling with gcc -O3 does not notice the vectorization possibility, though this may change in future.

At some point I will add an appendix describing the checksum.

Section 3 – Header block semantics.

The I/O routines do zero compression and checksum verification automatically, and there is no current pressure, as far as I know, to change this. At the level of the I/O routines a file starts with five 64-bit words in a header (along with the indication that it is a header). The second word is an application "file type", currently holding 1-5 as follows in the hdr[0] column.

Hdr[0]	Hdr[1]	Hdr[2]	Hdr[3]	Hdr[4]
1 - matrix	fdef - field order	nor - #rows	noc = #cols	0 - not used
2 - bitstring	Always 1	# bits	# set bits	0 - not used
3 - map	Always 1	# domain	# image	0 - not used
4 - polynomial	fdef - field order	total degree	Number factors	0 - not used

Section 4 Format of matrices.

Meataxe-64 finite field formats are defined for all fields of order up to (but not including) 264. The first format defined is the FELT format (not used in files as yet) holding single field elements - actually an unsigned 64-bit integer. It expresses all elements of such a field as polynomials modulo the Conway polynomial, where a polynomial anxn + ... + a0 is held as the integer obtained by replacing the indeterminate x in the expression by p - the characteristic. Hence, for example, 3x+4 over a field of characteristic 7 is held as 3.7+4 = 25.

Format D is specified in terms of the field format. For fields of order 17 or greater, each FELT is stored in the smallest of uint64_t, uint32_t, uint16_t or uint8_t that can hold every element of the field. In memory (in principle) these are held in machine-endian form, but in practice the code only works on little-endian machines so the statement is currently rather academic. For fields of order q ≤ 16 the entries are packed such that a uint8_t holds as many as possible with the first vector entry added to q times the second, added to q2 times the third (q ≤ 5) added to q3 times the fourth (q ≤ 4) etc.
Hence the entries are packed into bytes in a little-endian form. For example, a byte containing 11 over the field of order 3 represents the vector [2 0 1] (2.1+0.3+1.9).
As another example, for the field of order 9 each byte holds a number in the range 0-80, each representing two consecutive vector entries - the first plus 9 times the second, so the vector [ x+1 , 2x ] is converted first to the "field" format, yielding [ 4 , 6 ] and then to format D, yielding 58 (not 42 . . . the field elements are held little-endian!).
A vector then consists of the minimum number of entries needed to hold it, with zero elements appended to complete the last byte if required (for fields of order ≤ 16 only). Hence, for small fields, a vector may consist of any number of bytes, so that, for example, each vector of dimension 12 over GF(3) occupies three bytes.

Section 5 – "bitstring" type.

Not yet documented.

Section 6 – "map" type.

The map type, frequently used for permutations, holds a map from . . .

The domain set {0,1,2, . . . ,<#domain-1>} to
The image set {0,1,2, . . . ,<#image-1> }

It should be noticed that previous meataxe systems used permutations on points numbered from 1. zcv therefore subtracts 1 from all point numbers and zpr adds 1.

Each entry occupies 8 bytes in a little-endian fashion, there being #domain words, each less than #image.

Section 7 – "Algebra" type.

At present, this is simply a "wrapper" for the number of generators, as used in split and standard base. There is the possibility later for adding further information, such as short relators, rewrite systems, alternative standard base setting etc.

Section 8 – "Sparsified" type.

The next word trip contains the number of "triples" (see below). The next word nord contains the number of dense rows. There then follow 3x"trip" 64-bit words of the form [ v , u , k ], and then "nord" rows in matrix format (see section 4). The user of a sparsified matrix must compute the total number of columns of U by taking noc (from the header) and rounding up if necessary to the nearest multiple of f->entbyte, and then adding k. These are the column numbers indexed by 'u' in a triple. A triple [v,u,k] indicates that k columns must be copied from an input vector starting at column v to U starting at column u for k columns. It should be noticed that DCut and DPaste use these values. The vector U is then considered as a vector in the original space and a vector W to be multiplied by the dense part of the sparsified matrix.

Section 9 – "perm cvt" type.

Not yet designed.