Meataxe-64
HPMI using single-precision floats.
Richard Parker 22.3.2018

Section 1 – Introduction

This is a design document for an HPMI implementation aimed at using the single-precision floating point capability of modern x86 chips to produce an HPMI suitable for working with primes 197-1669. A similar method(not currently under design) should also work up to around 33,000,000 using double-precision. The floating point numbers will normally hold exact integers.

The central operation is to multiply Aij by Bjk and add the result into Cik, so the first question is how to do this as fast as possible. There are four classes of machine that I currently propose to allow for, namely . . .

'a' uses SSE multiply and add.
'g' uses AVX multiply and add.
'k' uses FMA at 256-bit length.
'?' uses AVX-512 (not sure what this class will be called - maybe 'm')

The main target is 'k', but 'g'and '?' are also of considerable significance.

The high speed of the floating point operations, combined with the relatively large data size, makes it desirable to keep the data in the form of 16-bit integers in real memory, converting back and forth to floats as needed. It should take about 12 mu-ops (3-4 clocks) to convert 128 bytes and thereby save one cache-line fetch, and this is considered worthwhile. It also means that much of the code can work with integers, simplifying programming somewhat.

To fully utilize the range in which floating point stores integers exactly, these 16-bit integers (and the floats into which they are converted) are signed. Mod p, the numbers used are from -p/2 to +p/2, so that the product of two such is at most p2/4 in absolute value allowing four times as many to accumulate without fear of overflow as would be the case if positive numbers up to p were used.

For class 'k' machines, particularly Haswell+ from Intel, two the 256-bit fused multiply-and-add can be done in each clock-cycle making even the time to load data from L1 cache critical. We therefore use each load of A and B three times, so that for convenience we require that all three dimensions (including the "box") be divisible by three. The alcove is 24 and the cauldron 144.

The implementation for AVX-512 is not being attempted in detail here. The correct way to utilize 32 512-bit registers for this work is a very different problem, and will not be attempted until I have access to a suitable machine and until the performance details are available. It is hoped that most of the support routines (format conversions etc.) will still be applicable to this case also, though possibly warranting a performance rewrite to use AVX-512 for the format conversions themselves in the fullness of time.

Section 2 – The Brick Mad 192 24 144.

The usual reasons for trying to pin matrix C into L2 cache applies to the floating-point HPMI also - it writes as well as reads, and tends to be harder to compress. As usual, the matrix pinned should be roughly square. Also the rows of B/C should (AVX-512) have a length divisible by 192 bytes, and the other two dimensions should also be divisible by three, so the natural shape of matrix C (single precision) is ~192 rows of 144 columns (110,592 bytes). Matrix B needs to fit into L1 cache, so is 1/8 of the size, or 24 rows of 144 columns (13824 bytes). Hence matrix A is ~192 x 24, where the 192 number can vary but must be divisible by 3.

The operation of the brick mad is summarized below for AVX. SSE has only 12 columns for B and C in the first inner loop so must be repeated 12 times instead of 6. Outside all this, it is assumed that the next step will keep the C-block constant and vary the A and B blocks, varying the j parameter to deal with all the 24-entry alcoves along the slab (or part of slab under Strassen).

     C	A	B
    . . . 72	Fragment does 72
Inner fragment	3x24 += 3x1 * 1x24	FMA
    . . .	24 j	Load A, Load B
Inner loop	3x24 += 3x24 * 24x24	Count 24 iterations
    . . .	6 k	Load/Store C 3x3, reduce sometimes.
Middle loop	3x144 += 3x24 * 24x144	Count 6 iterations (12 for SSE)
    . . .	64 i	Decompress A 3x24
Outer loop	~192x144 += ~192x24 * 24x144	Count ~64 iterations
    . . .	96 j	Decompress B 24x144
first external loop ~192x144 += ~192x~2K * 2Kx144	The sub-Strassen slab
    . . .	16 k	Compress/Decompress C 192x144
second E. L.	~192x2K += ~192x2K * 2Kx2K
    . . . 10 i	Afmt conversion
third EL	2Kx2K += 2Kx2K * 2K*2K	Completing the sub-Strassen slab
    . . .	Cfmt & Bfmt conversion

	Scale	Const	Loop	work when counter expires
Aux Bux	3 1 24		-	fma, load B, load/b'cast A
Afx Bfx ctr24	3 24 24	C float	24	(reduce) store C load C
Bfx Cfx ctr6	3 24 144	A float	6	A int -> float
Afx Cfx ctr64	192 24 144	B float	64	B int -> float
Afx Bfx ctr100	192 2400 144	C float	100	C float <-> int
Bix Cix ctr20	192 2400 2880	A int	20
Aix Cix ctr10	1920 2400 2880	B int	10

Section 3 – The inner loop.

For the inner loop, all three sets of values (A B and C) are already in the form of floats, and the 3x3 matrix of vectors for C are sitting in nine registers. A and B should be in L1 cache. The loop has the job of multiplying (AVX) a 3x1 by 1x24 -> 3x24 which consists of . . .

1. Loading three registers with A0j-A2j (these can all use the same register)
2. Loading three registers with Bj0-Bj2.
3. Doing the nine fma instructions Cik += Aij*Bjk.

1. Loading the Aij.
For class 'g' and 'k' the VBROADCASTSS loads one 32-bit memory location into all eight vector positions. It is 1 mu-op P23 latency 5 reciprocal throughput 0.5 on Haswell and Broadwell, and latency 3 on Skylake.
For class 'a' we need two instructions. MOVSS is one mu-op to port 2 (the only port doing reads from memory on Nehalem) latency 2 and gets the memory location into the low 32-bits of the destination register. The SHUFPS with the same register for source and destination can then be used to duplicate that low 32 bits into all four positions, using port 5.

2. Loading the Bjk.
For class 'g' and 'k', this is a simple VMOVAPS (the unaligned version runs at the same speed) which is stated as 1 mu-op P23 latency 3 reciprocal throughput 0.5 on Haswell, Broadwell and Skylake. It depends on the AVX flag only. For class 'a', the MOVAPS is still one mu-op to port 2 (the only port that can read memory) on Nehalem but, of course, only loads 128 bits of data.

3. The fma instructions.
For class 'k', the VFMADD231PS is available. It is stated as 1 mu-op P01, latency 5, reciprocal throughput 0.5 on Haswell and Broadwell, and latency 4 (otherwise the same) on Skylake. On Piledriver/Steamroller/Ryzen it is 2 ops, latency 5-7 (depending on where the result is going) and reciprocal throughput 1.
For class 'g', two instructions are needed for each multiply-and-add, with VMULPS going to one port VADDPS going to another. Furthermore we need an additional register to hold the result of the multiply before adding it in. On the other hand, the dependency chain is much reduced, since the adds have latency of 1. There is therefore no great reason to do nine accumulations in parallel, and it may be advantageous to reorganize the loop accordingly.
For class 'a' we use the corresponding MULPS and ADDPS which, as well as only doing 128 bits, also are only two-operand so destroy one of the inputs, and in four cases we wish to retain both. Hence we also need four MOVAPS to do register-register moves, an operation which is not eliminated on Nehalem as it is on later processors.

Summary of inner loop
Class 'k'	Class 'g'	Class 'a'
Load A	3P23 L=5	3P23 L=5	3P2 3P5
Load B	3P23	3P23	3P2
FMA	9P01 L=5	9P0 9P1 L...	9P0 9P1 4P5
Total	15mu 9P01	24mu 9P0	31mu 9P0

Hence we see that the inner loop is multiply/add bound across the board. On the piledriver, all of these instructions are done in two halves, but at least they are single instructions, so the shared decode should not be a problem.

It is not clear how much the inner loop should be unrolled. The loop administration consists of updating the A and B pointers, decrementing the count and branching back. TBD we could do this in one mu-op if we had to, using indexed addressing for everything based on a counter that is incremented, terminating at zero. At the other extreme we use three mu-ops for this, whose impact can be arbitrarily reduced by unrolling.

Section 4 – The middle loop.

The middle loop is concerned with loading and storing matrix C and any sparsity we wish to use with matrix A, and the occasional reduction of matrix C modulo p.

Reduction mod p can be done by
1. Multiplying by r = 1/p.
2. Adding the constant S = 3.222.
3. Subtracting S off again!
4. Multiplying the result by p
5. Subtracting from the original number.

This can be achieved in three instructions in class 'k' since steps 1 & 2 can be combined into a single fma, as can steps 4 and 5 (by multiplying by -p since there is no fused multiply-and-subtract). This gives an indication that the largest prime available to the method (assuming reduction every 24 operations) is 1669. All numbers will be at most 834 in absolute value and 24x8342=16693344, which is 83872 short of 224. Hence it is sufficient that reduction mod p results in a number in the range -83871 to +83871. TBD prove this little result, and indeed get precise bounds for the result of this reduction, since it can probably be used in CtoD also.

There is an alternative use of the ROUNDPS instruction to replace steps 2 and 3. This is faster on older chips, partly because it is better implemented, and partly because, without the fused multiply-and-add, the above five instructions must be done separately and roundps replaces two of them (2 and 3). Hence the class 'k' version should use add/subtract, and the class 'a' and 'g' versions should use roundps.

A completely different method is to use CMPGTPS, ANDPS and SUBPS as a reduction method. It seems clear that the above methods are faster, however.

The middle loop therefore first tests to see if reduction is to be performed, and if it is, performs it.

We may estimate performance by counting the number of mu-ops to P01, which may well be the critical resource. The inner loop has 24x9P01, and the reduction has 27P01 making 243 P01. The middle and outer loops do 384 of these giving an absolute minimum of 46656 clocks, during which time it must fetch 8064 values for A and B combined. This comes to 1.45 clocks per byte if these values occupy 4 bytes, and 2.89 clocks per byte if we compress them to 2 bytes.

Section 5 – Decompression.

The raw measure of bandwidth requirements comes to the need to fetch one cache-line from real memory every 100 clocks or so. Although this will probably be OK on many machines, there is clearly a need to at least investigate how much work it would take to reduce this. The main idea is that the data for A and/or B is put into 16 bits, and decompressed as and when needed. How quickly can this be done.

One idea is to store them as 16-bit (half-precision) floats. The VCVTPH2PS can do this provided the F16C flag is set, taking 128 bits of 16-bit floats and making 256 bits of 32-bit floats out of it. Numbers -2048 to +2048 are held exactly, so this is suitable. On Skylake, Fog says it is P01 P23 from memory, but a reciprocal throughput of 1, which is hard to understand. On Ivy Bridge, Haswell and Broadwell it is P1 P23 but it is not described on Sandy Bridge. Piledriver and Ryzen both have it taking four ops.

Another idea is to use VPMOVSXWD P5 P23 to convert from signed 16-bit to signed 32-bit notation, and then to use the VCVTDQ2PS instruction to convert a 32-bit integer into a 32-bit float, taking P1 though with latency 3. This has the substantial advantage of starting with a format that can be readily converted on all chips, but it does need three mu-ops. The SSE version of the 16-32 bit integer move is SSE4.1, so is class 'd' upwards, and the convert from integer to float is SSE2 (so always available). For class 'a' the 16-32 bit extension would have to be done scalar.

For primes 197-251, of course there is the option of halving the bandwidth yet again using bytes.

Section 6 – The external loop.

Here is the table giving the number of 24-fma operations that can be done without fear of overflow. F = 2 x sqrt(224/24.N)

No of ops	F	Max Prime	Next prime	Range
1 x 24	1672.18	1669	1693 no	1187-1669
2 x 24	1182.41	1181	1187 no	967-1181
3 x 24	965.44	953	967 no	839-953
4 x 24	836.09	829	839 no	751-829
5 x 24	747.82	743	751 no	691-743
6 x 24	682.67	677	683 yes 691 no	641-683
7 x 24	632.03	631	641 no	593-631
8 x 24	591.21	587	593 no	563-587
9 x 24	557.39	557	563 no	541-557
10 x 24	528.79	523	541 no	509-523
11 x 24	504.18	503	509 no

As a worked example, consider whether one reduction every 9.24=216 is adequate for p=557. Numbers mod 557 are in the range -278 to +278, and 216.2782 = 16,693,344, which is 83,872 short of 224 = 16777216. The nearest float to 1/557 is 30843571/234, which is slightly less than 2-36 too small. If this is multiplied by a number at most 224 in absolute value, the result will be at most 2-12 too small. Hence the error should be rounded correctly and the result again in the range -278 to +278. Indeed this encourages us to wonder whether 683 might be OK with 6.24 which it is!

Section 7 – Sparsity in A.

Here is the table giving t